## Slide 1: Masters, Slaves and Clients
Slide 1
Date: 2012-09-19
Notes: Month Year
        John Doe, Some Company
Page 1

## Slide 2: Executive Summary
  “…radio equipment shall be so constructed that it effectively uses the spectrum allocated to terrestrial/space radio communications and orbital resources so as to avoid harmful interference.”
This document considers a range of issues related to master devices, slaves and client devices
  Regulations are getting more complicated with other primary services in the same band, co-channel and on adjacent channels
  Regulations are updated more frequently in anticipation of future issues and in response to difficulties experienced
  In general, devices have to earn the right to operate as client or slave, otherwise they have to be certified as master, and without reconfiguration operate legally within a regulatory domain
    The lowest common denominator master could work worldwide in 2.4 GHz bands, but there is no common denominator for 5 GHz bands
  Slaves and client devices operate under control of their master, and system operation is tested before regulatory approval is received
  A few other related matters => fix

## Slide 3: 802.11ac is changing the information that client devices use to configure transmission
12/297r0 has detailed review of issues with managing BSS emissions footprint
  https://mentor.ieee.org/802.11/dcn/12/11-12-0297-00-00ac-tpc-operating-classes-and-channel-switching.pptx
  This presentation builds on 11ac Draft 3.0 and the client control text of 12/379r6
  https://mentor.ieee.org/802.11/dcn/12/11-12-0379-06-00ac-tpc-operating-classes-and-channel-switching.docx

## Slide 4: Executive Summary
This document considers a range of issues related to master devices, slaves and client devices
  Regulations are getting more complicated with other primary services in the same band, co-channel and on adjacent channels
  Regulations are updated more frequently in anticipation of future issues and in response to difficulties experienced
  In general, devices have to earn the right to operate as client or slave, otherwise they have to be certified as master, and without reconfiguration operate legally within a regulatory domain
    The lowest common denominator master could work worldwide in 2.4 GHz bands, but there is no common denominator for 5 GHz bands
  Slaves and client devices operate under control of their master, and system operation is tested before regulatory approval is received
  A few other related matters => fix

## Slide 5: DFS and TPC are broad UNII requirements in FCC Part 15
And further regulations in subpart C
i.e.
TPC
adv-
Ised
party
=
manu
i.e.
TPC
adv-
ised
i.e.
This is the clause that lets you know that the FBI can knock on the end-user’s door. For the manufacturer, the products had better be in compliance with Part 15 . For the end-user, hopefully there is a channel and/or a TPC level that avoids harmful interference , else no operation.
The AP has the right and the responsibility to select the channels and the max TX power of the clients
Which in turn refer us to more regulations
Which in turn refer us to more regulations in subpart A
And which also refers us to other subparts
Which defines TX power, etc
Part 15 has a subpart for UNII
1
2

## Slide 6: FCC UNII-band rules evolve
47 CFR 15 Subpart E—Unlicensed National Information Infrastructure Devices – triennial review
FCC KDB 443999 removing operation in 5600-5650 MHz (2010-10)
FCC KDB 594280 restating master and client rules (2011-02)
  Section 2.931 requires the grantee to ensure that the product as sold continues to comply with the conditions of the grant.
FCC KDB 848637 UNII client devices without radar detection (2011-04)

## Slide 7: EU 5 GHz bands and rules evolved
EN 301 893 v1.5.1 (2008-12) added 40 MHz occupied bandwidths while protecting other services
  Changes to permit 802.11n operation
EN 301 893 v1.6.1 (2011-12) added wider occupied bandwidths while protecting other services
  Changes to permit 802.11ac operation
EN 301 893 v1.7.1 (2012-06) added politeness requirements in technology neutral form
  Listen Before Talk with listening proportional to transmit power, higher power requires more silence than lower power
  5.725-5.85 GHz band ERC 70-03 Short Range Device rules permit transmissions up to 25 mW

## Slide 8: Current view/existing 5 GHz spectrum: channelization for 20/40/80 MHz
20/40/80 MHz channelization (802.11 Global table)
  Consists of two adjacent IEEE 20/40 MHz channels
  Non-overlapping channelization
*FCC KDB 443999 Restricting U-NII devices from 5600-5650 MHz https://apps.fcc.gov/oetcf/kdb/index.cfm
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
5170
MHz
5330
MHz
5490
MHz
5710
MHz
5735
MHz
5835
MHz
144
Currently available channels
TDWR unavailable channels*

## Slide 9: 5 GHz radio SKUs that come from regulations continue to evolve
Some of the 5 GHz SKUs come from different OOBE filter and amplifier requirements, others come from channels to remain unused.
The following slides show a county’s 2011 GDP ranking and its 5 GHz allowed channels.

## Slide 10: 5 GHz channels allowed by EU (#1)
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
20 MHz
40 MHz
80 MHz
160 MHz
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.875 GHz
22
10
5
2
# of non-overlapping channels

## Slide 11: 5 GHz channels allowed by China (#2)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40 or 80 MHz)
Maybe by 2014 China will add lower 5 GHz bands
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.850 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
5
2
1
0

## Slide 12: 5 GHz channels allowed by India (#3), Mexico (#11) & others
Regulatory
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.875 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
13
6
3
1

## Slide 13: 5 GHz channels allowed by Japan (#4)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
19
9
4
2

## Slide 14: 5 GHz channels allowed by Russia (#6)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.875 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
16
8
4
1
144

## Slide 15: 5 GHz channels allowed by Brazil (#7) & Taiwan (#19)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40 or 80 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.850 GHz
20 MHz
40 MHz
80 MHz
160 MHz Channels Currently Not Possible For Taiwan
# of non-overlapping channels
17
7
3
0
144

## Slide 16: 5 GHz channels allowed by Korea (#12)
Regulatory SKU
802.11 Access Point Chooses One of the Above Center Frequencies using Channel Bandwidth (20, 40, 80 or 160 MHz)
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
5.15~5.35 GHz
5.47~5.725 GHz
5.725~5.825 GHz
20 MHz
40 MHz
80 MHz
160 MHz
# of non-overlapping channels
19
9
4
1

## Slide 17: Master Devices Background
  In 5 GHz radar bands, master devices must perform Initial Channel Availability Check before transmitting
    Current FCC rules require adjacent channel checks if occupied spectrum is within 30 MHz of 5600-5650 MHz TDWR band
    Current EU rules require 1 minute channel availability check
  Master devices set constrained transmit power to control emissions footprint of BSS as required by law
  "…radio equipment shall be so constructed that it effectively uses the spectrum allocated to terrestrial/space radio communications and orbital resources so as to avoid harmful interference“.

## Slide 18: More regulatory background
  Each client’s manufacturer is responsible for ensuring that the client meets the regulations for which it was homologated
    Obvious … but also incomplete
  More importantly, the default unlicensed radio frequency device regulatory approval is as a master device; to be approved as a client device the manufacturer must show that the frequencies and transmit powers the client device uses conform to regulations:
    client devices have the obligation to emit equal or less than what masters permit them to
    using exactly the same mechanisms that masters and clients were documented to use when working together when masters and clients were presented by manufacturer for homologation (see next slide)
  Especially if the local regulations could be location/time/AP-state dependent, but – by the previous bullet – actually anyhow, then the client also needs to hear the client permissions from its AP
    The client needs to get enough current-channel permissions from the Beacon that it can transmit to the AP (bootstrap) and preferably select one AP over another
    The client needs to get all current-channel permissions from the Probe/(Re)Assoc Response that it can participate fully in the BSS
    The client needs to get the next-channel permissions before/inside the channel switch

## Slide 19: More on 5 Ghz Beacon information
  In 5 GHz radar bands, master devices currently beacon so that legacy devices can join the BSS
    Have four bandwidths and two beaconing strategies today
Where “my BW and channel” could be
  “this is my *beacon* channel and bandwidth, and the constrained TX power for that BW is X” [most efficient if we get new spectrum – can send 40 or 80 MHz beacons]
  “this is my *primary* channel and bandwidth, and the constrained TX power for that BW is X” [most backwards compatible to legacy STAs]

## Slide 20: Open Discussion

## Slide 21: Backup Slides

## Slide 22: Some non-Wi-Fi product vendors have not maintained our level of care – and we want to continue avoiding their path
i.e. the exec can now be subject to jail time if the mess doesn’t get cleaned up - and promptly: actions have consequences
Re-engineering; and/or restricted orderability of products (fewer sales channels)
Expensive personnel down-time
It is generally regarded as a career-limiting maneuver to depend on a senior exec to clean up your mess
  E.g. FCC enforcement: 15 companies named, shamed and/or fined at: http://www.fcc.gov/encyclopedia/weather-radar-interference-enforcement
  For one large corporation, the Consent Decree included:
    a. Compliance Officer. LargeCorp will designate a senior corporate manager ("Compliance Officer") who is responsible for administering the Compliance Plan.
    c. Compliance Reports. LargeCorp will file compliance reports with the Commission 90 days after the Effective Date, 12 months after the Effective Date, and 24 months after the Effective Date. Each report shall include a compliance certificate from the Compliance Officer stating that the Compliance Officer has personal knowledge that LargeCorp has established operating procedures intended to ensure compliance with this Consent Decree, together with an accompanying statement explaining the basis for the Compliance Officer's compliance certification.
    b. Training. LargeCorp will train and provide materials concerning Section 302(b) of the Act and Parts 2 and 15 of the Rules pertaining to U-NII devices and the requirements of the Consent Decree to those of its employees who are involved directly in the development and marketing of U-NII devices imported, marketed and sold by LargeCorp in the United States.
Notes: Interference happens, regulators come calling. If shortly thereafter the interference is still happening, then oftentimes a consent decree is negotiated between lawyers. The *manufacturer* is the responsible party in part 15, and any operator can cause trouble for the manufacturer.

## Slide 23: WISPA Links
Are you near TDWR?
  http://wispa.cms.memberfuse.com/tdwr-locations-and-frequencies
  // starting to list two frequencies per TDWR
If so, register here
  http://www.spectrumbridge.com/udia/home.aspx
  “This tool allows a user (network operator or installer) to:
  • Search and confirm if their device is operating within 35 km proximity of TDWR site(s)
  • Voluntarily register certain technical information into the online database”