## Slide 1: Proposals for the FD Frame Capability, Security and Neighbour AP Information Content Design
Date: 2012-11-03
Authors:

## Slide 2: Abstract
This contribution is intended to continue the discussion about a detailed design of the FILS Discovery (FD) Frame content items, including FD Capability, FD Security, and FD Neighbor AP information.
This contribution provides supporting materials for the 802.11ai draft specification document text proposal for a detailed design of the FD frame contents in Contribution, 12/1236.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
Progress has been made regarding the FILS Discovery Frame content design in the TGai September meetings, e.g., reached a general consensus for a detailed design for:
  SSID, Access Network Options, AP’s Next TBTT, AP Configuration Change Count;
However, 3 content items are still remaining to be designed in details:
  Capability, Security, and Neighbor AP’s Next TBTT information
This contribution continues the discussions of detailed designs for those three content items.

## Slide 5: Capability Info Item in FILS Discovery Frame -- Recap from Contribution 12/1030
Discussion points from2012-July meeting (12/0913r3)
  It is one of the optional info items in FD frame;
  Its purpose is to provide info for AP/Network initial de-selection;
  Additional discussion about the Support data rates
    Attempt to eliminate the supported rates element, by using the reserved bits in capability info field to indicate the identified minimum rates.
Reference materials identified in 2012-July meeting (12/0913r3)
  Beacon/Probe Response in 802.11-2012 spec
    Capability info field: p438, section 8.4.1.4
    Supported Rates element, p478, 8.4.2.3
    Extended Capabilities element, p562, section 8.4.2.29
    Neighbor Report element, 8.4.2.39
  Measurement Pilot frame
  11ah short beacon (11/1503r2, 12/0129r3)
Further Design Considerations
  What capability indicators are needed in FD frame?
  Detailed encodings of the capability indicators?

## Slide 6: Capability Info Item in FILS Discovery Frame – con’t Recap from Contribution 12/1030
Proposal:
  Design a fixed-size new capability field in FD frame, e.g., 3 bytes;
  Use the 2-byte Capability field as defined in Figure 8-38 in 802.11-2012 as starting point; and remove the unnecessary subfields for FD frame uses, e.g.,
    DSSS-OFDM
    PBCC
    Channel Agility
    APSD
  Add some new info items, e.g.,
    Supported minimum rate
    PHY type
    IPv4 / IPv6 support
  Use a 1-bit indicator in the FD frame control field to indicate the presence of the Capability info item in the FD frame.

## Slide 7: Capability Info Item in FILS Discovery Frame – con’t Recap from Contribution 12/1030

## Slide 8: Security Info Item in FILS Discovery Frame -- Recap from Contribution 12/1030
Discussion points from 2012-July meeting (12/0913r3)
  It is one of the optional info items in FD frame;
  Its purpose is to provide info for AP/Network initial de-selection;
Reference materials
  RSNE in Section 8.4.2.27 in 802.11-2012 spec
Further Design Considerations
  What Security indicators are needed in FD frame?
  Detailed encodings of the Security indicators?

## Slide 9: Security Info Item in FILS Discovery Frame (con’t) -- Recap from Contribution 12/1030
Proposal:
  Design a fixed-size new Security field in FD frame, e.g., 4 bytes;
  Use the RSNE as defined in Section 8.4.2.27 in 802.11-2012 as starting point; and consider changes to make it smaller in size, e.g.,
    Re-design the RSN Capabilities subfield to reflect its practical uses and 11ai specific considerations;
    Limit the numbers of Pairwise suites and AKM suites, e.g., 2 for each
    Introduce 4-bit codes to identify Cipher Suites and AKM Suites
    Remove PMKID count and PMLID list
  Add some new info items, e.g.,
    Security capability indicators for FILS authentication methods support, e.g.,
      FILS Fast-EAP based authentication
      FILS EAP-RP based authentication
      FILS Non-EAP Fast authentication
      FILS Fast Authentication without 3rd-party
  Use a 1-bit indicator in the FD frame control field to indicate the presence of the Security info item in the FD frame.

## Slide 10: Security Info Item in FILS Discovery Frame (con’t) -- Recap from Contribution 12/1030

## Slide 11: Neighbor AP’s TBTT Info Item in FILS Discovery Frame
Discussion points from 2012-July meeting (12/0913r3)
  It is one of the optional info items in FD frame;
  Its purpose is to enable optimizations for multiple APs/Channels scanning.
Reference materials in 802.11-2012
  Neighbor report element, Section 8.4.2.39;
  Beacon timing IE, Section 8.4.2.107, for neighbor's next beacon Tx time;
  AP channel report IE, Section 8.4.2.38
Additional reference material:
  Reduced Neighbor AP Report: 12/1054r2 and 12/1098r5
Design Considerations
  cannot use a value from the transmitting AP’s timestamp or the neighbor AP’s timestamp to indicate the neighbor AP’s next TBTT, due to the un-synchronized status of the STA and the APs;
  Use Operating Class / Operating Channel to identify where to find neighbor APs;
  Allow multiple APs/TBTTs on the same channel

## Slide 12: Neighbor AP’s TBTT Info Item in FILS Discovery Frame – con’t
Proposal:
  Use a 2-byte info field to identify the Channel for neighbour AP(s):
    Operating Class subfield: 1 byte, an enumerated value defined in Annex E in 802.11-2012 specifying the operating class of the neighbour AP;
    Channel Number subfield: 1 byte, an enumerated value defined in Annex E in 802.11-2012 specifying the operating class within the Operating Class of the neighbor AP;
  Use an 1-byte Next TBTT subfield: an offset value, in unit of TU, specifying the time between the FD frame Tx time and a Neighbour AP’s next TBTT.
  Use a more compressed encoding (comparing to the Reduced Neighbor AP Report IE) to:
    Allow multiple neighbor AP’s TBTT info fields for the same channel;
    Allow multiple channels to be included;
  Use an 1-bit indicator in the FD frame control field to indicate the presence of Neighbor APs’ TBTT info in the FD frame.

## Slide 13: Neighbor AP’s TBTT Info Item in FILS Discovery Frame – con’t

## Slide 14: Neighbor AP’s TBTT Info Item in FD Frame – con’t

## Slide 15: Discussion on FD Frame Body Extensibility
The proposed FD frame body design is extendible, when needed;
Two basic mechanisms:
  Use the available bits in the FD frame control field;
  Use optional information elements.

## Slide 16: Straw-Polls
Straw-Poll-1:
Do you support the proposal of the FILS Discovery (FD) capability info item encoding as described in Slide 7 of this contribution?
Result Yes No Abstain_______________

## Slide 17: Straw-Polls
Straw-Poll-2:
Do you support the proposal of the FILS Discovery (FD) Security info item encoding as described in Slide 10 of this contribution?
Result Yes No Abstain_______________

## Slide 18: Straw-Polls
Straw-Poll-3:
Do you support the proposal of the FILS Discovery (FD) Neighbor APs’ Next TBTT info item encoding as described in Slide 13 of this contribution?
Result Yes No Abstain_______________

## Slide 19
References:
IEEE Std 802.11™-2012
11-12-0151-13-00ai-proposed-specification-framework-for-tgai
11-12-0913-03-00ai-paasive-scanning-discussions
11-12-0741-01-00ai-discussions-about-fils-discovery-frame-content-design
11-12-0406-05-00ai-passive-scanning-improvements-draft
11-12-0669-01-00ai-passive-scanning-improvements-ad-hoc-report
11-12-0742-00-00ai-FILS-Discovery-Frame-Format-Discussions
11-11-1137-09-00ah-specification-framework-for-tgah
11-11-1503-02-00ah-short-beacon
11-12-0129-03-00ah-short-beacon
11-11-1031-00-00ai-air-time-consumption-by-beacon-and-probe
11-12-0053-01-00ai-gas-version-control-including-normative-text
11-12-0158-03-00ai-proposed-additions-to-sfd
11-12-1029-00-00ai-FILS-Discovery-Frame-Format-Discussions
11-12-1054-02-00ai-fils-reduced-neighbor-report
11-12-1236-00-00ai-spec-text-for-FD-Frame-Definition