## Slide 1: Discussion of Outstanding TGai Security Topics
Date: 2012-10-30
Authors:
Name | Company | Address | Phone | email
René Struik | Struik Security Consultancy | Toronto ON, Canada | USA: +1 (415) 690-7363 Toronto: +1 (647) 867-5658 Skype: rstruik | rstruik.ext@gmail.com

## Slide 2
Background
The following contributions provide background:
Presentations
11-12-0794-03-00ai-authentication-with-local-authentication-and-optional-remote-authorization
Specification text:
11-12-1172-00-00ai-suggested-edits-to-12-1164-02-00ai-tgai-spec-text-proposal-for-fils-authentication
11-12-1151-03-00ai-suggested-edits-to-12-1045-02-00ai-tgai-spec-text-proposal-for-fils-authentication-
protocol-draft
11-12-1045-04-00ai-tgai-spec-text-proposal-for-fils-authentication-protocol
Updates provided now:
Elaboration on questions resulting from Palm Springs meeting
Details of cryptographic protocol ingredients (shown in context) – most already originally in 12/794r3
Main message:
Opportunity for full conversion on protocol details, so as to arrive at solid, well-understood, yet nimble and flexible protocol and that is even already standardized elsewhere

## Slide 3
Outline
Protocol recap
Computational cost public-key crypto
Certificate structure
“piggy-backed data” along key confirmation flows
Note:
Our exposition is relative to certificate-based public-key protocol (i.e., without online
third party), but does leave out details not necessary for current discussion

## Slide 4
Protocol Recap
Security properties:
Key establishment, mutual entity authentication, implicit key authentication, mutual key confirmation, etc.
A
Random X, CertCA(IdA,QA)
MACk1(IdA || IdB || X || Y )
Key Establishment
Key Confirmation
B
Random Y, CertCA(IdA, QB)
MACk1(IdA || IdB || X || Y )
STA
AP

## Slide 5
Computational Cost Public-Key Crypto
Implementation cost ECC on constrained platforms:
ATMega 128, 7.3828 MHz platform [1]: Koblitz curve K-163: 0.32s; K-233 curve: 0.73s (in assembly)
Hardware-assisted implementation: much faster
Anecdotal evidence: required with constrained smartgrid applications (e.g., US, Germany, France, etc.)
Ref: [1] Diego F. Aranha, Julio López, Leonardo B. Oliveira and Ricardo Dahab. Efficient implementation of elliptic curves on sensor nodes. Conference on Hyperelliptic curves, discrete Logarithms, Encryption, etc., Frutillar, Chile, 2009
Options, as specified with 12/1172r0:
Prime curve: P-256
  FIPS Pub 186-3, NIST SP 800-56a, ANSI X9.63-2001
Binary curve: K-283
  FIPS Pub 18-3, NIST SP 800-56a, ANSI X9.63-2001
Motivation:
Prime curves:
more vulnerable to crypto implementation attacks (side channel/fault attacks) and denial of service attack;
most suitable when implemented on platform with efficient integer arithmetic;
Binary curves:
less vulnerable to crypto implementation attacks (side channel/fault attacks) and denial of service attacks;
most suitable for resource-constrained, sensor-style platforms (e.g., 802.11af, low energy mode)
Legacy constructs: RSA, ordinary DLP not specified, since not meeting FILS requirements

## Slide 6
Key Info Field - Certificates (1)
Function of KeyInfo field
Distribution of authentic long-term public keys QA and QB
Options
Device Certificates: KeyInfoA = “CertCA(IdA, QA)” Example: X509v3-style, etc.
  Logical separation of identifier space and public keys (same IdA can get new public key QA)
  Device configuration does not bind elements of identifier space and public keys
  Assignment of identifier could precede crypto operations (e.g., transceiver chip with Id,
  with higher-layer crypto and binding added later on when building system)
  Independent verification of authenticity binding possible, trivial key extraction
  Authorization based on management of device identities
  Requires CA who binds elements of identifier space and public keys
Manual “Certificates”: KeyInfoA = “(IdA, QA)” Example: hashed public keys, etc.
  Logical binding of identifier space and public keys (new public key QA results in loss of IdA)
  Device configuration binds elements of identifier space and public keys
  Assignment of identifiers cannot precede crypto operations (e.g., transceiver chip can only obtain Id
  once higher-layer crypto added later on when building system)
  Independent verification of binding possible, trivial key extraction
  Authorization based on management of public-key related identities
  Does not require CA for authentic binding, but no evidence on “sanity checks” key generation
Both require authentic authorization operations (device provisioning, personalization, etc.)

## Slide 7
Key Info Field – Certificates (2)
Function in context of key authentication
Verification that only party that may be capable of computing the key is indeed its perceived communicating party
Options, as specified with 12/1172r0:
KeyInfo verification
Device Certificates: KeyInfoA = “CertCA(IdA, QA)”
  X509v3-style ECDSA certificate, with SHA-256 hash function
  Cryptographic scheme standardized with FIPS Pub 180-2, FIPS Pub 186-3, ANSI X9.63-2001
  Certificate scheme standardized with RFC 3280, RFC 5480
Manual “Certificates”: KeyInfoA = “(IdA, QA)”
  Same as device certificate, but now without signature field
  Scheme standardized with IETF: approved draft farrell-decade-ni-10 (“Naming things with hashes”)
Note: KeyInfoA can be locally stored as hashed version (e.g., using SHA-256 hash function)
Question: Does specifying ordinary certificates and manual certs (“hashed keys”) suffice?
(I did not hear any further feedback from Palm Springs participants after September 2012 meeting)

## Slide 8
“Piggy-Backed Info” (1)
Basic Protocol:
Security properties:
Key establishment, mutual entity authentication, implicit key authentication, mutual key confirmation, etc.
A
Random X, CertCA(IdA,QA)
MACk1(IdA || IdB || X || Y )
Key Establishment
Key Confirmation
B
Random Y, CertCA(IdA, QB)
MACk1(IdA || IdB || X || Y )
STA
AP

## Slide 9
“Piggy-Backed Info” (2)
Extended Protocol #1:
(with “piggy-backing”)
Security properties:
Key establishment, mutual entity authentication, implicit key authentication, mutual key confirmation, etc.
Additional functionality:
Authentication of exchanged “piggy-backed info” TextA and TextB (if any), via authentication tags key confirmation messages
A
Random X, CertCA(IdA,QA)
MACk1(IdA || IdB || X || Y || [TextA]), TextA
Key Establishment
Key Confirmation
B
Random Y, CertCA(IdA, QB)
MACk1(IdA || IdB || X || Y || [TextB]), TextB
STA
AP
Piggy-backed info may originate remotely

## Slide 10
“Piggy-Backed Info” (3)
Extended Protocol #2:
(with “piggy-backing”)
Security properties:
Key establishment, mutual entity authentication, implicit key authentication, mutual key confirmation, etc.
Additional functionality:
Authentication of exchanged “piggy-backed info” TextA and TextB (if any), via authentication tags already in key confirmation messages (if field present)
Confidentiality and authenticity of exchanged “piggy-backed info” TextA and TextB (if any), via special enciphering function not present on basic protocol
A
Random X, CertCA(IdA,QA)
MACk1(IdA || IdB || X || Y || [TextA]), [TextA]k2
Key Establishment
Key Confirmation
B
Random Y, CertCA(IdA, QB)
MACk1(IdA || IdB || X || Y || [TextB]), [TextB]k2
STA
AP
Piggy-backed info may originate remotely

## Slide 11
“Piggy-Backed Info” (4)
Options for securing “piggy-backed data”:
Data authenticity only: Simply use authentication tag key confirmation
Data authenticity via key confirmation tag, confidentiality separately: use, e.g., CTR mode construct1
Both authenticity and confidentiality separately: use any combined authentication and encryption mode (AEAD mode), e.g., CCM, GCM, OCB
Notes:
With options #2, #3, so-called “nonce misuse resistance” is a non-issue, since
  Enciphering function uses “fresh” key across different invocations along key confirmation message flows
  Nonce space of both protocol parties easy to separate
  Easy to use two “fresh” keys if really desired (use one key in each direction)
Simplest option is to reuse (elements of) existing constructs, so as to save implementation cost (Option #2: CTR mode; option #3: CCM mode)
Alignment of nonce structure with reused construct beneficial (depending on prevalent hardware [RS: please drop me a note!])
Fully compliant with standards (NIST, ANSI, etc.)
1See, e.g., 12/1151r3, §11.9a.2.4b, 11.9a.2.5b

## Slide 12
Other Considerations
Use standards whenever possible:
  Reuses existing implementations and makes compliance process easier
  Fosters interoperability, confidence in sufficient scrutiny
  E.g., use standard representations ECC point, reference NIST SP 800-56a schemes
Keep protocol engine separate from usual frame processing state machine
  Allows reuse of existing crypto state machines, without 802.11-specific “tweaks” of general components
  Allows reuse of key agreement engine for other applications besides 802.11ai (e.g., NFC protocol on WiFi-enabled device)
  Avoids convoluted security arguments (easier to study properties of protocol)
  E.g., no enciphering of entire Association Request/Response frame, but only payload fields (where key agreement flows reside)

## Slide 13
List of Questions after Palm Springs meeting
(no doubt, partial – additions welcome)

## Slide 14
Questions Resulting from Palm Springs Meeting (1)
TGai mailing list: (David Goodall, e-mail as of September 21, 2012, 7.35pm EDT)
1. What functionality or advantages do we lose when we lose the EAPOL key frames?
A specific example is that the multi-band operations introduced in 11ad require use of fields which were added to EAPOL key frames 1-4. If we don’t have the EAPOL key frames in the 11ai mechanism, and we want the multi-band operation, then we need to do some extra specification work. This should be do-able but there may be an ongoing requirement to maintain this part of the multi-band functionality in more than one place in the 802.11 specification.
I need to review further to see if there any other similar issues.
2. Will 11ai fast initial link setup be fast for low power, CPU-challenged 802.11 devices?
An example is a mobile battery powered 802.11 RFID sensor tag with perhaps a 50 MHz 32 bit CPU. I gather that the current non-TTP proposal will take perhaps 10 ms on a smart phone with a 1 GHz processor so it does not appear suitable for low power devices. Rene Struik has indicated that this issue can be addressed with a different selection of elliptic curve and various processing techniques.

## Slide 15
Questions Resulting from Palm Springs Meeting (2)
Main outstanding topics resulting from Palm Springs sessions on TGai security:
Certificate structure
Mechanism for authentication and (possibly) encryption of “piggy-backed data” along key confirmation
Other topics:
Reuse of existing crypto and security functionality
Compliance to external specifications (e.g., key wrap?)