## Slide 1: Omission of Probe Request
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
HanGyu Cho | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | HanGyu.Cho@lge.com
Date: 2012-11-05
Authors:

## Slide 2: Abstract
Current Probe Request omission procedure which was described in P802.11ai D01 was incomplete and needs to add the further explanation.
Thus, we clarify the Probe Request omission operation which was described in P802.11ai D01.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1, 2

## Slide 4: Motivation (1/3)
Omission of Probe Request
  The 802.11ai D01 is describing that a STA may not transmit a Probe Request frame to a channel at which the STA has received:
    A broadcast addressed Probe Request frame to which the clause 10.1.4.3.5(Criteria to respond to probe request) allows at least the same responses as the information indicated in the received MLME-SCAN.request primitive.
However, draft does not describe how the STA operates after omitting Probe Request transmission.

## Slide 5: Motivation (2/3)
STA not receiving the Probe Response frame after omitting the Probe Request transmission
  After omitting the transmission of Probe Request frame, STA can not receive Probe Response frame successfully in the following cases.
    Collision
      Probe Response frame is collided with other frame.
    Hidden node problem
      STA is hidden from the APs transmitting Probe Response even though it has received a broadcast Probe Request from other STA.
    Unicast Probe Response
      AP transmits the Unicast Probe Response frame as a response to the broadcast addressed Probe Request frame.
If the STA switches to other the channel, STA may not discover the APs even though there are desired APs in the vicinity.

## Slide 6: Motivation (3/3)
The draft specification should clarify how the STA operates in case of not receiving a Probe Response frame after omitting the Probe Request transmission.

## Slide 7: Proposal
If a STA receives a broadcast addressed Probe Request frame to which the clause 10.1.4.3.5(Criteria to respond to probe request) allows at least the same responses as the information indicated in the received MLME-SCAN.request primitive, the STA may not transmit a Probe Request frame to a channel. (Already in the draft D01)
The STA sets a ProbeTimer to 0 and start the ProbeTimer.
If PHY-CCA.indication (busy) primitive has not been detected before the ProbeTimer reaches MinChannelTime, then send its own Probe Request frame, else process the received probe responses or Beacon.
If neither Probe Response nor Beacon has been received until ProbeTimer reaches MaxChannelTime, the STA send its own Probe Request frame.

## Slide 8: Motion
    Move to add the normative text of 11-12-1269- Tgai-Spec-Text-Proposal-for-Omission-of-Probe-Request to the P802.11ai D01.
    Mover:
    Seconder:
    Result
    Yes No Abstain_______________