## Slide 1: BSS/Network Status Information for a Fast AP/Network Selection
Date: 2012-11-04
Authors:

## Slide 2: Abstract
This document provides further details for a feature described in Subsection 6.3.4 in the 802.11ai SFD (Specification Framework Document), 12/0151r13, for a fast AP/Network selection.
This contribution also provides supporting materials to the detailed text proposal for the TGai draft Specification document, as proposed in Contribution 12/1271.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
A high-level feature description in Subsection 6.3.4 in TGai SFD:
  AP may include an indicator for AP availability to attachment to the Beacon and Probe Response.
  Multiple previous TGai contributions:
  KDDI: 11/1565r0, AP Status Broadcast
    include IEs, e.g., BSS load or other IEs related with AP status and performance in Beacon.
    Include WAN Status info in Beacon.
  China Mobile contribution: 12/0545r1, Access Control Mechanism for FILS
    In 11ai management frames, e.g: beacon, probe response , GAS, carry the network load information for STA’s AP/Network selection:
    the congestion information of the AP; The available bandwidth information etc.
  HTC contribution: 12/1051r2, Multi-channel information for AP discovery
    AP can attach the loading information of BSSs on other channels in the probe response and beacon, e.g., A condensed and aggregated loading information; Use a coarser unit to represent info such as BSS load, BSS Avg access delay, BSS Available Admission Capacity
Further details are needed for TGai Specification Document.

## Slide 5: Discussion on AP Availability Information
The purpose of providing AP availability information in Beacon/Probe Response:
  For a fast AP/Network selection, by avoiding selecting a congested or near-congested AP/Network and also by avoiding the query overhead.
  Note that AP Availability info in Beacon / Probe Response is not about the physical link availability, as it assumes that the STA already can receive Beacon / probe response.
AP availability information can be presented by:
  BSS/AP status/load indicators;
  Access Network link, or called Backhaul Link, status/load indicators.
BSS/AP Status/load Indicators
  Already have multiple in the current 802.11 Spec (802.11-2012); see next two slides for further discussions;
  Too many / Too much overhead  need to pick!
Backhaul Link Status/Load indicators
  Does not exist in the current 802.11 spec;
  Need to be defined.

## Slide 6
802.11-2012 BSS Status/Load Indicators
  5 relevant IEs in 802.11-2012 spec:
    BSS load IE: 2+5 bytes, containing the info of
      STA count: the total number of STAs currently associated with this BSS;
      Channel utilization: the percentage of time, linearly scaled with 255 representing 100%, that the AP sensed the medium was busy;
      Admission Capability: the remaining amount of medium time available via explicit admission control, in units of 32 μs/s.
    BSS Available Admission Capacity IE: 2+2+2*n bytes, containing the info of Admission Capabilities for each UP/AC (User Priority / Access Category);
    QoS Traffic Capability IE: 2+1+m bytes, containing the info of STA counts for each UP/AC ;
    BSS Average Access Delay IE: 2+1 bytes, containing the info of a scalar indication of average medium access delay;
    BSS AC Access Delay IE: 2+4 bytes; containing the info of Access Delay for each UP/AC.

## Slide 7
Discussions on BSS Status/Load Indicators
    Do we need all those 5 BSS Status/Load IEs in Beacon / Probe response for a fast AP/Network selection?
      No. Too much overhead, also redundant.
      A simple indicator or indicators for the STA to avoid selecting a congested or near-congested BSS.
      How about just BSS Load IE?
    Do we need the per-UP/AC BSS Status/Load indicators?
      Not really, for overhead reduction!
      At initial link setup, the STA can use a simple indicator of LAN link loading and other parameters, e.g., PHY rates, to estimate if it should avoid the BSS/AP due to the potential LAN link congestion.

## Slide 8
Backhaul Link Status Indicator Considerations
  Backhaul Link: the communication link that connects the BSS/AP with external networks.
Backhaul Link Status descriptors / measures:
  Backhaul Link availability: available, not-available;
  Downlink / Uplink Rate: the data rate of the Backhaul link;
  Downlink / Uplink Load: the traffic load on the Backhaul link.
Downlink (DL):
  Backhaul Link direction from external network to the BSS/AP;
Uplink (UL):
  Backhaul Link direction from the BSS/AP to external network.

## Slide 9
Proposals
Mandate BSS Load IE, as defined in Subsection 8.4.2.30 in 802.11-2012 spec, in Beacon and Probe Response frames, for 11ai-capable BSS/AP;
Define a Backhaul Link Status Information Element (IE)
  Can be included in Beacon and/or Probe Response frames;
  Can also be included as a sub-element in Neighbor report.

## Slide 10
Backhaul Link Status IE
Element ID | Length | Backhaul Link Info | DL Rate | UL Rate | DL/UL Load
Octets:
Link Status | Reserved
Bits:
Meaning | Value
Link Down | 0b00
Link up | 0b01
Link under test | 0b10
Link Full | 0b11
DL / UL Rate: in unit of 100 kilobits per second
DL / UL Load:
  0b0000 to 0b1010: load in percentage, at a step of 10%;
  0b1011 to 0b1110: reserved
  0b1111: load info not available.
DL Load (4 bits) | UL Load (4 bits)
Bits:
1 | 1 | 1 | 2 | 2 | 1
B0 - B1 | B2 - B7
B0 – B3 | B4 - B7

## Slide 11: Straw Polls
Straw-Poll-1: Do you support that 11ai-capable BSS/AP shall include the BSS Load IE, as defined in Subsection 8.4.2.30 in 802.11-2012 spec, in the Beacon / Probe Response frame?
Result Yes No Abstain_______________

## Slide 12: Straw Polls
Straw-Poll-2: Do you support introducing the Backhaul Link Status Element as proposed on Slide 10 in this contribution, to the Beacon / Probe Response for the 11ai-capable AP?
Result Yes No Abstain_______________

## Slide 13
References:
IEEE Std 802.11™-2012
11-12-0151-13-00ai-proposed-specification-framework-for-tgai
11-11-1565-00-00ai-ap-status-broadcast
11-12-0545-01-00ai-access-control-mechanism-for-fils
11-12-1051-02-00ai-multi-channel-information-for-ap-discovery