## Slide 1: PAPR Reduction for MCS0 Rep 2
Date: 2012-11-12
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Jun Zheng | Broadcom |  |  | 
Eldad Perahia | Intel Corp. |  |  | eldad.perahia@intel.com
Shahrnaz Azizi | Intel Corp. |  |  | shahrnaz.azizi@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Thomas Kenney | Intel Corp. |  |  | thomas.j.kenney@intel.com
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Yong Liu | Marvell |  |  | yongliu@marvell.com
Yongho Seok | LG Electronics | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Hangyu Cho | LG Electronics |  |  | 
Vinko Erceg | Broadcom |  |  | verceg@broadcom.com
Nihar Jindal | Broadcom |  |  | 

## Slide 2
Authors continued:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm |  |  | 
Eugene Baik | Qualcomm |  |  | 
Lin Yang | Qualcomm |  |  | 
Tao Tian | Qualcomm |  |  | 
Bin Tian | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
Richard Van Nee | Qualcomm |  |  | 
Allert Van Zelst | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Hyoungjin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Sayantan Choudhury | Nokia | 2054 University Avenue, Suite 600, Berkeley, CA 94704 | +1 510 599 9268 | sayantan.choudhury@nokia.com
Klaus Doppler | Nokia |  |  | 
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | mori.ken1@jp.panasonic.com
Harya Wicaksana | Panasonic |  |  | Harya.Wicaksana@sg.panasonic.com

## Slide 3
Authors continued:

## Slide 4: Problem Definition and Proposed Solution
Repetition is well known to increase PAPR in OFDM systems.
MCS0 rep2 (MCS10) was adopted as the lowest MCS for 1MHz and, as shown in the next slide, has higher PAPR than MCS0. Higher PAPR is especially problematic for the lowest MCS due to the limiting effect on PA backoff which reduces range.
Typical solutions try reduce the PAPR by randomizing the repeated sequence
We investigate here a simple scheme to reduce PAPR for MCS0 rep2 as follows:
  We start with the 12 coded bits for MCS0 rep2: b=[b0,b1,b2,…,b11]
  Using a 12 bit long sequence s we create the 2nd copy bb=b XOR s
  Concatenate [b,bb] to create a sequence of 24 coded bits, interleave and add pilots
The best sequence is found by sweeping through all 4096 combinations and minimizing a metric defined as the 2e-4 percentile point of the PAR CCDF.
The best sequence found is: s=[1 0 0 0 0 1 0 1 0 1 1 1] (meaning flip the sign of the 1st, 6th,8th, 10th,11th 12th repetitions) .

## Slide 5: Simulation results
CCDF based on 4x oversampling and 500,000 OFDM symbols.
Results shown for fixed pilots and boosted traveling pilots

## Slide 6: Straw Poll
Do you support the following change in section R.3.2.2.2.A
  The “2x block-wise repetition” performed on a per-OFDM symbol basis:
    Cout=[C1….C2NDBPS , C1….C2NDBPS ], where [C1….C2NDBPS] are the FEC output bits per symbol.
  The “2x block-wise repetition” performed on a per-OFDM symbol basis:
    Cout=[[C1….C2NDBPS ], [C1….C2NDBPS ] XOR s], where [C1….C2NDBPS] are the FEC output bits per symbol and s=[1 0 0 0 0 1 0 1 0 1 1 1]
Y
N
A