## Slide 1: RAW Slot Assignment
Date: 2012-11-12
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Introduction
General procedures of uplink and downlink channel access (4.2.1, 4.2.2, 4.2.3) were adopted in the TGah SFD [1].
R.4.2.2.A describes the concept of using the TIM IE to determine the slot boundary of a STA to start channel access
  “Paged STA starts the contention at slot boundary defined as a function of STA position in the TIM IE and additional info determined by Association or Beacon frame.”
This presentation proposes a simple slot assignment scheme using TIM IE and RAW PS IE

## Slide 5: RAW Parameter Set Element
4.4.3.1.2 in the TGah SFD defines the fields in the RAW PS IE:
Feature | Value | Interpretation
Page ID | TBD bits | Indicates the page index for hierarchical AID (based on hierarchical AID) of the allocated group
Block Offset | TBD bits | Assuming 32 blocks per page, these bits indicate the starting block index of the allocated group
Block Range | TBD bits | Indicates the number of blocks (starting from the block offset) for the allocated group
RAW Start Time | 8 bits | Duration in TU from end of beacon transmission to RAW Start time
RAW Duration | TBD bits | Duration of RAW in TU
Access restricted to paged STA only | 2 bits | Bit 1: Set to 1 if only STA with their TIM bit set to 1 are allowed to perform UL transmissions Bit 2: Set to 1 if RAW is reserved for frames with duration smaller than slot duration, such as PS-Polls / trigger frames (ignored if Bit 1 is not set)
Group/Resource allocation frame indication | 1 bit | Set to 1 to indicate if STAs need to wake up at the beginning of the RAW to receive group addressed frames such as resource allocation (format of the resource allocation frame TBD)
Slot definition | TBD bits | Include Slot duration signaling Slot assignment to STA Cross boundary transmissions allowed/not allowed Format is TBD

## Slide 6: Slot Assignment using TIM IE
Example
Restricted Access Window (RAW) duration = TRAW
Slot
Boundary
Slot
Boundary
Slot
Boundary
Slot
Boundary
Slot
Boundary
Slot
Boundary
Slot duration (Ts ) = TRAW / NRAW
Beacon
TIM IE
RAW Parameter Set IE
…
RAW Start Time
(TRAW START)
Number of slots
in the RAW = NRAW
1
0
1
0
0
1
0
0
1
0
TIM bitmap
AID:
1
0
0
1
0
N
M
N+1
x
STA with AID = x mapped to i -th slot
Slot i

## Slide 7: Proposal
Define a field in the slot definition field that indicates the slot duration (TS)
Derive NRAW by dividing the RAW duration (TRAW) with the slot duration (TS)
  i.e. NRAW = TRAW/TS
Define a STA-Slot mapping function :
  = i (the slot index assigned to a STA)
  If the RAW is for both paged and unpaged STAs
    x is the AID of a STA
  If the RAW is restricted to paged STAs only
    x is the position index of a paged STA among all the paged STAs when sequentially arranged based on their AIDs
      For example, if there are n paged STAs in front of the paged STA, x=n (assuming that the first paged STA’s bit position is defined to be x=0).
  is an offset value in the mapping function that is provided to address fairness among the STAs indicated in the TIM
    Use an existing field of the received Beacon frame for (e.g. Timestamp or FCS)
  indicates the modulo operation

## Slide 8: Example 1a
Both paged and unpaged STAs are allowed to access RAW
Number of AIDs =
Restricted Access Window (RAW) duration = TRAW
Slot duration (Ts ) = TRAW / NRAW
Beacon
TIM IE
RAW Parameter Set IE
…
RAW Start Time
(TRAW START)
Number of slots
in the RAW = NRAW=15
1
0
1
0
0
1
0
0
1
0
TIM bitmap
x=AID:
1
0
0
1
0
1
2
Slot 0
3
4
5
6
7
8
9
10
11
12
13
14
15
Slot 1
Slot 2
Slot 3
Slot 14
Slot index= f(7) = (7+3) mod 15 = 10
Slot 10
…
Slot index= f(14) = (14+3) mod 15 = 2

## Slide 9: Example 1b
Both paged and unpaged STAs are allowed to access RAW
Number of AIDs >
Restricted Access Window (RAW) duration = TRAW
Slot duration (Ts ) = TRAW / NRAW
Beacon
TIM IE
RAW Parameter Set IE
…
RAW Start Time
(TRAW START)
Number of slots
in the RAW = NRAW=8
1
0
1
0
0
1
0
0
1
0
TIM bitmap
AID:
1
0
0
1
0
1
2
Slot 0
3
4
5
6
7
8
9
10
11
12
13
14
15
Slot 1
Slot 2
Slot 3
Slot index= f(7)
= (7+3) mod 8 = 2
Slot 7
Slot index= f(15)
= (15+3) mod 8 = 2
Two STAs (AID=7 and AID=15) mapped to one slot (slot index =2) in the RAW

## Slide 10: Example 2
Restricted to paged STAs only (i.e. AID bit = 1 in TIM IE) to access RAW
Restricted Access Window (RAW) duration = TRAW
Slot duration (Ts ) = TRAW / NRAW
Beacon
TIM IE
RAW Parameter Set IE
RAW Start Time
(TRAW START)
Number of slots
in the RAW = NRAW=6
1
0
1
0
0
1
0
0
1
0
TIM bitmap
AID:
1
0
0
1
0
1
2
Slot 0
3
4
5
6
7
8
9
10
11
12
13
14
15
Slot 1
Slot 2
Slot 3
Slot index= f(2) = (2+3) mod 6 = 5
Slot 5
Slot index= f(5) = (5+3) mod 6= 2
0
1
2
3
4
5
x=Position index of a STA among
all the paged STAs
Slot 4

## Slide 11: Straw Poll
Do you support the slot assignment scheme as outlined in slide 7?
  Y/N/A

## Slide 12: Motion
Move to accept in the SFD the slot assignment scheme outlined in slide 7.
  Y/N/A

## Slide 13: Reference
[1] TGah Specification Framework, IEEE 802.11-11/1137r11