## Slide 1: Relays for 802.11ah
Date: 2012-11-12
Authors:

## Slide 4: Introduction
Need for Relays in 11ah
  Extend the range for AP -STA link
    DL: Increased range with 900MHz carrier may not be sufficient in applications with remote sensors or scenarios with obstructions in AP to STA path
    UL: STA may have substantially lower TX power than AP so the STA may not be able to reach the AP
      Relays can be used to close the STA to AP link
  Lower the power consumption at STAs
    STAs can have shorter transmissions by using higher MCSs when sending to a Relay. Reduces Tx power consumption at the STA.
Design for Relay based protocols has been prepared to comply with:
  Simplicity in design, minimum change to existing specs
  No change required for non-relay STAs
    STA need not be even aware that its data is being relayed

## Slide 5: General Approach
The Relay is a device that consists of the following
  Two logical entities: A relay STA (R-STA) and a Relay AP (R-AP)
    R-STA associates with a parent node
    R-AP allows STAs to associate and obtain connectivity to the parent node (via the R-STA)
We outline capabilities and signaling for enabling a standard interoperable design of a Relay
  Define the capabilities and function of R-STA and R-AP
R-STA
R-AP
RELAY

## Slide 6: Advantages Of The Approach
Ensures restricting the relay framework to a tree structure since R-STA can associate with exactly one AP
Accommodates bi-directional relay functionality without any changes required for non-relay (legacy) STAs
  Usefulness/working of uplink-only relays is not clear:
    For example how will association requests be forwarded to an AP without changes to association procedure
Simple addition to existing specification text
  Addition of a few MAC capabilities to AP/STA to be used in a relay only

## Slide 7: Core Elements for Standardization
R-STA is a non-AP STA with the following capabilities
  4 address support
    Capable of transmitting/receiving a {ToDS=1,From DS=1} frame to /from the root AP it is associated with
  Supports forwarding and receiving frames from the R-AP
R-AP is an AP with the following additional capabilities
  4 address support mandatory, i.e.
    R-AP is allowed to send/receive {To DS = 1, From DS = 1} frames to an associated STA based on STA capability
    R-AP capable receiving a 4 address frame and forwarding the frame with 3 addresses to an associated STA
  Supports forwarding and receiving frames to/from the R-STA
  Able to indicate it is a R-AP
    (1 bit or indicate root-AP address/SSID in beacon, TBD)

## Slide 8: Example of Relay Operation
Relay Initialization
  R-STA associates with the root AP
  Association Request indicates 4 address capability
  After a successful R-STA association with the root AP, R-AP can send beacons or respond to probe requests
    The beacons/Probe Response frames should include the root-AP’s SSID
End STAs associate with R-AP of a Relay, based on SSID
  End STAs need not know it is a relay
  Security association is between the R-AP of the relay and STA (per hop security)
Forwarding Operation
  Performed by R-AP based on the A3 address obtained for the MSDU
  Backward learning bridge principle may be used to set up the forwarding tables
  A-MSDU can be used to improve efficiency

## Slide 9: Optimization on Fame Delivery Procedure
Relay may have to distribute MSDUs from multiple STAs to AP
All the MSDUs can be packed in a A-MSDU from relay to AP
To DS
  STA transmits frames using 3 Address format
    A1: Relay Address, A2: STA Address, A3: Destination Address
  Relay transmits frames using A-MSDU format
    A1: AP Address, A2: Relay Address, A3: BSSID Address
    DA in A-MSDU: Destination Address, SA in A-MSDU: STA Address

## Slide 10: Optimization on Fame Delivery Procedure
Relay may have to distribute MSDUs from AP to multiple STAs
All the MSDUs can be packed in a A-MSDU from AP to relay
From DS
  STA transmits frames using 3 Address format
    A1: Relay Address, A2: STA Address, A3: Destination Address
  AP transmits frames using A-MSDU format
    A1: Relay Address, A2: AP Address, A3: BSSID Address
    DA in A-MSDU: STA Address, SA in A-MSDU: DS Address

## Slide 11: Conclusion
To be competitive, 11ah must define a relay procedure:
  Allows for range extension
  Allows for improved link budget and energy saving at STAs
    Higher MCS and hence lower length transmissions can be used at STAs
Relay is an entity that logically includes a STA (to connecting with a parent AP) and an AP (STAs can associate with it)
  Forwarding can use the backward learning bridge principle and use 4 addresses
  Use of A-MSDU improves efficiency, by aggregating packets to/from multiple sources

## Slide 12: Straw poll 1
Do you agree to define a relay entity which constitutes of R-STA and an R-AP as described in slides 7?

## Slide 13: Straw poll 2
Do you agree that a relay should include root AP’s SSID in Beacon/Probe Response frames?

## Slide 14: Straw Poll 3
Do you support the frame delivery mechanism using A-MSDU format between AP and Relay?