## Slide 1: PS-Poll TXOP
Date: 2012-11-14
Authors:

## Slide 4: Introduction
STA can send a PS-Poll/trigger frame to poll the data buffered at AP. AP responds with the polled data or ACK.
STA may also have data to send to AP.
Slides [1] proposed an approach for speed frame exchange, which supports both downlink and uplink transmission.
In this presentation, we propose to include PS-Poll in the Speed Frame Exchange procedure.

## Slide 5: An Example of Speed Frame Exchange
Station with Uplink Data Only [1] :
SIFS
ACK
DATA
STA wakes from sleep, e.g. at a scheduled wake time
STA returns to sleep since last MoreData from AP is 0
SIFS
ProbeDelay
AP
STA
Wake
ACK
SIFS
STA, with buffered UL traffic, starts transmission with UL DATA instead of PS-POLL.
MoreData=0
RspFrm=00
DATA
MoreData=1
RspFrm=00
MoreData=0
RspFrm=11
MoreData=0
RspFrm=10
MoreData is used to allow responder to correctly set Response Frame bits
Because of MoreData in UL, responder knows that DATA is next

## Slide 6: PS-Poll TXOP
Problem: The first UL data from the STA in PS state
  Collisions cannot be omitted
    PS-Poll / Trigger frame is allowed for the STAs that are not indicated in TIM [2]
PS-Poll can also work as the initial frame well in Speed Frame Exchange
  PS-Poll also has More Data bit in its Frame Control field
  AP can respond with Data or ACK according to the current rule [3]
  PS-Poll does not carry data
STA can choose to send UL Data or PS-Poll to get the buffered data at AP.
ACK
PS-Poll
SIFS
ProbeDelay
AP
STA
Wake
DATA
SIFS
DATA
SIFS

## Slide 7: PS-Poll Format
Release the definition of PS-Poll format
  Allow the AID field to be switched to Duration
Frame Control | Duration/ID | BSSID (RA) | TA | FCS
2 | 2 | 6 | 6 | 4

## Slide 8: Reference
[1] 12/0834r0 Speed Frame Exchange
[2] 12/0127r1 Lowe power medium access
[3] IEEE 802.11-2012

## Slide 9: Straw poll / Pre-motion 1
Do you agree to allow PS-Poll as the first Uplink frame in Speed Frame Exchange?
  Y
  N
  Abs

## Slide 10: Straw poll / Pre-motion 2
Do you agree to change PS-Poll format as in slide 7?
  Y
  N
  Abs