## Slide 1: Other 802.11 Service Discovery Concepts
Date: 2012-11-12
Authors:

## Slide 2: Abstract
This presentation is to provide informative background of other Service Discovery concepts within the 802.11 WLAN domain.

## Slide 3: Services in 802.11
Access to Network Connectivity (e.g. Internet)
Tunneled Direct Link Setup (TDLS)
TGah - Short Beacon Frame proposal
TGai - FILS Discovery Frame proposal

## Slide 4: Access to Network Connectivity
This is the primary use of WLAN today - access to the Internet
Service Discovery involves Scanning Process
  Passive Scanning
    AP uses Beacon to Advertise availability to Network
    STAs respond to Beacon and Request Access to the Network
  Active Scanning
    STAs send probes looking for APs to respond (look for supplier)
    APs respond where Service Features match query in Probe

## Slide 5: Tunneled Direct Link Setup (TDLS) Based on the 802.11z amendment - included in 802.11-2012
TDLS Discovery used to locate supporting devices
  TDLS Discovery Request sent encapsulated in a Data Frame
    Sent thru AP with Peer STA or Broadcast address
    Alternative Setup approaches possible when peer STA is known
  TDLS Discovery Response sent directly to originating STA
  Peer devices must be operating in same BSS

## Slide 6: TGah - Short Beacon Frame Information from TGah Specification Framework (doc 11-11-1137r11)
Idea is for AP to periodically send a Short Beacon
  Would Help STAs exiting sleep locate the full Beacon
  Would Occur Regularly within the inter-Beacon interval
STAs receiving this frame
  Could quickly know if they had the AP/BSS they were looking for

## Slide 7: TGai - FILS Discovery Frame Information from TGai Specification Framework (doc 11-12-0151r13)
Idea is for AP to periodically send a Short Beacon
  Permits unassociated STAs to improve time to Discover APs
  Would Occur Regularly within the inter-Beacon interval
May Provide Info on Other Scan Targets
  Help STA set its channel switching for known APs
TGai group is discussing role and info to be carried
  If it carried enough Info for association - almost as big as beacon
TGai did look at TGah Short Beacon
  Different type of STAs involved (associated -vs- unassociated)

## Slide 8: Considerations & Possible Impacts
TDLS Discovery utilizes a request resent from AP
  Searching for a supporting device within same BSS
TGah and TGai helping STAs find the AP
  They differ in association states of STAs doing scans
PAD ‘Service Discovery’ - info for generalized search
  Need to describe service and means to distribute info
  Network Access is one service that relates to TGah and TGai work
  TDLS Discovery has a constrained search approach
Sending Data may not be the Big Issue
  Scanning Approaches may become the Awkward activity
  Directing scanning sequences may affect detection Interoperability