## Slide 1: Mandatory Optional PHY Features for 11ah
Date: 2012-11-12
Authors:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm |  |  | svverman@qti.qualcomm.com
Bin Tian | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Hongyuan Zhang | Marvell |  |  | Hongyuan@marvell.com
Eldad Perahia | Intel Corp. |  |  | eldad.perahia@intel.com
Shahrnaz Azizi | Intel Corp. |  |  | shahrnaz.azizi@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Thomas Kenney | Intel Corp. |  |  | thomas.j.kenney@intel.com
Sudhir Srinivasa | Marvell |  |  | sudhirs@marvell.com
Yong Liu | Marvell |  |  | yongliu@marvell.com
Yongho Seok | LGE | LG R&D Complex Anyang-Shi, Kyungki-Do, Korea | +82-31-450-1947 | yongho.seok@lge.com
Jinsoo Choi | LGE |  |  | 
Jeongki Kim | LGE |  |  | 
Hangyu Cho | LGE |  |  | 
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Nihar Jindal | Broadcom |  |  | 
Vinko Erceg | Broadcom |  |  | verceg@broadcom.com
Jun Zheng | Broadcom |  |  | 

## Slide 2
Authors continued:
Name | Affiliations | Address | Phone | email
Tao Tian | Qualcomm |  |  | 
Eugene Baik | Qualcomm |  |  | 
Lin Yang | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
Richard Van Nee | Qualcomm |  |  | 
Allert Van Zelst | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI | 138 Gajeongno, Yuseong-gu, Dajeon, Korea | +82 42 860 5635 | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Hyoungjin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Jaewoo Park | ETRI |  |  | parkjw@etri.re.kr
Sok-kyu Lee | ETRI |  |  | Sk-lee@etri.re.kr
Sayantan Choudhury | Nokia | 2054 University Avenue, Suite 600, Berkeley, CA 94704 | +1 510 599 9268 | sayantan.choudhury@nokia.com
Klaus Doppler | Nokia |  |  | 
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | mori.ken1@jp.panasonic.com
Harya Wicaksana | Panasonic |  |  | Harya.Wicaksana@sg.panasonic.com

## Slide 3
Authors continued:

## Slide 4: Abstract
For 11ah, sensor use-case is deemed to be one of the key areas that will drive technology adoption
Makes sense for the mandatory features in 11ah to allow for low-cost low-power sensor solutions
In this submission
  We propose an initial mandatory feature set for 11ah based on above philosophy
  Also propose a change to the existing preamble support text in SFD

## Slide 5: Proposed features for non-AP STA
Following features are critical, yet offer enough scope for simplification in implementations
  1MHz and 2MHz channel width
  1MHz PPDU, 2MHz PPDU with short preamble
  Single spatial stream MCS0 to 2, and MCS10 (for 1MHz PPDU only)
  Binary convolutional coding
  Normal Guard Interval
  Fixed Pilots

## Slide 6: Proposed features for AP-STA
For AP side, raise the bar slightly to
  1MHz and 2MHz channel width
  1MHz PPDU, 2MHz PPDU with short preamble
  Single spatial stream MCS0 to 7, and MCS10 (for 1MHz PPDU only)
  Binary convolutional coding
  Normal Guard Interval
  Fixed Pilots

## Slide 7: Long preamble support
Current spec frame work ties the mandatory/optional support of different >=2MHz preambles to device type
  Both short and long preambles are mandatory at the AP.
  For a STA,
    If it supports only 1MHz/2MHz, short preamble is mandatory, and long preamble is optional (exchanged by capability fields).
    Otherwise, both short and long preambles are mandatory.
  Any device shall be able to detect and decode SIGA field in the long preamble for CCA
We propose to remove the dependency on device type from the preamble support text
Reasons on slide 9

## Slide 8: Proposed text preamble support
We think the existing preamble support text (given on previous slide) should be changed to the following:
  For any device,
    If it supports only 1MHz/2MHz, short preamble is mandatory, and long preamble is optional (exchanged by capability fields).
    Otherwise, both short and long preambles are mandatory.
  Any device shall be able to detect and decode SIGA field in the long preamble for CCA.

## Slide 9: Reasons for removing dependency on device type
Initial 11ah solutions might share the chip between AP and STA
No reason for a AP (which is 1/2 MHz only capable) optimized for sensor use-case to support long preamble
  Long preamble has higher overhead
  Long preamble is mainly in the standard for beam-forming and MU
    Not that relevant for sensors

## Slide 10: Pre-motion 1
Do you agree to add the following text at the beginning of Section 3 (S1G Physical Layer) of the SFD ?
“An 11ah Non-AP STA shall support:
    1MHz and 2MHz channel width
    1MHz PPDU, 2MHz PPDU with short preamble
    Single spatial stream MCS0 to 2, and MCS10 (for 1MHz PPDU only)
    Binary convolutional coding
    Normal Guard Interval
    Fixed Pilots”
  Y
  N
  A

## Slide 11: Pre-motion 2
Do you agree to add the following text at the beginning of Section 3 (S1G Physical Layer) of the SFD ?
“An 11ah AP STA shall support:
    1MHz and 2MHz channel width
    1MHz PPDU, 2MHz PPDU with short preamble
    Single spatial stream MCS0 to 7, and MCS10 (for 1MHz PPDU only)
    Binary convolutional coding
    Normal Guard Interval
    Fixed Pilots ”
  Y
  N
  A

## Slide 12: Pre-motion 3
Do you support the change proposed below in the spec frame work document (Red box :existing text, Green box: proposed text) ?
  Both short and long preambles are mandatory at the AP.
  For a STA,
    If it supports only 1MHz/2MHz, short preamble is mandatory, and long preamble is optional (exchanged by capability fields).
    Otherwise, both short and long preambles are mandatory.
  Any device shall be able to detect and decode SIGA field in the long preamble for CCA
  For any device,
    If it supports only 1MHz/2MHz, short preamble is mandatory, and long preamble is optional (exchanged by capability fields).
    Otherwise, both short and long preambles are mandatory.
  Any device shall be able to detect and decode SIGA field in the long preamble for CCA.