## Slide 1: Title – PHY Author List
Date: 2012-11-11
Authors:

## Slide 3
James Wang, MediaTek.

## Slide 4: Title – MAC Author List
Date: 2012-11-08
Authors:

## Slide 7: 11-12-0852-00-00ah Sectorization for Hidden Node Mitigation by Huawei
Sectorization was proposed by Huawei to mitigate hidden node (because the number of active nodes is reduced in a specific sector)
AP divides the space in multiple sectors and use a TDM approach to allow STA transmissions in one sector at the time
Stations are allowed to transmit and receive data only in the time interval corresponding with their sector (called as Sector Interval in the drawing)
Some time interval can be left for channel access of all sectors at the same time
This approach applies to BSS with sector-only (no omni) BSS
Since STAs have to wait for its sector for channel access, latency is large
Beacon
Sector 1
Access STAs in Sector 1
Beacon
Sector 2
Access STAs in sector 2
Beacon
Sector 3
Access STAs in sector 3
Omni
Beacon
Access all STAs in the BSS
Sector Interval 1
Sector Interval 2
Sector Interval 3
Omni Interval
大同

## Slide 8: 11-12-1103-00 Sectorized Beam Operation by MediaTek et al
A proposal introducing a more flexible sectorized beam operation was presented in the Extend f-to-f September
  AP can switch back and forth between sectorized beam(s) and omni beam
  Sectorized beam is used only when AP is aware of the STA’s sector either in scheduled transmission such as RAW or during a TXOP of a STA. AP switches back to omni otherwise.
  The sectorized receive beam is used in conjunction with the sectorized transmit beam within an TXOP
  AP indicates the sectorized beam operation in Beacons, Probe Response, or Association Response.
This proposal requires an AP to be able to transmit/receive both omni and sectorized beam (We assumes that only AP (not STA) uses sectorized beam)
The forming of the sector beam is implementation specific
Beacon
Beacon
Sector 2
Beacon
AP
STA
RAW1
RAW1
RAW2
RAW2
RAW3
TXOP
James Wang, MediaTek

## Slide 9: Objectives
This follow-up presentation provides a more detailed description of the Sectorized Beam Operation to achieve
  Enhanced network spatial re-use of the wireless medium
  reduced OBSS interference
Nov 2012

## Slide 10: Benefits of the Sectorized Beam Operation
Sectorized beam transmission reduces interference to the neighboring AP and stations
Sectorized beam reception reduces interference from the neighboring AP and stations
BSS1
BSS2
Reduced
Interference
to adjacent BSS
via Sectorized
Beam Transmission
AP1
AP2
Sectorized Beam
STA1
STA2
BSS1
BSS2
Reduced
Interference
from adjacent BSS
via Sectorized
Beam Reception
AP1
AP2
Sectorized Beam
STA1
STA2
Note: STA-to-STA path loss is high
Nov 2012

## Slide 11: Issues with the Sectorized Beam Operation
Hidden Node
  If the AP transmits with a sectorized beam, some STAs in the same BSS or OBSS (in different sectors) might not receive the AP signal. This also creates the hidden node problem (which can interfere with the STA reception).
  Some STAs (such as STA2) in same BSS but not in the same sector cannot receive the sectorized beam to set their NAVs properly
AP1
Sectorized Beam
STA1
STA2
AP2
Not in the same sector as STA 1
Nov 2012

## Slide 12: Proposed Solution
A simple solution to the issues described in the preceding chart is to employ the omni-beam transmission to set up proper protection duration (for both AP and STAs) at the beginning of a TXOP and then use the sectorized beam for the remainder of the duration
This allows STAs to set their NAVs properly and prevents STAs in same BSS and OBSS AP/STA from accessing the channel at the same time
AP
STA
Omni-Beam Duration
NAV
NAV
TXOP
Sectorized-Beam Transmission and Reception Duration
Nov 2012

## Slide 13: Proposed Solution (continued)
During the sectorized beam transmission, some SO (spatially-orthogonal) OBSS STA and AP will not receive the AP1 and STA1 signals.
To enhance the spatial re-use of the medium, we want to allow the SO OBSS STA or AP to be able to access the channel during the sectorized beam transmission protected duration
AP1
STA1
Omni-Beam Duration
NAV
NAV
TXOP
Sectorized-Beam Transmit and Receiver Duration
AP1
STA1
SO OBSS STA2
SO OBSS AP2
OBSS STA3
Spatial Re-use by out-of-range OBSS STAs and APs
Note: SO (Spatially Orthogonal) OBSS STA/AP is defined as the OBSS STA/AP which can receive the omni transmission but not the sectorized transmission from AP1 and not the transmission from STA1
Nov 2012

## Slide 14: SO (Spatially Orthogonal) Condition - 1
AP can use omni-preamble to set up TXOP protection for the sectorized beam transmission.
Once the proper TXOP protection is set up with a long preamble, the sectorized transmission (with greenfield BF) shall be used for the remainder of the TXOP.
SO condition is confirmed by an OBSS STA/AP not receiving
  STA1’s transmission (OBSS STA expects a following STA1 transmission when it sees Ack Ind= 00, 10, Ack Ind=11/Ack Policy=00 in the AP1 Omni packet packet),
  and the AP1’s sectorized transmission portion within the long packet
Omni Packet
Long Packet
ACK
AP1
STA1
Example TXOP Protection
Omni-Preamble
Sectorized Beam
NAV
NAV
Can be spatially re-used by SO OBSS STA and AP
ACK or RSP
NAV protected BF duration
Nov 2012

## Slide 15: SO (Spatially Orthogonal) Condition - 2
AP can also use the short-preamble with omni-transmission to set up TXOP protection for the sectorized beam transmission.
As shown in the examples, the TXOP protection is set up at the second transmission by AP
Once the proper TXOP protection is set up, the sectorized transmission (with greenfield BF) shall be used for the remainder of the TXOP.
SO condition is confirmed by an OBSS STA/AP not receiving
  STA1’s transmission (OBSS STA expects a following STA1 transmission when it sees Ack Ind= 00, 10, or Ack Ind=11/Ack Policy=00 in the AP1 Omni packet packet)),
  and the AP1’s sectorized transmission (following the omni packet with ACK Policy=Block Ack*).
Omni packet
ACK or RSP
short packet
AP1
STA1
Example TXOP Protection
Omni-Beam
Sectorized Beam
NAV
NAV
Can be spatially re-used by SO OBSS STA and AP
NAV
ACK or RSP
ACK Policy=BACK or NO ACK*
short packet
*Note: maybe easier to have a new indicator in SIG for a following sectorized beam packet
Nov 2012

## Slide 16: SO (Spatially Orthogonal) Condition 3 - RTS/CTS
RTS
Long Preamble
ACK
AP1
STA1
Example TXOP Protection
Omni-Preamble
Sectorized Beam
NAV
NAV
Can be spatially re-used by SO OBSS STA and AP
CTS
NAV protected BF duration
RTS
Short Preamble
ACK
AP1
STA1
NAV
NAV
Can be spatially re-used by SO OBSS STA and AP
CTS
NAV protected BF duration
Ack Policy=BACK or No ACK*
Short Preamble
Short Preamble
*Note: maybe easier to have a new indicator in SIG for a following sectorized beam packet
James Wang, MediaTek

## Slide 17: SO (Spatially Orthogonal) Condition - 4
The followings illustrate an exchange initiated by STA
long packet
AP
STA
TXOP
Omni-Preamble
Sectorized Beam
NAV
NAV
Can be spatially re-used by out-of-rang OBSS STA and AP, if the AP transmission can be identified as the response frame to PS-Poll/Trigger from STA
PS-Poll/Trigger/ Other Frame
ACK or RSP
short packet
AP
STA
TXOP
Omni-Preamble
Sectorized Beam
NAV
NAV
PS-Poll/Trigger/ Other Frame
ACK or RSP
short packet
Can be spatially re-used by out-of-rang OBSS STA and AP (if the AP transmission can be identified as the response frame to PS-Poll/Trigger)
Ack Policy=BACK or No ACK*
Note: If the AP transmission cannot be identified as a response to STA’s frame, the SO OBSS condition to be confirmed by slide 14 or 15
*Note: maybe easier to have a new indicator in SIG for a following sectorized beam packet
Nov 2012

## Slide 18: Spatial Re-use Channel Access Rules
When the protection is set up by omni transmission for a duration within a TXOP and if the SO condition is confirmed by an OBSS STA/AP, the OBSS STA/AP can cancel its NAV to initiate a new SO exchange starting with a non-BF RTS/CTS.
Once an AP switches to the sectorized beam transmission during an exchange, it shall continue with greenfield sectorized beam transmission for the remainder of the protected duration
Note: SO (Spatially Orthogonal) condition is defined as a OBSS STA/AP which receives the omni transmission but not the sectorized transmission from the AP (which is either the TXOP holder or responder) and not the transmission from the STA (which is either the TXOP responder or holder).
Nov 2012

## Slide 19: Possible Sector Training Techniques
Some APs can identify STA’s best Sector during the reception of STA signals - no additional training required
Some APs can use the channel measurement report (CSI) via sounding and feedback to figure the STA’s best sector – no additional training required
For APs with few sectors, a trial-and-error approach, in which AP transmits sectorized beam packet to the STA to solicit STA’s response, can be used – Already supported
Another training and feedback proposal – see “ETRI Sectorization”
Nov 2012

## Slide 20: Conclusions
A flexible sectorized beam operation with a spatial re-use channel access rule is proposed in which
  OBSS interference is mitigated (No need for coordination between BSSs, STA driven, distributed approach)
  Significant increased in network capacity can be achieved via the spatial re-use of the medium (by SO OBSS STA and AP)
  Within RAW, STAs can have different sectors
Nov 2012

## Slide 21: Strawpoll
Do you support the proposed sectorized beam operation described in Slide 8 and Slide 18 ?
  Yes
  No
  Abstain
Nov 2012

## Slide 22: Strawpoll
Do you support the SO conditions described in Slide 14 to Slide 17
  Yes
  No
  Abstain
Nov 2012

## Slide 23: Motion 1
Move to add in the SFD the proposed sectorized beam operation described in Slide 8 and Slide 18 ?

## Slide 24: Motion 2
Move to add in the SFD the SO conditions described in Slide 14 to Slide 17
  Yes
  No
  Abstain