## Slide 1: Clarifications on 1 MHz Preamble and Timing-Related Constants
Date: 2012-11-12
Authors:
Nov 2012

## Slide 2
Nov 2012

## Slide 3
Nov 2012

## Slide 4: Motivation (1/2)
There is inconsistency for 1 MHz SIG field duration in the latest 11ah SFD [1]:
  The figure for illustrating 1 MHz preamble format shows that the duration of the SIG field is 5~6 symbols.
  However, actually the duration of SIG field is fixed to 6 symbols since the SIG field consists of 36 bits and uses MCS 10.

## Slide 5: Motivation (2/2)
The latest 11ah SFD [1] is lack of definition for duration of each of second and subsequent 1 MHz LTF fields
The latest 11ah SFD [1] is also lack of summary on timing related constants

## Slide 6: Suggested Modifications on 1 MHz Preamble Format
  The figure for illustrating 1 MHz preamble format shall be modified so that the duration of the SIG field is fixed to 6 symbols.
  For keep the consistency with ≥2 MHz short preamble, the figure for illustrating 1 MHz preamble format shall be modified so that each of second and subsequent 1 MHz LTF fields has a duration of one symbol.
Short preamble format for ≥2 MHz

## Slide 7: Summary of Timing-Related Constants
Parameter | CBW1 | CBW2 | CBW4 | CBW8 | CBW16 | Description
NSD | 24 | 52 | 108 | 234 | 468 | Number of data subcarriers per OFDM symbol
NSP | 2 | 4 | 6 | 8 | 16 | Number of pilot subcarrier per OFDM symbol
NST | 26 | 56 | 114 | 242 | 484 | Total number of useful subcarriers per OFDM symbol
NSR | 13 | 28 | 58 | 122 | 250 | Highest data subcarrier index per OFDM symbol
F | 31.25 kHz |  |  |  |  | Subcarrier frequency spacing
TDFT | 32 s = 1/F |  |  |  |  | IDFT/DFT period
TGI | 8 s = TDFT/4 |  |  |  |  | Guard interval duration
TDGI | 16 s |  |  |  |  | Double guard interval
TSGI | 4 s = TDFT/8 |  |  |  |  | Short guard interval duration
TSYML | 40 s = TDFT + TGI = 1.25  TDFT |  |  |  |  | Duration of OFDM symbol with normal guard interval
TSYMS | 36 s = TDFT + TGIS = 1.125  TDFT |  |  |  |  | Duration of OFDM symbol with short guard interval
TSYM | TSYML or TSYMS depending on the GI used |  |  |  |  | OFDM symbol duration
TSTF | 160 s = 4  TSYML | 80 s = 2  TSYML |  |  |  | STF field duration
TDSTF | n.a. | 40 s = TSYML |  |  |  | ≥2 MHz long preamble D-STF field duration
TLTF1 | 160 s = 4  TDFT + 2  TGI + TGI2 | 80 s = 2  TDFT + TGI2 |  |  |  | First LTF field duration
TLTFs | 40 s = TSYML |  |  |  |  | Second and subsequent LTF field duration
TDLTF | n.a. | 40 s = TSYML |  |  |  | ≥2 MHz long preamble D-LTF field duration
TSIG | 240 s = 6  TSYML | 80 s = 2  TSYML |  |  |  | SIG field duration
TSIGA | n.a. | 80 s = 2  TSYML |  |  |  | ≥2 MHz long preamble SIGA field duration
TSIGB | n.a. | 40 s = TSYML |  |  |  | ≥2 MHz long preamble SIGB field duration
*Note: red colored values are derived according to the proposed modification on 1 MHz preamble format in slide 4.

## Slide 8: References
[1] Proposed specification framework for TGah, IEEE 802.11-11/1137r11, September 2012.
Nov 2012

## Slide 9: Straw poll 1
Do you agree to use the following figure for illustrating 1 MHz preamble format to replace the one in 11ah SFD?
Nov 2012

## Slide 10: Straw poll 2
Do you agree to add the summary of timing related constants in slide 5 into 11ah SFD?

## Slide 11: Motion 1
Move to use the following figure for illustrating 1 MHz preamble format to replace the one in 11ah SFD?
Nov 2012

## Slide 12: Motion 2
Move to add the summary of timing related constants in slide 5 into 11ah SFD?
Nov 2012