## Slide 1: TSF Timer Freq. Management and Measurement Procedure (TFM2P)
Date: 2012-11-13
Authors:

## Slide 2: Abstract
The detailed three procedures of enhanced power saving function which employs the proposed TFM2P (TSF timer Frequency Management & Measurement Procedure) is presented.
TFM2P can be used with existing Power Saving mechanisms to allow STA waking up precisely and sleeping longer, and some sort of access control mechanisms for following operational conditions;
  numerous numbers of sensors or meters, with lower traffic at each STA, requiring battery conservation. (use case 1a/c/d/e/f)
  access control numerous numbers of sensors or meters using wake-up timing control schemes by TSF timer synchronization, rather than simple ALOHA. (RAW, TWT, PS-mode, etc.)
Notes: /c

## Slide 3: Principle of PS feature
Synchronize peer nodes to TSF
Schedule or Trigger for STA wake-up
Sleep as long as possible for peer nodes to queue
Awake as short as possible to communicate quickly
Accuracy of TSF sync does set the duty ratio , due to wake-up margin.
; for small
  c.f. Peer to peer clock frequency accuracy=40ppm,
  (1) = (36ms / 15min) + 40 = 40 + 40 ppm
  (2) = (360us / hour) + 40 = 0.1 + 40 ppm or = (3.6ms / 10 hour) +40 = 0.1 +40 ppm

## Slide 4: Wake-up synchronization Simple AP announcement of TSF accuracy (1)
Wake-up Timing margin depends on TSF timer freq. accuracy △;
Wake-up margin -△· (TW – TS)
AP
(e.g. TSF master)
STA
(e.g. TSF slave)
sleep again
scheduled wake-up time (ideal case)
actual sleep duration
TW
± △· (TW –TS)
≈
TW
notified
△ includes
accuracy of
both AP & STA
< 11-12/130r0 “Beacon Reception of Long Sleeper” >
  AP is supposed to announce TSF accuracy △, (△<100ppm)
  STA is able to wake up at (TW –TS)(1 - △) +TS
  TS : TSF timer value just after last time it was synchronized
STA
awake
TS
(IEEE802.11-2012)
Tolerance
±100ppm

## Slide 5: Wake-up synchronization Simple AP announcement of TSF accuracy (2)
Awake period of STA may become much longer than actual
Communication.
Wake-up margin - △· (TW –TS)
AP
(e.g. TSF master)
STA
(e.g. TSF slave)
sleep again
scheduled wake-up time (ideal case)
actual sleep duration
TW
± △· (TW –TS)
≈
actual
communication
TW
notified
TW-actual
actual wake-up point of time
Communication may happen within green window.
STA have to be awake during entire blue period
while actual communication duration may be a part of awake period.
STA
awake
± △·( TW – TS)
STA awake

## Slide 6: Wake-up sync. using TFM2P AP announcement of TSF timer stability (1)
Wake-up Timer Stability information (±ε) as well as △;
compensated by measured TSF frequency Tw-compen
announced AP
( TSF master)
Receiver side
measured STA
(e.g. TSF master)
sleep
again
scheduled wake-up time (ideal case)
TW
± △· TW
measured AP side
point of time (by STA)
±ε
△measured
≈
Tw notified after TSF frequency measurement
STA
awake
-ε
wake-up margin
< TFM2P involves two parameters, i.e. △ and ε >
  AP advertise △worst and ε
  STA to wake up at,
  (TW-compen –TS)(1 - ε)+TS ≃ (TW –TS)(1 + △measured - ε) +TS

## Slide 7: Wake-up sync. using TFM2P AP announcement of TSF timer stability (1)
Wake-up Timer Stability information (±ε) as well as △ ;
compensated by measured TSF frequency Tw-compen
announced AP
( TSF master)
Receiver side
measured STA
(e.g. TSF master)
sleep
again
scheduled wake-up time (ideal case)
TW
± △· TW
measured
point of time
-ε
△measured
≈
Tw notified after TSF frequency measurement
actual
communication
TW-actual
actual point of time
STA
awake
STA to wake up at
(TW-compen –TS)(1 - ε)+TS ≃ (TW –TS)(1 + △measured - ε)+TS
after once TFM2P has carried out .

## Slide 8: Comparison of Wake-up synchronization (1)
Simple Accuracy Announcement and TFM2P (frequency measurement)
(Tw - TS) (1- △advertised ) + TS
Less wake-up margin
by TSF freq. offset compensation
and freq. stability information
awake
sleep again
sleep
STA w/t TFM2P
(e.g. TSF slave)
wake-up margin
using accuracy information
(△advertised )
AP
(e.g. TSF master)
STA w/o TFM2P
(e.g. TSF slave)
wake up
sleep again
scheduled wake-up time Tw
sleep
± △advertised · ( TW –TS)
awake
actual
communication
Informed Tw is used
with △advertised
(TW – TS)(1 + △measured - εadvertised) + TS
Informed Tw and εadvertised
is used with
measured frequecy

## Slide 9: Comparison of Wake-up synchronization (2)
AP
STA
STA
STA
AP
STA
STA
STA
AP
STA
STA
STA
Simple
accuracy
announcement
(broadcast)
Broadcast
(uni-directional)
Receiving
broadcasted
accuracy information,
then calculate wake-up margin, △AP+STA
Time Stamp
announcement
for TFM2P
(broadcast)
Time Stamp
handshake for
TFM2P
(node by node)
Broadcast
(uni-directional)
Unicast handshake
(node by node)
accuracy △AP
accuracy
accuracy
Stability ε
B1+B1timestamp
B2+B2timestamp
Stability ε
M1+Ack
M2+Ack
M4+Ack
M5+Ack
M6+Ack
Receiving
four broadcasted
time stamp for measuring TSF freq.,
then calculate wake-up margin, △measured , ε
B1+B1timestamp
B2+B2timestamp
B2+B2timestamp
B1+B1timestamp
Handshaking
two time measurement
to determine each precise offset and freq.,
then calculate wake-up margin, △measured , ε
M3+Ack
M7+Ack
M8+Ack
Proposed three procedures of TFM2P for Power Saving

## Slide 10: Comparison of Wake-up synchronization (3)
Scheme | Broadcast or Handshake | Inaccuracy information | Resulting Wake-up Accuracy | Battery life improvement (ex. estimated) | Update | Required mechanism | PHY/MAC Support
IEEE802.11 2012 (Conventional) | None | Pre-defined by Std. | ±100 ppm +offset | Reference (1.0) | None | TSF synch only | Not required
Timer accuracy notification [11-12/130r0] | Broadcast w/o handshake | by AP announcement | ±20~50 ppm +offset | 1.6 times (1.2~2.0) | Not Required | TSF timer freq. accuracy advertisement | MAC: required
TFM2P | Broadcast (Time-Stamp Announcement) w/o handshake | by direct TSF frequency measurement + AP stability advertisement | ±2~10 ppm +offset | 2.5 times (1.5~4.0) | Conditionally preferred | TSF timer freq. accuracy advertisement + Two time measurements + Calculation & compensation | MAC: required PHY: optional
 | Node by node w/t bi-directional handshake |  | ±1~5 ppm null offset |  | Conditionally Required |  | MAC: required PHY : preferable

## Slide 11: Typical mechanism of TFM2P using Broadcast (1)
Full beacons with DTIM always carry ToD time stamp for TFM2P.
All ToD time stamps correspond to its N-times previous DTIM beacon.
Each pair of successive ToD time stamps may be used for TSF frequency estimation with corresponding previous pair of ToA time stamps.
Beacon Interval
Beacon Transmissions
( can be short beacon )
Busy medium other transmissions
Full Beacon DTIM
N-times previous ToD time stamp
Full Beacon DTIM
N-times previous ToD time stamp
N-times DTIM Interval ( N ≥ 1 )
TIM
TIM
TIM
TIM
≈
≈
≈
TFM2P frequency measurement pair
DTIM
DTIM
AP as Clock master broadcasts Time Stamp Announcement with no handshake.

## Slide 12: Typical mechanism of TFM2P using Broadcast (2)
t1=ToD(B1)
t9=ToD(B3)
B4B3-timestamp
B2B1-timestamp
t2=ToA(B1)
t6=ToA(B2)
t1 are known
t5 are known
Sending STA(f1)
Receiving STA(f2)
: can be a network wide common value
of virtual master clock frequency, and
determines the resolution of each time
stamp measurement.
e.g. 1MHz, and 1us (i.e. TSF resolution) ( TBD : always fixed 1us or defined by upper layer )
f1⧋
f2 =
f2= f1
t5=ToD(B2)
B3B2-timestamp
t10=ToA(B3)
Estimation in this figure, t9 and t10 is not used.
B1B0-timestamp
AP as Clock master broadcasts Time Stamp Announcement with no handshake.

## Slide 13: Typical mechanism of TFM2P using Broadcast (3)
f1⧋ = 1MHz : f1 with no error
i.e. = (t5-t1) ( perfectly accurate timestamp )
No information has to be informed to peer node
for f2 calculation.
f2= f1
f2 =
therefore : = ⧋1+δ2
f1 ≈ at AP, as master frequency;
δ2 (e.g. ppm) should be the calibration factor of f2 to schedule Tw , wake-up time.
t1=ToD(B1)
t9=ToD(B3)
B4B3-timestamp
B2B1-timestamp
t2=ToA(B1)
t6=ToA(B2)
t1 are known
t5 are known
Sending STA(f1)
Receiving STA(f2)
t5=ToD(B2)
B3B2-timestamp
t10=ToA(B3)
Estimation in this figure, t9 and t10 is not used.
B1B0-timestamp

## Slide 14
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
Ack
M1
Ack
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M2)
t7=ToD(M2)
t1and t4 are known
t5and t8 are known
offset1 ⧋ [(t2-t1)-(t4-t3)]/2
offset2 ⧋ [(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)
M2timestamp
f1⧋
: Network wide virtual master clock
frequency. However, in general, there
may exist no master clock station,
neither AP nor STA. Therefore, each
STA may behave to synchronize to
hypothetical or specific STA ‘s master
clock with freq. of , using any pre-
defined control algorithm.
Typically, the freq. may determine
the resolution of time stamp, and Tw .
TFM2P mechanism by node-by-node handshake (1)
Handshake can be between AP/MP & STA, STA & STA or MP & MP.
M1timestamp

## Slide 15
t1=ToD(M1)
t4=ToA(Ack)
t5=ToD(M2)
t8=ToA(Ack)
M2
Ack
Ack
M1
Ack
Ack
t2=ToA(M1)
t3=ToD(M1)
t6=ToA(M2)
t7=ToD(M2)
offset1=[(t2-t1)-(t4-t3)]/2
offset2=[(t6-t5)-(t8-t7)]/2
Sending STA(f1)
Receiving STA(f2)
f1⧋ = ⧋ 1+δ1
and therefore ratio / ⧋ p, have to be known by all STAs within network.
If STA(f1) knows the accuracy of f1 , i.e. ,
δ1 (ppm) should be informed to STA(f2).
At STA(f2) side, = (1+δ1 ) can be re-calculated.
f2= f1
TFM2P mechanism by node-by-node handshake (2)
How all STAs synchronizes each other is out of scope of this standard.
M1timestamp
M2timestamp
f2⧋ = ⧋ 1+δ2

## Slide 16
TFM2P mechanism by node-by-node handshake (3)
How all STAs should synchronize each other after node-by-node calibration can be achieved, is out of scope of this standard.
However, node-by-node TFM2P is expected to be instrumental because of following reasons,
By utilizing existing 11v timing measurement scheme identical to PTP/IEEE1588, the best time and frequency accuracy of TSF for wake up can be used with the precise timing offset nulling.
This also means that the quick frequency estimation can be possible using shorter time interval of two time measurements.
IBSS, MBSS without AP can still utilize TFM2P for wake up.
To perform such sort of applications, for example, timing sensitive control using DLS, TFM2P works.
Forward looking applications may be facilitated by precise synch..

## Slide 17: Procedure (1) : General ( IE in full beacon body )
STA can examine TFM2P availability in Extended Capabilities Element by acquiring full beacon [ bit xx-xx+1 : TBD ]. If AP provides TFM2P, STA are able to select and perform any of TFM2P service available, i.e. simple accuracy announcement, TFM2P time stamp announcement (AP-broadcast), or TFM2P node-by-node handshake.
            Even if all STAs can use simple TSF accuracy information only without frequency measurement, AP should still provide accuracy announcement and stability information of corresponding services in TFM2P IE carried by frame body of full beacon including the detailed parameters. It is up to STA’s decision if any frequency measurement is performed or not.
            As like existing TSF timer advertisement, STA shall correct its TSF timer offset with AP timer, and this corrected timer value has to be stored as TS , which is the origin of wake up timing calculation.

## Slide 18: Procedure (2) : Time Stamp Announcement ( AP-broadcast )
If AP provides TFM2P and a STA selects the timestamp announcement (AP-broadcast) service to calculate its wake up margin, the STA has to obtain AP timer stability information (±εadvertised ) and number of times ( N ) of full beacon carrying DTIM to measure AP TSF timer frequency. Usually, N should be more than 1sec = 1million times of 1us TSF.
Then the STA acquires three consecutive full beacons N-times apart each other and takes ToA information of first two reception by STA PHY itself. Furthermore, STA collects the ToD information corresponding to first two full beacon carried by last two beacons.
Now the STA has two set of ToD-ToA pairs from three full beacon and can estimate the frequency correction coefficient (δ2 ; ppm). The timing resolution of stamps may be always 1us or defined by higher layer [TBD].
Eventually STA determines the wake up margin from, △measured , εadvertised and STA specific stability ( εSTA ; see “implementation practice”) if required.

## Slide 19: Procedure (3) : Node-by-node handshake ( STA-unicast )
If a STA provides TFM2P node-by-node handshake and peer STA selects this handshake as the frequency measurement mechanism to calculate its wake up margin, the STA has to acquire peer timer stability information (±εadvertised ) and the frequency correction coefficient (δ1). In case of WLAN, the master clock frequency doesn’t make a important sense and can be always same as TSF clock of 1MHz (1us) for . This simplifies the entire TFM2P procedure ( p = 1, always ) while the network can not involve different master frequency other than 1MHz. [TBD]
The peer information can be acquired using WNM request/response (action) frame for TFM2P [TBD], which is carrying necessary IE [TBD].
Then, a pair of timing measurements can be performed along with existing standardized procedure (IEEE802.11-2012), while the interval of two time measurements has to be more than 1sec = 1million times of 1us, TSF granularity usually or defined by higher layer [TBD].

## Slide 20: Procedure (3) : Node-by-node handshake ( STA-unicast )
…. Continued from previous slide.
The data format of timestamp should be same as 802.1AS structure with 1ns resolution.
    struct Timestamp
    {
    UInteger48 seconds;
    UInteger32 nanoseconds;
    };
Now the STA has two set of ToD-ToA pairs from two times repetition of timing measurement handshake and can estimate the frequency correction coefficient (δ2 ; ppm), using peer correction coefficient (δ1 ; ppm).
Eventually STA determines the wake up margin from, △measured , εadvertised , δ1 and STA specific stability factors ( εSTA ) if required.
( refer to “implementation practice” )

## Slide 21: Addition to Extended Capabilities IE [TBD]
Extended capability Element.
Octets : 1 1 n
Element ID = 127
Capability bit = xx - xx+1 [ TBD, e.g. 49-50 ]
Element ID | Length | Capabilities
bit | Information | Notes
xx-xx+1 | TFM2P Service availability | Set to 0, when unavailable. TSF accuracy = ±100ppm Set to 1, when simple accuracy announcement of TSF and TFM2P timestamp announcement (AP-broadcast) are available. (for AP only) Set to 2, when simple accuracy announcement of TSF and/or TFM2P node by node handshake are available. (for AP (and), for STA(and/or)) Set to 3, when all TFM2P timestamp announcement (AP-broadcast), node by node handshake and simple accuracy announcement are available. (for AP only)

## Slide 22: New IE for TFM2P (1) [TBD]
Information Element.
Octet : 1 1 1 1 1 1 10
Element ID = xxx [ TBD, e.g. 175 ]
Capability
  0 for TFM2P unavailable. Accuracy has to be ±100ppm and stability has to be ±0.
  1 for TFM2P simple accuracy announcement of TSF and TFM2P timestamp announcement (AP-broadcast) are available as well. (usually for AP only)
  2 for TFM2P simple accuracy announcement of TSF and TFM2P node by node handshake are available as well. (for both AP and STA)
  3 for all TFM2P simple accuracy announcement of TSF, timestamp announcement (AP-broadcast) and node-by-node handshake are available. (usually for AP only)
  4 for TFM2P simple accuracy announcement of TSF is only available. (usually for STA only)
  5 for TFM2P node-by-node handshake is only available. (usually for STA only)
  6-255: reserved.
Element ID | Length | TFM2P capability | Accuracy | Stability | N | ToD Time stamp AP-broadcast | reserved
Note, N : number of times of DTIM beacon for the interval
between two time measurements

## Slide 23: New IE for TFM2P (2) [TBD]
Information Element.
Octet : 1 1 1 1 1
Accuracy : 2 times integer in ppm (means ±value = 0 to absolute max. ) i.e. resolution of half ppm
Stability : 4 times integer in ppm (means ±value = 0 to absolute max. ) i.e. resolution of quarter ppm
ToD Time stamp announcement in case of AP-broadcast
    struct Timestamp
    {
    UInteger64 microseconds;
    UInteger16 nanoseconds;
    };
Element ID | Length | TFM2P capability | Accuracy | Stability | ToD Time stamp AP-broadcast | reserved
This is different from 802.1AS structure,
because TSF timer resolution of 1us has to
be maintained.

## Slide 24
Implementation practice for TFM2P mechanism
How much wake up margin should set at each STA is out of the scope of Standard. However following implementation practice should work for typical implementation of usual sensor nodes including all of use case 1 applications in general.
Wake up margin at the frequency estimating STA may be the sum of peer stability information and actual latest fluctuation of measurement by itself.
The difference ( i.e. fluctuation ) between latest measured frequency correction coefficient and previous coefficient ( △ δ2 ) can be summed up with the advertised stability information (±εadvertised ), in addition to the STA’s stability coefficient value.
This estimating STA side stability coefficient value with the fluctuation ( △ δ2 ) can be always updated and maintained for next δ2 estimation using TFM2P. ( εSTA )
If the fluctuation (△ δ2 ) is small, εSTA will be minimum.

## Slide 25
Straw poll (1)
Do you support to include the TSF timer frequency measurement function into SFD.
  Yes
  No
  Abstain

## Slide 26
Straw poll (2)
Do you support to include proposed TFM2P procedure as the TSF timer frequency measurement function, into SFD.
  Yes
  No
  Abstain

## Slide 27: References
[1] 11-12/130r0 “Beacon Reception of Long Sleeper”
[2] IEEE802.11-2012
[3] IEEE1588/PTP
[4] 11-11/0905r5” TGah Functional Requirements and Evaluation Methodology Rev. 5”
[5] PAR and 5C

## Slide 28: Appendix : PHY-assist rules for time stamp
Timing Measurement Procedure: IEEE802.11-2012
Standardized mechanism of ToD/ToA time stamp
  Proposed Measurement Point for both ToD/ToA
    Either end of STF or start of LTF : tLTF
Proposed ToA validation by Sig with no CRC error
  Every detection of tLTF is stored (over written) if CRC passed.
By TFM2P Procedure
  ToA time stamp of frame destined to the STA itself only be used.

## Slide 29: Examples

## Slide 30: Frequency Measurement (example 1)
f1⧋ =
f2 = =
= 1000000
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578901-1234567890)-(1234667890-1234678901)]/2
= 11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627477-1235616466)-(1235716466-1235727477)]/2
= 11011
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
No frequency error
Propagation Delay=0
f2= f1 = f1 = f1

## Slide 31: Frequency Measurement (example 2)
f1⧋
f2= f1 = f1
f2 = =
= 1000000
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578902-1234567890)-(1234667892-1234678902)]/2
= (11012+11010)/2=11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627478-1235616466)-(1235716468-1235727478)]/2
= (11012+11010)/2=11011
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
No frequency error
Propagation Delay=1uSec

## Slide 32: Frequency Measurement (example 3)
f2 = =
= 1000003.815
f2= f1 = 1.000003815 f1
f1⧋ =
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578902-1234567890)-(1234667892-1234678902)]/2
= (11012+11010)/2=11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627482-1235616466)-(1235716468-1235727482)]/2
= (11016+11014)/2=11015
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
f2 frequency offset ≈ 4ppm
Propagation Delay=1uSec

## Slide 33: Frequency Measurement (example 4)
f2 = =
= 1000007.629
f2= f1 = 1.000003815 f1
f1⧋ =
3.815
offset1= [(t2-t1)-(t4-t3)]/2
=[(1234578902-1234567890)-(1234667892-1234678902)]/2
= (11012+11010)/2=11011
offset2=[(t6-t5)-(t8-t7)]/2
=[(1235627482-1235616466)-(1235716468-1235727482)]/2
= (11016+11014)/2=11015
t1
t4
t5
t8
M2
Ack
M2
Ack
M1
Ack
M1
Ack
t2
t3
t6
t7
Sending
STA(f1)
Receiving
STA(f2)
f1,f2 frequency offset ≈ 4ppm
Propagation Delay=1uSec

## Slide 34: End