## Slide 1: Setting of ProbeTimer
Authors:
Name | Affiliations | Address | Phone | email
Lin Cai | Huawei | 3601 Algonquin Road, Suite 1000, Rolling Meadows, IL 60008 | 1-847-848-1778 x 379 | Lin.cai@huawei.com
George Calcev | Huawei | 3601 Algonquin Road, Suite 1000, Rolling Meadows, IL 60008 |  | George.Calcev@huawei.com
01/02/2013

## Slide 2: Active Scanning in Existing Standard Sepcification[1]
If PHY-CCA.indication (busy) primitive is not detected, scan the next channel when ProbeTimer reaches MinChannelTime
Otherwise, when ProbeTimer reaches MaxChannelTime, process all received probe responses
[1] 11REVmb-D12, Cls 10.1.4.3.3

## Slide 3: Active Scanning (Cont’d)
If CCA busy primitive is detected but no AP exists in the scanned channel, STAs have to scan for MaxChannelTime before switching to the next channel
  MinChannelTime = 0.67 ms [2,3]
  MaxChannelTime = 15 ms [2,3]
[2] M. Ryong Jeong, et.al., ”Fast Active Scan for Measurement and Handoff,” DoCoMo USA Labs, Contribution to IEEE802, May 2003.
[3] M. Emmelmann, “Achievable gains in AP Discovery,” FOCUS, doc. IEEE 802.11-10/0922r1
Probe
MinChannelTime
MaxChannelTime

## Slide 4: Problem with Current Active Scanning Procedure
CCA is based on energy detection technique
In a WiFi channel without an AP, it is possible that a STA may sense the channel busy due to transmissions of
  Probe requests from other STAs
  Non-Wifi devices such as microwave, cordless phone, etc.
  Energy leakage from adjacent channels
If PHY-CCA.indication (busy) primitive invoked by probe requests’ transmissions or non-WiFi devices, a STA needs to wait for a MaxChannelTime, which causes long delay

## Slide 5: Proposed Solution
If CCA busy primitive is not detected, a STA sets its ProbeTimer to MinChannelTime
If CCA busy primitive is detected, a STA processes the received information; if the STA finds that busy indication is only invoked by Probe Request messages or non-decodable messages, STA may set the ProbeTimer to MedChannelTime, which is smaller or equal to MaxChannelTime, as there is no hard evidence of APs’ presence

## Slide 6: Proposed Solution
If CCA busy primitive is detected, a STA processes the received information; the STA sets their ProbeTimer to MaxChannelTime if it receives messages with implicit or explicit evidence of APs’ existence, including data frames, management frames (association, authentication, etc.), and control frames (CF-End, CF-End+ACK frames, PS-poll, etc.)
Probe
MinChannelTime
MaxChannelTime
Idle channel
Channel busy invoked by probe requests or non-decodable messages
Channel busy invoked by other data/management/control messages
MedChannelTime

## Slide 7: Conclusion
In current standard, energy detection based CCA is used for determining the ProbeTimer, which may cause long scanning delay when no AP exists in the scanned channel
To reduce unnecessary scanning delay and make a wise decision, STAs should be able to decide its ProbeTimer based on the detection of other messages rather than CCA only

## Slide 8: Straw Poll 1
Do you agree to: “Add a new ProbeTimer called MedChannelTime that allows a STA during the active scanning procedure to move to the next channel when MedChannelTime expires if only Probe Requests or non-decodable energy is sensed in the scanned channel?”
Yes
No
Need more information

## Slide 9: Straw Poll 2
Do you agree to modify the condition of ProbeTimer setting to: “a STA should first check PHY-CCA.indication primitive, and if it is detected busy, shall check the received information and ignore Probe Request and non-decodable messages?”
Yes
No
Need more information

## Slide 10: Motion1
Do you agree to: “Add a new ProbeTimer called MedChannelTime that allows a STA during the active scanning procedure to move to the next channel when MedChannelTime expires if only Probe Requests or non-decodable energy is sensed in the scanned channel?”
Yes
No
Abstrain

## Slide 11: Motion 2
Do you agree to modify the condition of ProbeTimer setting to: “a STA should first check PHY-CCA.indication primitive, and if it is detected busy, shall check the received information and ignore Probe Request and non-decodable messages?”
Yes
No
Abstain

## Slide 12: Backup Slides Delay of Active Scanning
M APs uniformly distributed over N channels
  The probability that there is at least one AP in any given channel is
    P=1-(1-1/N)^M
  Given an AP exists in a given channel, the expected time a STA spends in scanning this channel is
    T1= ProbeDelay + Tx_ProbeReq + MaxChannelTime
  Given no AP exists in a given channel
    CCA busy primitive is not detected (ideal case):
    T2_{ideal}=ProbeDelay + Tx_ProbeReq + MinChannelTime
    CCA busy primitive is detected due to interference/requests (non-ideal case):
    T2_{Non-ideal}=ProbeDelay + Tx_ProbeReq + MaxChannelTime
  Expected scanning delay in one channel: D=T1*P + T2 *(1-P)

## Slide 13: Delay of Active Scanning (Cont’d)
Parameters[3]:
  ProbeDelay = 0.1 ms
  MinChannelTime = 0.67 ms
  MaxChannelTime = 15 ms
  Tx_ProbeReq = 0.4 ms
  N=14 channels
Chart: 
Ideal Case | 2.1936 | 3.144 | 4.0266 | 4.8461 | 5.6071 | 6.3138 | 6.9699 | 7.5792 | 8.145 | 8.6703 | 9.1582 | 9.6112 | 10.0318 | 10.4224 | 10.7851 | 11.1218 | 11.4346 | 11.725 | 11.9946 | 12.245
Non-ideal Case | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5
Number of APs M
Expected scanning delay over each channel (ms)
[3] M. Emmelmann, “Achievable gains in AP Discovery,” FOCUS, doc. IEEE 802.11-10/0922r1

## Slide 14: Delay Comparison
Expected delay with proposed timer
  D=T1*P + T2_{proposed} *(1-P), where
  T2_{proposed} = ProbeDelay + Tx_ProbeReq + ProbeTimer (e.g., 2ms or 5ms)
Number of APs M
Expected scanning delay over each channel (ms)
Chart: 
Ideal Case | 2.1936 | 3.144 | 4.0266 | 4.8461 | 5.6071 | 6.3138 | 6.9699 | 7.5792 | 8.145 | 8.6703 | 9.1582 | 9.6112 | 10.0318 | 10.4224 | 10.7851 | 11.1218 | 11.4346 | 11.725 | 11.9946 | 12.245
Non-ideal Case | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5
MedChannelTime=2ms | 2.9643 | 3.8597 | 4.6911 | 5.4632 | 6.1801 | 6.8458 | 7.464 | 8.038 | 8.571 | 9.0659 | 9.5255 | 9.9522 | 10.3485 | 10.7165 | 11.0582 | 11.3754 | 11.67 | 11.9436 | 12.1976 | 12.4335
MedChannelTime=5ms | 5.75 | 6.4464 | 7.0931 | 7.6936 | 8.2512 | 8.769 | 9.2498 | 9.6962 | 10.1108 | 10.4957 | 10.8532 | 11.1851 | 11.4933 | 11.7795 | 12.0452 | 12.292 | 12.5211 | 12.7339 | 12.9315 | 13.115