## Slide 1: Higher Layer Packet Container Proposal Presentation
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com
Date: 2013-01-07
Authors:

## Slide 2: Abstract
This document is presentation material about 11-13/xxxxrx.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: FILS Authentication/Association (D0.2)
STA
AP
Authentication
Authentication
Association Request
Association Response
Key Derivation
Key Derivation
Protected

## Slide 5: Proposal
Higher Layer Packets (HLPs) are piggy-backed in Association Request/Response as IE(s).
  They can be protected.

## Slide 6: HLP Container IE
Type 1
  Used for non-fragmented HLP and the first element of fragmented HLP.
Type 2
  Used for the subsequent elements of fragmented HLP.

## Slide 7: Example of Usage 1 (1 HLP, non-fragmented)
HLP length: 200 octets, LLC/SNAP length: 8 octets
200 octets
200 octets
IE Header (NFrag = 0)
Type 1

## Slide 8: Example of Usage 2 (1 HLP, fragmented)
HLP length: 600 octets, LLC/SNAP length: 8 octets
  Split to 3 elements, 234 octets (A), 255 octets (B) and 111 octets (C) in order.
600 octets
A: 234 octets
B: 255 octets
C: 111 octets
A: 234 octets
IE Header (NFrag = 2)
B: 255 octets
IE Header
IE Header
C: 111 octets
Type 1
Type 2
Type 2

## Slide 9: Example of Usage 3 (2 HLPs, non-fragmented)
HLP A length: 200 octets, LLC/SNAP length: 8 octets
HLP B length: 200 octets, LLC/SNAP length: 8 octets
A: 200 octets
A: 200 octets
IE Header (NFrag = 0)
Type 1
B: 200 octets
B: 200 octets
IE Header (NFrag = 0)
Type 1

## Slide 10: Example of Usage 4 (2 HLPs, fragmented)
HLP A length: 600 octets, LLC/SNAP length: 8 octets
HLP B length: 600 octets, LLC/SNAP length: 8 octets
A1: 234 octets
IE Header (NFrag = 2)
Type 1
A: 600 octets
Type 1
B: 600 octets
A2: 255 octets
A3: 111 octets
B1: 234 octets
B2: 255 octets
B3: 111 octets
A1: 234 octets
IE Header
A2: 255 octets
IE Header
A3: 111 octets
IE Header (NFrag = 2)
B1: 234 octets
IE Header
B2: 255 octets
IE Header
B3: 111 octets
Type 2
Type 2
Type 2
Type 2

## Slide 11: Forward Sequence 1 (Successful Authentication, HLP from 3rd party in time)
The AP forwards HLP-A from non-AP STA after successful authentication.
If the AP receives HLP-B from 3rd Party in dot11AssociationResponseTimeOut, the AP forwards it in Association Response.
STA
AP
Association Request (w/HLP-A)
Association Response (w/HLP-B)
3rd Party
Successful Authentication
HLP-A
HLP-B
dot11AssociationResponseTimeOut

## Slide 12: Forward Sequence 2 (Authentication Failure)
The AP silently discards HLP-A after authentication failure.
STA
AP
Association Request (w/HLP-A)
3rd Party
Authentication Failure
Silently discards HLP-A

## Slide 13: Forward Sequence 3 (Successful Authentication, HLP from 3rd party NOT in time)
The AP forwards HLP-A from non-AP STA after successful authentication.
If the AP receives HLP-B from 3rd Party after dot11AssociationResponseTimeOut, the AP forwards it as a Data Frame.
STA
AP
Association Request (w/HLP-A)
Association Response (w/HLP-B)
3rd Party
Successful Authentication
HLP-A
HLP-B
dot11AssociationResponseTimeOut
HLP-B as Data Frame

## Slide 14: Questions & Comments

## Slide 15: Motion
Move to include the text in 11-13/xxxxrx into the TGai Draft Specification Document.
Moved:
Second:
Result (Y/N/A):