## Slide 1: Higher Layer Packet Container Proposal Presentation
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com
Date: 2013-03-18
Authors:

## Slide 2: Abstract
This document is a presentation material about 11-13/0040r4.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Background
We discussed about higher layer setup. Such as,
  11-11/977r6
  11-11/1047r5
  11-11/1108r1
  11-11/1167r0
In these discussions, I proposed DHCP proxy protocol but some issues are found through the discussion.
  Delayed server response
    Require to define new management frames
  Roaming between FILS and non-FILS APs.
Generic Container for higher layer is better.

## Slide 5: Concept
The AP forwards HLP-A from non-AP STA to 3rd party after successful key confirmation.
The AP forwards HLP-B from 3rd party to non-AP STA.
STA
AP
Association Request (HLP-A)
Association Response (HLP-B)
3rd Party
Successful Key Confirmation
HLP-A
HLP-B
Beacon/Probe Resp.
Authentication
Key Derivation
Key Derivation

## Slide 6: Issues
How to fragment large higher layer packet?
How to protect the higher layer packets?
How long to wait the response from the servers?
These will be solved by Rene’s proposal.

## Slide 7: Proposal
Higher Layer Packets (HLPs) are piggy-backed in Association Request/Response as IE(s).
  They can be protected.
Define 3 new attributes.
  dot11HLPTransportDuringAssoc
  dot11HLPMaxWaitTime
  dot11HLPWaitTime
Define 2 new IEs.
  HLP Max Wait Time IE
  HLP Wait Time IE
Define 1 new element for Secure Container (it may proposed by Rene)
  HLP Container IE

## Slide 8: Attributes
dot11HLPTransportDuringAssocActivated
  Truth Value
dot11HLPMaxWaitTime
  Integer (millisecond)
  This attribute indicates the maximum time that the AP allows to wait the HLP after the AP receives Association Request.
dot11HLPWaitTime
  Integer (millisecond)
  This attribute indicates the time that the non-AP STA requests to wait the HLP after the AP receives Association Request.
  dot11HLPWaitTime <= dot11HLPMaxWaitTime
  dot11HLPWaitTime < dot11AssociationResponseTimeOut

## Slide 9: HLP Max Wait Time IE
Max wait time in unit of millisecnd.
Transmitted in Beacon and Probe Response.

## Slide 10: HLP Wait Time IE
Wait time in unit of millisecnd.
Transmitted in Association Request.

## Slide 11: HLP Container element
This element is capsulated in Secure Container.

## Slide 12: HLP Wait Time Negotiation
AP transmits HLP Max Wait Time in Beacon and Probe Response.
STA selects the value of HLP Wait Time that is less than dot11AssociationResponseTimeOut and less than or equal to the received HLP Max Wait Time.
STA transmits HLP Wait Time to AP by Association Request.
AP waits the duration of HLP Wait Time to receive HLP from 3rd party.
If HLP(s) comes in time, AP forwards it to STA by Association Response.
If HLP(s) does not come in time, AP forwards it to STA by data frame.
STA
AP
3rd party
(e.g. DHCP server)
3. Assoc. Req.
(HLP Wait Time
HLP-A)
4. HLP Wait Time
5. Assoc. Resp.
(HLP-B)
1. Beacon/Probe Resp.
(HLP Max Wait Time)
2. Select
HLP Wait
Time
HLP-A
HLP-B
HLP-B’
6. Data Frame
(HLP-B’)

## Slide 13: Why “HLP Max Wait Time” and “HLP Wait Time” are required?
AP
  AP may not care about the contents of HLP.
  AP does not know how long to wait the response from 3rd party. (AP does not know even whether a response will come or not.)
  AP does not know the attribute dot11AssociationResponseTimeOut of the STA. But AP must transmit Assoc. Resp. by STA’s dot11AssociationResponseTimeOut.
  AP may hold the state of association process. It may use memory. So AP may want to restrict HLP wait time.
STA
  STA knows its own dot11AssociationResponseTimeOut.
  STA knows the contents of HLP and expected wait time.
  STA may want to associate fast without HLP piggy-backing.
So HLP wait time negotiation is required.

## Slide 14: Forward Sequence 1 (Successful Key Confirmation, HLP from 3rd party in time)
The AP forwards HLP-A from non-AP STA after successful authentication.
If the AP receives HLP-B from 3rd Party in dot11HLPWaitTime, the AP forwards it in Association Response.
STA
AP
Association Request
(dot11HLPWaitTime, HLP-A)
Association Response (HLP-B)
3rd Party
Successful Key Confirmation
HLP-A
HLP-B
dot11HLPWaitTime
Beacon/Probe Resp.
(dot11HLPMaxWaitTime)
Authentication

## Slide 15: Forward Sequence 2 (Key Confirmation Failure)
The AP silently discards HLP-A after authentication failure.
Key Confirmation Failure
Silently discards HLP-A
STA
AP
Association Request
(dot11HLPWaitTime, HLP-A)
3rd Party
Beacon/Probe Resp.
(dot11HLPMaxWaitTime)
Authentication

## Slide 16: Forward Sequence 3 (Successful Authentication, HLP from 3rd party NOT in time)
The AP forwards HLP-A from non-AP STA after successful authentication.
If the AP receives HLP-B from 3rd Party after dot11HLPWaitTime, the AP forwards it as a Data Frame.
STA
AP
Association Request
(dot11HLPWaitTime, HLP-A)
Association Response
3rd Party
Successful Key Confirmation
HLP-A
HLP-B
dot11HLPWaitTime
Beacon/Probe Resp.
(dot11HLPMaxWaitTime)
Authentication
HLP-B as Data Frame

## Slide 17: Examples
TGai draft should NOT define any IP specific protocols.
  Because it’s IETF business.
  It may cause consistency issues in the future.
But we should inform expected usage.
So some examples are shown in Annex part.

## Slide 18: Example Usage for DHCPv4 with RCO
STA
AP
Association Request
DHCPDISCOVER w/RCO
Association Response
DHCPACK w/RCO
DHCP
Server
DHCPDISCOVER w/RCO
DHCPACK w/RCO

## Slide 19: Example Usage for DHCPv4 without RCO
STA
AP
Association Request
DHCPDISCOVER
Association Response
DHCPOFFER
DHCP
Server
DHCPDISCOVER
DHCPOFFER
Data Frame
DHCPREQUEST
Data Frame
DHCPACK
DHCPREQUEST
DHCPACK

## Slide 20: Example Usage for IPv6 Stateless Configuration
STA
AP
Association Request
(RS)
Association Response
(RA)
Router
RA
Authentication
Authentication
RA
RS

## Slide 21: Example Usage for ARP/NDP
STA
AP
Association Request
Association Response
(Gratuitous ARP, NA)
Node (e.g. gateway, DNS server)
NS/NA
Authentication
Authentication
ARP

## Slide 22: Benefits of the Proposal
This proposal provides just container for higher layer. So it can be used by any higher layer protocols.
This proposal can support roaming within a local network without IP address change.
AP does not required to keep state of the STA’s IP address.
Easy co-extence with non-FILS AP/STAs.
It can be installed to existing network which uses DHCP without any changes in network.

## Slide 23: Issues of AP local IP address pool
IP address of the STA will be changed by roaming.
  STAs will be disconnected by roaming.
Separate IP address pools are required in AP and DHCP server for suppoting both FILS and non-FILS STAs.
  We implemented, refer 11-13/0323r
It’s bad idea to locate FILS specific IP address pool in AP.
FILS STA
AP
DHCP Server
non-FILS STA
IP address pool
for FILS STAs
IP address pool
for non-FILS STAs

## Slide 24: Translation or Pass through
Translation
  AP translates 11ai specific IEs from/to DHCP messages.
  AP must keep STAs’ DHCP state for DHCP renew.
Pass through
  AP decapsulates/encapsulates DHCP messages from/to HLP container.
  AP does not care DHCP state.
  DHCP renew is done by Data Frame as existing .11 network.
STA
AP
DHCP Server
11ai Specific IE
DHCP messages
STA
AP
DHCP Server
DHCP messages
in HLP container
DHCP messages

## Slide 25: Roaming Between FILS APs by Pass through model
FILS STA connects to FILS AP1 with FILS and gets IP address from the DHCP server.
When the STA is moving to FILS AP2, the STA can keep IP address according to DHCP and no need to request IP address as in existing IEEE802.11 network.
Following DHCP renew is done by Data Frames as existing network.
FILS
AP1
FILS
AP2
FILS
STA
DHCP
Server
Local Network
FILS
STA

## Slide 26: Roaming Between FILS APs by Translation model
FILS STA connects to FILS AP1 with FILS and gets IP address from the DHCP server.
When the STA is moving to FILS AP2,
  The STA requests IP address to AP2.
  Or AP1 tranfers DHCP state to AP2. How to do it?
FILS
AP1
FILS
AP2
FILS
STA
DHCP
Server
Local Network
FILS
STA
How to transfer DHCP state?

## Slide 27: Roaming from FILS AP to non-FILS AP by Pass through Model
FILS STA connects to FILS AP with FILS and gets IP address from the DHCP server.
When the STA is moving to non-FILS AP, the STA can keep IP address according to DHCP and no need to request IP address as in existing IEEE802.11 network.
Following DHCP renew is done by Data Frames as existing network.
FILS
AP
non-FILS
AP
FILS
STA
DHCP
Server
Local Network
FILS
STA

## Slide 28: Roaming from FILS AP to non-FILS AP by Translation Model
FILS STA connects to FILS AP with FILS and gets IP address from the DHCP server.
When the STA is moving to non-FILS AP,
  The STA requests IP address by DHCP.
  Or ome tricky implementations are required in APs, STAs and DHCP servers.
FILS
AP
non-FILS
AP
FILS
STA
DHCP
Server
Local Network
FILS
STA

## Slide 29: Roaming fron non-FILS AP to FILS AP by Pass through Model
FILS STA connects to non-FILS AP and gets IP address from the DHCP server.
When the STA is moving to FILS AP, the STA can keep IP address according to DHCP and no need to request IP address as in existing IEEE802.11 network.
Following DHCP renew is done by Data Frames as existing network.
non-FILS
AP
FILS
AP
FILS
STA
DHCP
Server
Local Network
FILS
STA

## Slide 30: Roaming fron non-FILS AP to FILS AP by Translation Model
FILS STA connects to non-FILS AP and gets IP address from the DHCP server.
When the STA is moving to FILS AP, the STA,
  STA requests IP address by 11ai specific IE.
  Or sycronize state between FILS AP and DHCP server.
non-FILS
AP
FILS
AP
FILS
STA
DHCP
Server
Local Network
FILS
STA
How to syncronize
state?

## Slide 31: Implementation
Pass through
  Always use DHCP client for IP layer configuration.
Translation
  Switch FILS IP address configuration and DHCP for supporting both FILS and non-FILS AP.

## Slide 32: Questions & Comments

## Slide 33: Straw Poll
Which HLS mechanism to be supported by TGai?
  Both
  11-13/0040r4 Generic HLP container
  11-13/0267r0 802.11ai specific IP address assignment
  Neither
Result:

## Slide 34: Motion
Move to include the text in 11-13/0040r4 into the TGai Draft Specification Document.
Moved:
Second:
Result (Y/N/A):

## Slide 35: Backup

## Slide 36: Aggressive Implementation
The specification of this proposal does not prohibit the aggressive implementation shown in next slides.
But we do not recommend such implementation because DHCP is fast enough.

## Slide 37: Aggressive AP Implementation for DHCPv4 with RCO
STA
AP
Association Request
DHCPDISCOVER w/RCO (v4)
Association Response
DHCPACK w/RCO (v4)
Gratuitous proxy ARP of the Router
DHCPv4
Server
ARP
Authentication
Authentication
Router
DHCPDISCOVERw/RCO
DHCPACK w/RCO
AS
Authentication
1. AP can know the STA’s MAC address. So the AP can issue DHCPDISCOVER message here for reduce the wait time.
2. AP confirms that the STA requests DHCPDISCOVER to forward.
3. AP inspected DHCPDISCOVER in 2. So the AP assumes DHCPACK will come and can trasmit Association Response immediately after receiving DHCPACK.