## Slide 1: Supplementary specifics of sensor use cases: traffic, lifetime and data responsiveness
Date: 2013-01-14
Author:

## Slide 2: Abstract
Supplementary specifics of 11ah usecases (1c, 1e/f, 1g) with battery operation are introduced, in order to facilitate defining the feature of enhanced power saving functions.
Sensor synchronization (with time-stamped data set) and quick event responsiveness are frequent requirements for every usecases including smart grid (1a) with no battery operation.
Traffic types classified in 11ah usecase document as “continuous, periodic, burst and event based” are numerically summarized.
  ~100ms/data to ~ 24hour/data and duty ratio of 0.0001% to 10%.
Typical battery life requirements are numerically summarized, based on the examples.
  About 10 years battery life is a common goal for various fixed sensors.
  A few years is minimal goal even for small stick-on (one time) sensors.

## Slide 3: Conclusion: Waking up period (sleep duration)
Continuous: ~100ms/data ( Tx period is equal to data sampling rate)
  No sleep time or short waking up period.
  Data may be lost if communication failed.
Periodic: 0.1sec ~ 30min ~ 24hour/data
  Data may be stored and queued at sensor side.
Burst: Usually based on query by host system or human intervention.
Average duty ratio of 0.0001% ~ 10% (near continuous).
  Data may be stored and structured at sensor side except for continuous sensor.
  Sometimes data are preprocessed or compressed, e.g. human data collection.
Event based: Data sensed on abnormal occurrences are always time critical.
  Secure and reliable transmission is required.
  Event based and periodic operation may be commonly combined in one sensor node.

## Slide 4: Conclusion: Battery life (operation w/o cell change)
Battery life requirement depends on each application and changes substantially according to slight changes of condition.
  For example, 1 month for a chilled red blood cell and 10years for RBC plasma.
10 years battery life may be a common goal for various fixed sensors.
  Maximum expectation spans 50-100years with energy harvesting in case of automated vineyard application, which is as same as lie time of grapevine.
A few years is minimal goal even for small stick-on (one time or temporal ) sensors using a button cell battery.

## Slide 5: Conclusion: Synchronization and responsiveness
Synchronization over sensors is essential for majority of applications.
  Accuracy of synchronization depends, relatively tight on vibration sensors in case of structural health monitoring, moderate at home healthcare application, and loose at automated vineyard.
Most tight synchronization are required in case of industrial control including smart grid (peak cut) application.
  Already presented in the crafting process of 11ah usecase document.
Responsiveness is important for event based applications.
  Time-critical alert or real time notification is required in hospital blood storage application and bridge/tunnel safety application.

## Slide 6: Supplemental examples

## Slide 7: Healthcare/Industrial monitoring ( 1e/f ) < example: Hospital storage rooms >
Industrial Monitoring includes;
  Process Monitoring, Control automation.
  Machine and operator Surveillance.
  Supply Chain Management, Asset Tracking and Storage Monitoring.
This type of application works based on both periodic and event driven notifications.
  Periodic data is used for monitoring temperature and humidity in the storage rooms.
  The data over or under a predefined threshold is meaningful to report.
Stored blood cannot be used if it is exposed to the wrong environment for about 30 minutes.
  Thus, event-driven data sensed on abnormal occurrences is time-critical and requires secure and reliable transmission.
Chilled RBC (red blood cell) storage has to be up to ~ 1 month, and 10 years for frozen RBC/Plasma.

## Slide 8: Civil structural health monitoring ( 1c/e/f ) < example: Bridge/Tunnel safety monitoring >
Emergency notification and historical record of stress
  Fire, fracture or collapse.
  Over-threshold vibrations, displacement or force.
  Water, rain or snow level, etc.
Mainly event based, but usually with periodic or burst as well
  Baseline monitoring with sensor synchronization (Periodic).
  Data retrieval (with pertaining time stamps) by human patrol (Burst).
Such kind of event based traffic is required to;
  have priority of information delivery.
  transmit in a highly reliable manner.
Short term diagnostic purpose requires up to 1 year monitoring, and up to 10 years monitoring for preventive maintenance.

## Slide 9: Home healthcare (1e/f/g) < example: Healthcare by tele-assistance >
Health and vital signals are monitored and transmitted to home appliance or gateway device for tele-assistance services.
  Support for the elderly.
  Diagnostics and guidance for care giving family of the ailing patient.
Data is gathered in both periodic and event driven fashion.
  Vital event data can be very time critical.
  Trend record has to be gathered by periodic data transfer.
Real time and reliability must be guaranteed depending on
  Vital event signal have to alert real time.
  Reliable data synchronization should be kept among sensors.
The diagnostic cycle time of chronic disease can be a few week to months, but battery life should be more than a few years.
    Battery change may not be expected by the ailing patient in rural area.

## Slide 10: Agricultural Monitoring (1c) < example: Automated vineyard >
Long term trend of sensing data are recorded to control spraying area by area in vineyard.
  temperature/humidity of atmosphere/soil
  climate including sun shine, precipitation and wind
Time synchronization among sensors is required.
  Periodic data set may be generated once every 30-60munites.
  Airflow and temperature/humidity have to be synchronized.
Long term system reliability or data continuity has to be kept.
Battery life time of sensors are expected to be
  5 years. (annual 20% increase of coverage or density without maintenance)
  Up to the lifetime of grapevine itself which is 50 to 100 years, same as humankind.
  Aero-vane or solar PV cell may assist for energy harvest.

## Slide 11: References
        [1] doc.: IEEE 802.11-11/0457r0
        “Potential Compromise for 802.11ah Use Case Document”
        [2] doc.: IEEE 802.11-11/0905r5
        “TGah Functional Requirements and Evaluation Methodology Rev. 5”
        [2] rfc6568
        “Design and Application Spaces for 6LowPAN”
        [3] rfc5673
        “Industrial Routing Requirements in Low-Power and Lossy Networks”
        [4] rfc5826
        “Home Automation Routing Requirements in LLN”
        [5] rfc5867
        “Building Automation Routing Requirements in LLN”