## Slide 1: SERVICE Field
Date: 2013-01-14
Authors:

## Slide 2
Authors continued:
Slide 2
Jan 2013

## Slide 3
Authors continued:

## Slide 4: Discussions
Different from 11ac, in 11ah ≥2MHz Long preamble in MU mode, SIGB CRC is inside SIGB itself.
This leaves 9 bits reserved in SERVICE field, if we keep using the 11a/n/ac 16-bit SERVICE field.
Now in 11ah there is very low rate modes like 1MHz MCS10, in which 9 unused bits waste more than one OFDM symbol.
Propose 11ah to use an 8-bit SERVICE field.
  First 7 bits are used as scrambler seed as in 11n.
  Remaining 1 bit reserved.

## Slide 5: Pre-Motion
Do you agree to add the following text into the spec framework
  11ah SERVICE field has 8 bits, in which first 7 bits are used for the scrambler seed, and the remaining 1 bit reserved.

## Slide 6: Motion
Move to add the following text into the spec framework
  11ah SERVICE field has 8 bits, in which first 7 bits are used for the scrambler seed, and the remaining 1 bit reserved.