## Slide 1: Enabling AP Sleep
Date: 2013-01-14
Authors:
January 2013

## Slide 2
January 2013

## Slide 3
January 2013

## Slide 4: Introduction
We want to define a protocol for enabling doze time for an AP
There are several use cases where allowing AP sleep is beneficial
  Battery operated Relays:
    A Relay is an entity constituting of a STA and an AP [1]
    Enabling battery powered relays required to define power save for AP
  Battery operated APs in sensor networks, e.g. mobile APs etc.
11ah already adopted scheduling mechanism that allow STAs/AP to agree on intervals of times where operations is permitted for a subset of STAs
  Restricted Access Window [2]
  Target Wake Time [3]
We propose a simple addition to those mechanisms (RAW/TWT), allowing AP to define intervals of time where it can go to Doze state
  And also allow STAs to sleep or perform STA-to-STA communications

## Slide 5: Proposal 1
AP can already setup RAW/TWT with STAs to indicate a time where preferred access is given to a certain group of STAs
      Currently, outside a RAW, any STA can access the medium
    We propose that outside those reserved times, STA operation with AP is not permitted and AP can go to sleep
      AP will still honor beacon transmission
      AP shall indicate a RAW for some other types of traffics (ex. Associating STAs)
Proposal: Define an indication from AP to signal that no transmission to AP (and from AP) is allowed except at times explicitly allocated to a RAW or TWT
  STA-STA transmissions may still be allowed
  Exception for AP to transmit the beacon

## Slide 6: Proposal 2
AP may not want/need to setup TWT/RAWs with all STAs
To enable sleep, AP just need to indicate a period of time where it will not be available for transmission/reception
  We propose to reuse the RAW setup to communicate this interval of time
Proposal: Define a signaling in RAW definition to indicate that for the duration of this RAW there cannot be transmission to AP (and from AP)
  STA-STA transmissions may still be allowed
  One bit indication in RAW is sufficient

## Slide 7: Example
Periodic RAW definition
  AP defines a Periodic RAW that is valid for a given interval of time
    e.g., indicated only per each long beacon period or in another persistent manner
With the proposed additions
  Proposal 1: Outside the periodic RAW, AP can sleep
  Proposal 2: Inside the periodic RAW, AP can sleep
TWT
time
LB
SB
SB
SB
SB
LB
PRAW
PRAW
PRAW
PRAW
PRAW
Min Awake
time
Sleep

## Slide 8: Conclusions
Currently, AP is supposed to be always in active state
There are several use cases where allowing AP sleep is beneficial
  Battery operated Relays:
    A Relay is an entity constituting of a STA and an AP [1]
    Enabling battery powered relays required to define power save for AP
  Battery operated APs in sensor networks, e.g. mobile APs etc.
To enable AP/relay to sleep we propose
  Indication from AP to signal that AP may be in doze state except for the times explicitly allocated by RAW/TWT
  Indicate that AP is in Doze state for the RAW duration

## Slide 9: Straw poll 1
Do you agree to define an indication from AP to signal that AP may be in doze state except for the times explicitly allocated by RAW/TWT?
  In this case, AP shall indicate a RAW for other types of traffic (ex. Association)

## Slide 10: Straw poll 2
Do you agree to define a signaling in RAW definition to indicate that AP is in Doze state for the RAW duration?

## Slide 11: References
[1] 11-12-1323-00-00ah-relay.pptx
[2] 11-12-0843-00-00ah-restricted-access-window-signaling-for-uplink-channel-access.pptx
[3] 11-12-0823-00-00ah-targetwaketime.pptx