## Slide 1: Client Positioning using Timing Measurements between Access Points
Date: 2013-01-15
Authors:

## Slide 2
Overview
Use cases
Overhead concern
Proposal for low overhead 802.11 based location
Clarifications in IEEE 802.11mc
Conclusion

## Slide 3: Use Cases - Few scenarios
Mall Scenario : User(s) receive coupon(s) for stores and they are trying to go from one store to another
  Typically there are multiple entry points to a Mall and it might take some time (order of 10’s of minutes) for a user to find his way to a store
  With users moving from one store to another in a mall, new users entering the mall, there could be hundreds of users trying to access the medium to get their location
Super Market : User trying to find his way to get to an item or to a facility in the store
Airport : User trying to get his way around a large airport
  A transcontinental aircraft can hold few hundred passengers
Stadium: Users locating their seats in a stadium

## Slide 4: Client to AP Timings Measurement Mechanism (Ref : 802.11 2012 Figure 10-23, 11-12-1249r2) Impact on System Throughput
Define K to be number of APs, K~=4, so that triangulation can be made (potentially there is a likely hood that K > 4 to ensure better location accuracy)
  This example assumes all the APs operate on the same channel. If the APs operate on different channels the absolute overhead remains the same but the overhead per channel becomes less
Frequency of Location Request = Freq
Singe Frame Exchange period = 160us (require 3 exchanges to make a single measurement)
  Ref : 802.11 2012 Figure 10-23 Timing Measurement Frame Exchange and 11-12-1249r2
  Minimum number of Frame Exchanges needed : 1) Request – ACK 2) M – ACK 3) M(t1,t4) – ACK
Number of clients per AP requesting Fine Timing Measurement = Clients_per_AP
Number of clients in the system trying to determine their location = Number_of_Clients
Impact on Throughput (Medium Occupancy time %) = 160us*3*K* Clients_per_AP*Freq
K = 4, Clients_per_AP = 100, Freq = Once per 5s, Impact on the throughput is : 160e-6*3*4*100/5s = 3.84% of Medium Time
K = 5, Clients_per_AP = 100, Freq = Once per 2s, Impact on the throughput is : 160e-6*3*5*100/2s = 12% of Medium Time
K = 5, Clients_per_AP = 300, Freq = Once per 2s, Impact on the throughput is : 160e-6*3*5*300/2s = 36% of Medium Time
Conclusion : System Throughput overhead = O(K * Number_of_Clients)

## Slide 5: Proposal to reduce overhead
APs provide Location information
  AP Geospatial location ANQP element already exists
APs perform round-trip-time (RTT) measurements with neighbors using the ‘Timing measurement procedure’ (TM)
  RTT is allowed between AP
Clients receive all TM packets and determine location
  Describe location determination calculation in IEEE 802.11 spec (clarification)
Optional scheduled TM mechanism between APs
  Reduces power consumption at clients

## Slide 6: AP’s Position
APs provide Location information
  AP Geospatial location ANQP (8.4.4.11) element already exists
The Location Configuration Information Report in the IEEE 802.11-2012 (8.4.2.24.10) specification already provides the AP’s lat/long/alt
AP location can also be provided through SUPL or higher layer protocol.

## Slide 7: Computation of client device location
By measuring the differential distance to multiple pairs of access points the client can now compute its location using the principles of hyperbolic navigation.
Generates a minimum of signaling overhead!
802.11 Timing measurement procedure
Access points engage in timing measurement procedures in a pair-wise manner with some regularity
APs broadcast their location
t1 = Time message M leaves AP 1
t4 = Time ACK from AP2 arrives at AP 1
Note: These are transmitted in message M2
t_c1 = Time message M from AP 1 reaches the client
t_c2 = Time the ACK from AP 2 reaches the client
D_12 = c*[ToF between AP1 and Client - ToF between AP2 and Client]
T = Time of flight between AP1 and AP2
  Known by client device from AP’s location
With c being the speed of light, the differential distance from the client to AP 1 and AP 2 can now be computed as:
D_12 = c*[(t_c1 – (t_c2 – ( t4 – t1 - T))]

## Slide 8: Hyperbolic Navigation – 2D example - Equations
Assume, for simplicity and without loss of generality that we have three APs located at (0,0), (0,b), and (c_x,c_y).
Assume the client device is located at (x,y)
We can then compute the location as detailed on the next slides

## Slide 9: Hyperbolic Navigation – 2D example - Equations
The basic differential distance equations:
Gives the following curves
,where
The desired location lies on the intersection of the two curves. (However, in general an additional AP may be required to uniquely determine the location).

## Slide 10: Hyperbolic Navigation – 2D example - Plot
y=gx+h
y=+-sqrt((e^2-1)*x^2+2edx+d^2)

## Slide 11: User Privacy
Regular client to AP RTT measurements allows the AP to calculate, or approximately calculate, the clients location
  Limited client privacy
The proposed method enables only the clients to calculate their location
  Privacy similar to GPS

## Slide 12: Changes to the specification
APs provide Location information
  AP Geospatial location ANQP element already exists
APs perform RTT measurement with neighbors
  RTT is allowed between AP, i.e. no change needed
Client receive TM packets and determine location
  Describe location determination calculation in IEEE 802.11 spec - Only clarification
Optional scheduled TM mechanism between APs
  Reduces power consumption at Client
  Not a required change
In summary: Very small or effectively no changes needed to specification!
Mostly some clarifications.

## Slide 13: Conclusions
A simple use of the existing timing measurement procedure to enable low overhead positioning of a large number of clients
APs perform timing measurement procedure between each others while clients listen to this communication and computes their location
  The system is scalable as the medium overhead is not affected by the number of clients (Number_of_Clients) performing their location measurements i.e., System Throughput overhead is lowered from O(K * Number_of_Clients) to O(K*Number_of_AP). Here :
      K = Number of Measurements needed to determine a single location
      Number_of_AP = The number of access points that are initiating the Timing Measurement (Potentially Number_of_AP can be 1 to service Number_of_Clients)
Location precision can possibly be improved as the method can allow (low overheads) for measurements to more APs as well as more frequent measurements
User privacy similar to GPS