## Slide 1: Implicit ACK for Relay
Date: 2013-01-14
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Background
TGah accepted the concept of sharing one TXOP for relay (for explicit ACK exchange) to reduce the number of channel contentions [1, 2].
RspFrm=11
Relay sends ACK, and set response frame bits to 11 for next outgoing frame
DATA
TD(V1)
TD(V2)
TA(V2)
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RspFrm=00
RspFrm=00
RspFrm=10
AP sends downlink DATA frame with response frame bits set to 00 to relay
After receipt of ACK, AP removes frame from buffer, and defers MAX_PPDU + ACK + 2*SIFS before next event
ACK
SIFS
TA(V1)
In SIFS time, relay sends DATA with a different MCS and response frame bits set to 00. Relay buffers frame until successful delivery or reaching of retry limit

## Slide 5: Proposed Scheme
To further improve MAC efficiency, we propose a single TXOP forwarding scheme without an ACK frame from Relay Station without increasing uncertainty.

## Slide 6: Proposed Scheme
The source station identifies if following packet is relay station’s forwarding packet by checking the SIG field of the following packet.
  9bit PAID subfield is defined for 2MHz SIG field.
  When a relay station forwards a received packet to a destination station, the destination station’s PAID shall be included in the PAID subfield.
  If the source station knows the destination station’s PAID, the source station can identify that following packet is relay station’s forwarding packet, by checking the PAID subfield of the following packet’s SIG field.
  Therefore, the source station can check its transmission success or not by checking SIG field of following packet only without decoding data payload part.

## Slide 7: Proposed Scheme
DL example
Relay sends DATA with a different MCS, and sets response frame bits to 00, and sets PAID subfield to that of the STA
DATA
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RspFrm=11
RspFrm=00
RspFrm=10
AP sends downlink DATA frame with response frame bits set to 11, so that other STAs can expect another DATA frame will follow
Within SIFS time, AP receives a PHY SIG field with response frame bits set to 00, and checks PAID subfield in PHY SIG field

## Slide 8: Proposed Scheme
UL example
Within SIFS time, STA receives a PHY SIG field with response frame bits set to 00, and checks PAID subfield in PHY SIG field
Relay sends DATA with a different MCS, and sets response frame bits to 00, and sets PAID subfield to that of the AP
DATA
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RspFrm=11
RspFrm=00
RspFrm=10
STA sends uplink DATA frame with response frame bits set to 11, so that other STAs can expect another DATA frame will follow

## Slide 9: Requirements
An AP needs to know PAID of STAs belong to the relay station for downlink transmission.
  Relay station needs to indicate a STA’s PAID to the root AP, when the STA is associated or the STA’s AID is changed.
A STA associated with a relay station needs to know PAID of the root AP for uplink transmission.
  Relay station needs to indicate associated STAs BSSID of the root AP.
  Current SFD already includes similar feature for R-AP:
    R-AP is able to indicate it is a R-AP (1 bit or indicate root-AP address/SSID in beacon, TBD)

## Slide 10: Straw Polls
SP1
  Do you support the concept of sharing one TXOP for relay with implicit ACK, where PAID in SIG field is used for ACK purpose as shown in slide 6?
SP2
  Do you support that relay station indicates an associated STA’s PAID to root AP when the STA becomes associated or the STA’s AID is changed, and indicates the BSSID of the root AP to newly associated STAs?
    And the BSSID of the root AP can be indicated in beacon frame.

## Slide 11: References
[1] IEEE 802.11-11/1137r12 Proposed Specification Framework for TGah
[2] IEEE 802.11-12/1330r0 Two-hop relay function