## Slide 1: TWT Grouping and Assignment for Z-Class STAs
Date: 2013-01-14
Authors:

## Slide 4: Motivation on TWT Grouping and Assignment
Proposition for a need of mechanism in order to spread out Z-class clients [1]
  AP control of wake times
  Propose:
    Requested Wake Time
    Target Wake Time
Proposition for exchange of TWTs during Association – always initiated by client [1]
  Can also be sent in MGMT Action frame to update during association
  Can send more than one IE, e.g. one for each direction, accommodates multiple phases and periods
Scheduling TWTs in groups may reduce signaling overhead
  Restricted TWT intervals of Z-class clients require signaling to TIM STAs in short and long beacons
  Discrete TWTs from clients within beacon intervals need increased signaling overhead when compared to clients grouped in TWT intervals

## Slide 5: TWT Grouping
Propose to introduce non-overlapping (pre-defined) TWT intervals (groups) for Z-class STAs
  Requested Wake Time from STAs are assigned to TWT intervals
  Each group is not an exact multiple or sub-multiple of other intervals
TWTs are periodic and protected from RAW durations accessed by TIM STAs
Each TWT interval (group) may support TWTs of multiple STAs
Without TWT group
With TWT group
Grouped into TWT interval

## Slide 6: Signaling of TWT Groups to Z-Class STAs
We propose that AP provides two parameters to each TWT group:
  TWT Group ID
  Zero phase offset value: Initial value of the group of TWTs with offset = 0; for example, 20 ms for TWT Group ID = 1 or 30 ms for TWT Group ID =2.
These parameters are conveyed to associated STAs to inform about their TWT Group
An illustration of our proposal is as below:
TWT Group ID = 1
TWT Group ID = 2
TWT Group ID = 3
TWT Group ID = N
Zero Phase Offset
of TWT Group 1
Zero Phase Offset
of TWT Group 2
TWT Group
20 ms
30 ms
40 ms

## Slide 7: Summary
We proposed to include TWT groups to support multiple non-TIM STAs within each TWT interval
  Reduced signaling overhead when compared to ungrouped discrete TWTs

## Slide 8: References
[1] Target Wake Time, July 2012, doc. IEEE 802.11-12/0823r0

## Slide 9: Straw Poll 1
Do you agree that the AP can assign a TWT Group ID and provide a zero phase offset TWT value to each group?