## Slide 1: Supplementary specifics of sensor usecases for defining the enhanced power saving feature
Date: 2013-01-15
Author:

## Slide 2: Abstract
We propose additional classifiers as a supplement to the 802.11ah use cases in order to clarify the power saving features in 802.11ah.
The supplemented classifier are essential to specify the 11ah use cases (1c, 1e/f, 1g) where battery operation are introduced, in order to facilitate defining the feature of enhanced power saving functions.
The additional classifiers include
  Data traffic types (duty cycle)
  Typical battery life requirements.
  Sensor collaboration, such as synchronization

## Slide 3: Proposed Classifier
# | Category | Comment (example)
1 | Location | Outdoor, indoor
2 | Environment type | Urban, sub-urban, rural
3 | STA/AP communication | 2-way (meter data & control)
4 | Data rate | 100 kbps ~3MHz
5 | BER/PER requirement | PER<10%
6 | Mobility | Stationary
7 | Traffic type (responsiveness) | Continuous/periodic/burst (Time-critical event)
 | wake up period (duty cycle) | 30min ~ 24hour (0.0001% ~ 10%)
8 | Battery life requirement | 1 month ~ 10years
9 | Sensor collaboration | Tight/Moderate/Loose/No synchronization
10 | Security requirement | High/Moderate
11 | Reliability | High/Moderate
12 | STA/AP capacity | STA (outdoor): 6000 , :AP: 1
13 | STA/AP category | STA: fixed (outdoor/indoor), AP: fixed (outdoor)
14 | STA/AP elevation | STA: 1m,..,10m , AP: 2m,..,30m
15 | Actors | Meter device (power, gas, water)

## Slide 4: Classifier: Traffic type (duty cycle)
Continuous: ~100ms/data ( Tx period is equal to data sampling rate)
  No sleep time or short waking up period.
  Data may be lost if communication failed.
Periodic: 0.1sec ~ 30min ~ 24hour/data
  Data may be stored and queued at sensor side.
Burst: Usually based on query by host system or human intervention.
Average duty ratio of 0.0001% ~ 10% (near continuous).
  Data may be stored and structured at sensor side except for continuous sensor.
  Sometimes data are preprocessed or compressed, e.g. human data collection.
Event based: Data sensed on abnormal occurrences are always time critical.
  Secure and reliable transmission is required.
  Event based and periodic operation may be commonly combined in one sensor node.

## Slide 5: Classifier: Battery life
Battery life indication (month, year, decade)
Battery life requirement depends on each application and changes substantially according to slight changes of condition.
  For example, 1 month for a chilled red blood cell and 10years for RBC plasma.
10 years battery life may be a common goal for various fixed sensors.
  Maximum expectation spans 50-100years with energy harvesting in case of automated vineyard application, which is as same as life time of grapevine.
A few years is minimal goal even for small stick-on (one time or temporal ) sensors using a button cell battery.

## Slide 6: Classifier: Collaboration
Indication of collaboration level among sensors (no synchronization, loose synchronization, tight collaboration)
Collaboration such as synchronization among sensors is essential for majority of applications.
  Accuracy of synchronization depends, relatively tight on vibration sensors in case of structural health monitoring, moderate at home healthcare application, and loose at automated vineyard.
Most tight synchronization is required in case of industrial control including smart grid (peak cut) application.
  Already presented in the crafting process of 11ah usecase document.
Responsiveness is important for event based applications.
  Time-critical alert or real time notification is required in hospital blood storage application and bridge/tunnel safety application.

## Slide 7: Supplementary examples

## Slide 8: Healthcare/Industrial monitoring ( 1e/f ) < example: Hospital storage rooms >
Industrial Monitoring includes;
  Process Monitoring, Control automation.
  Machine and operator Surveillance.
  Supply Chain Management, Asset Tracking and Storage Monitoring.
This type of application works based on both periodic and event driven notifications.
  Periodic data is used for monitoring temperature and humidity in the storage rooms.
  The data over or under a predefined threshold is meaningful to report.
Stored blood cannot be used if it is exposed to the wrong environment for about 30 minutes.
  Thus, event-driven data sensed on abnormal occurrences is time-critical and requires secure and reliable transmission.
Chilled RBC (red blood cell) storage has to be up to ~ 1 month, and 10 years for frozen RBC/Plasma.

## Slide 9: Civil structural health monitoring ( 1c/e/f ) < example: Bridge/Tunnel safety monitoring >
Emergency notification and historical record of stress
  Fire, fracture or collapse.
  Over-threshold vibrations, displacement or force.
  Water, rain or snow level, etc.
Mainly event based, but usually with periodic or burst as well
  Baseline monitoring with sensor synchronization (Periodic).
  Data retrieval (with pertaining time stamps) by human patrol (Burst).
Such kind of event based traffic is required to;
  have priority of information delivery.
  transmit in a highly reliable manner.
Short term diagnostic purpose requires up to 1 year monitoring, and up to 10 years monitoring for preventive maintenance.

## Slide 10: Home healthcare (1e/f/g) < example: Healthcare by tele-assistance >
Health and vital signals are monitored and transmitted to home appliance or gateway device for tele-assistance services.
  Support for the elderly.
  Diagnostics and guidance for care giving family of the ailing patient.
Data is gathered in both periodic and event driven fashion.
  Vital event data can be very time critical.
  Trend record has to be gathered by periodic data transfer.
Real time and reliability must be guaranteed depending on
  Vital event signal have to alert real time.
  Reliable data synchronization should be kept among sensors.
The diagnostic cycle time of chronic disease can be a few week to months, but battery life should be more than a few years.
    Battery change may not be expected by the ailing patient in rural area.

## Slide 11: Agricultural Monitoring (1c) < example: Automated vineyard >
Long term trend of sensing data are recorded to control spraying area by area in vineyard.
  temperature/humidity of atmosphere/soil
  climate including sun shine, precipitation and wind
Time synchronization among sensors is required.
  Periodic data set may be generated once every 30-60munites.
  Airflow and temperature/humidity have to be synchronized.
Long term system reliability or data continuity has to be kept.
Battery life time of sensors are expected to be
  5 years. (annual 20% increase of coverage or density without maintenance)
  Up to the lifetime of grapevine itself which is 50 to 100 years, same as humankind.
  Aero-vane or solar PV cell may assist for energy harvest.

## Slide 12: Smart Grid (1c) < example: Demand Response >
Peak shaving of total consuming power by DR (demand response) scheme is a typical application of smart grid.
  In order to perform statistically proper control of each appliance, data from sufficiently large number of power meters have to be collected without omission, every control response period.
  In slow (usual) DR, control response for peak shaving may have a minute of lead time, and in case of fast DR, same lead time can be seconds, e.g. 4 seconds.
Time synchronization is key aspect for DR both power control and prediction (EI) by measurement.
  Time definition may follow ISO 8601 of which resolution is usually a second but can be a millisecond.
DR signaling includes, emergency event, reliability event, etc.
Smart grid DR system have to provide no long battery operation.
  However, an appropriate period of battery operation should be required for black out.

## Slide 13
Straw poll
Do you agree that IEEE802.11ah Task Group considers the proposed supplementary classifiers in slide 4 to 6 for defining enhanced power saving function?
  Yes:
  No:
  Abstain:

## Slide 14: References
        [1] doc.: IEEE 802.11-11/0457r0
        “Potential Compromise for 802.11ah Use Case Document”
        [2] doc.: IEEE 802.11-11/0905r5
        “TGah Functional Requirements and Evaluation Methodology Rev. 5”
        [2] rfc6568
        “Design and Application Spaces for 6LowPAN”
        [3] rfc5673
        “Industrial Routing Requirements in Low-Power and Lossy Networks”
        [4] rfc5826
        “Home Automation Routing Requirements in LLN”
        [5] rfc5867
        “Building Automation Routing Requirements in LLN”
        [6] OpenADR 2.0a specification.