## Slide 1: 802.11mc HEMM
Date: 2013-01
Authors:

## Slide 2: Abstract
This document contains a discussion and proposals relating to CID148
What is HEMM anyway? What does "HCCA, EDCA mixed mode" mean? Which elements of HCCA and EDCA are used in HEMM?

## Slide 3: HEMM
Defined as “HCCA, EDCA Mixed Mode”
Appears only 6 times in 11e but a lot more in 802.11-1012
2 Major places in Specification:
  Table 8-5 TID
    8-15 is used for HCCA
    8-15 is also used for HEMM
    (So no way to differentiate)
  Access Policy in TS Info Field
    11 = HEMM
    01 = HCCA
    THIS IS THE ONLY DIFFERENTIATION IN THE SPEC

## Slide 4: HEMM
TS Operation 10.4.1
  Access Policy “to modify the HC’s scheduling behavior”.
  A TSPEC request may be set so that both HCCA and EDCA mechanisms (HEMM) are used.”
  Q. How does a TSPEC specify both HCCA and EDCA mechanisms?
  ANS. By setting Access Policy to 11.
  Q. How can a TSPEC refer to both EDCA and HCCA?
  ANS. Only if a TSPEC is a combined one. Is this possible?

## Slide 5: HEMM – Last Para 9.19.3.5.1 Edited by me for clarity
“HCF contention-based channel access shall not be used to transmit MSDUs belonging to an established TS (with the HC’s acceptance of the associated TSPEC), unless:
the granted TSPEC indicates it is permitted to do so when the Access Policy subfield of the TS Info field is equal to “HCCA, EDCA mixed mode” (HEMM),
the polled STA utilized the full TXOP provided by the HC, and it has more MPDUs to send. “
Discussion on this:
If there is a HCCA time slot allocated then the MSDUs must use it – that seems reasonable
BUT it stipulates that an TS cannot transmit using EDCA at all if the TSPEC is for HCCA.
If TSPEC is for HEMM then TS can use EDCA for any ‘surplus’ packets but only if time slot is totally used up.
So, if TSPEC is HEMM, then excess packets can be sent using EDCA
If TSPEC is HCCA, then excess packets can not be sent using EDCA.
This raises the question of EDCA Admission Control and if the AC has ACM bit set.

## Slide 6: HEMM – Last Para 9.19.3.5.1
“When this QSTA sends frames belonging to a TS using contention-based channel access, it shall encode the TID field in the QoS Data frame with the TID associated with the TS. “
OK, no problem here, irrespective of HEMMS
When the QAP grants a TSPEC with Access Policy subfield set to HEMM and if the corresponding AC needs admission control, the QAP shall include the Medium Time that specifies the granted time for EDCA access in the ADDTS response frame.”
So, EVEN IF ACM BIT NOT SET, the AP still returns a “Medium Time” for HEMM.
Two questions:
What is value of the Medium time? It is only for “excess traffic” so no real way of knowing what it required. The fall back would be to return a Medium Time equal to the values used in the TSPEC but his would be inefficient.
If no ACM bit set, does this violate any rule about responding Medium Time when not required?

## Slide 7: So what is HEMMS?
HEMMS is identified in a TSPEC by setting the Access Policy to 11. The TID is set same as HCCA.
HEMMS is set in the TSPEC so that the STA can send surplus packets outside the time slot.
A HEMMS TSPEC response includes Medium Time, so it allows the TS to use an AC that has ACM set.
My Question is “Do we need HEMM in addition to HCCA, or should we allow HCCA similar access to EDCA?”

## Slide 8: Keep HEMMS?
So HEMMS seems to be a way to protect an AC with ACM if there are surplus packets.
When does this problem arise and is it a big enough problem?
Problem arises if traffic exceeds the Time Slot allocation
  How often? How much?
More likely to be a problem for Video (VBR) and not a problem for voice or audio (CBR) unless the medium gets blocked.
As the medium is always possible to be blocked, one could argue that HCCA should never be used, and only HEMM makes any sense. If so, why have two schemes?
I personally cannot see any need for both schemes as HEMM has the back up that would be silly to not have.

## Slide 9: If we keep HCCA and HEMMS
Need to clarify how the Medium Time is calculated and to make clear if required if no AC has ACM bit set.
  Annex N could cover this
  What should the value of the Medium Time be? A proportion, the full amount? Even if one time slot is blocked, as Medium Time is calculated over a 1 second period, still not easy to work out what proportion it should be. Also it should be small as only used if the TSPEC ‘got it wrong”. (Would this really effect the admission policy calculation – NO)
  Should the STA be encouraged to modify its TSPEC if it finds itself having significant “excess” packets? No need if HEMM.
  SO why use HCCA ever, if HEMM provides this safe haven?
  why have two schemes?
  Is the only real reason to keep both is so that the term “HEMM” can be used (If HCCA did not exist, the “H” cannot be used)

## Slide 10: Just have HCCA
Simply allow HCCA to spill over into EDCA in the case that there are surplus packets.
We have argued that there is no practical reason why any TSPEC would restrict itself to HCCA only and the safe path is always to set HEMM as the Access Policy.
Questions
Do we still need a Medium Time in the ADDTS Response?
  NO If ACM bit set, simply allow excess packets to use AC on the assumption that this is a rare event. Remember TSPECs are pessimistic. Also if ACM not set, no problem, not needed.
  YES Have a Medium Time so that STA can test its Used Time and Admission Control works What if no ACM bit set? Only return if ACM set, but then it goes in circles (why sending a TSPEC asking for Medium Time?)

## Slide 11: Proposal (the Keep it Simple version)
Rewrite the last para of 9.19.3.5 as follows:
“MSDUs belonging to an established TS (with the HC’s acceptance of the associated TSPEC), must use the TXOP provided by the HC. If, and only if the polled STA has utilized the full TXOP provided by the HC, and it has more MPDUs to send, then it may transmit those MPDUs using contention-based channel access, including the case when the corresponding access category has the ACM bit set. When this QSTA sends frames belonging to a TS using contention-based channel access, it shall encode the TID field in the QoS Data frame with the TID associated with the TS. The QSTA should consider modifying the associated TSPEC if it needs to send MSDUs belonging to an established TS on a regular basis using contention based channel access.”
Q. Do we need the last sentence?

## Slide 12: HEMM – would we miss it?
In my opinion, no one would miss it.
Proposal
Remove all references to HEMM in the Standard
Rewrite final paragraph of 9.19.3.5.1 as indicated.