## Slide 1: Signal to Noise+Interference (SNIR) Variations on multiple TVWS channels
January15, 2013
Authors:
UPDATE: This contribution contains additional simulation results for 10dB SNIR difference on 2 accessed TV channels, one an adjacent channel, the other a non adjacent channel. The simulations also address an intermediate case with a 4dB SNR difference due to lower TX power.

## Slide 2: Simulation Overview
Main goal:
  Compare 2 channel MAC layer throughputs using 2 cases:
    MAC layer channel aggregation using one interleaver on each channel and independent MCS selection based on each channel SNIR
    PHY layer bonding using a single interleaver for both channels and a common MCS on bonded channels (11af baseline)
Simulation assumptions
  Rms Delay Spread: 100ns
  Two-channel operation
  Packet length
    1000 bytes for PHY bonding (Case B) over 2 channels
    500 bytes for MAC layer aggregation (Case A) on each channel
  Same noise level on both channels
  Different transmit power on two channels
    P_Tx1 = 40mw (adjacent) P_Tx2 = 100mw (non-adjacent)
  GI = 6 µs
  Target PER: 10% --MCS adaptation threshold for BOTH cases

## Slide 3: Consider Two Cases
Case A: MAC layer aggregation
  Each channel has independent MCS
  One interleaver on one channel
  MCS selection on each channel follows Table 23-19 of 802.11af specs
Case B: 802.11af- PHY layer bonding
  One interleaver over two channels
  Same MCS for two aggregated channels
    One encoder and same modulation modes
  MCS selection on two aggregated channel follows Table 23-23 of 802.11af specs

## Slide 4: Simulation Results - PER Performances of one channel(CaseA)
Fig.1 PER vs. SNR for a single 6MHz TVWS channel

## Slide 5: Simulation Results - PER Performances of two-bonded- channel (Case B)
Fig.2 PER vs. (S1+S2)/2N0, where S1 and S2 are transmit power for channel 1 and channel 2 respectively, N0 is the noise level on each channel, S2 = 2.5S1 (TxPower Difference on two channels = 4dB)
Fig.3 PER vs. (S1+S2)/2N0, where S1 and S2 are transmit power for channel 1 and channel 2 respectively, N0 is the noise level on each channel, transmit power on channel2 is 2.5 times of transmit power on channel1, i.e., S2 = 2.5S1 and interference on channel 1 is 5dB higher than the noise level and no interference on channel 2.

## Slide 6: Simulation Results- Received SNIRs and MCS’s for 4dB Tx Power Difference
Chart: Fig.4 CaseA: SNIRs and MCS's on two channels for TxPowDiff=4dB and no interference on both channels (MCS mapping is based on Fig. 1 on Slide 4) - InterDigital
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
SINR for Channel N+1 | 42.721 | 41.272 | 39.95 | 38.733 | 37.607 | 36.558 | 35.577 | 33.787 | 30.736 | 28.197 | 26.022 | 24.119 | 22.429 | 20.907 | 19.525 | 18.257 | 17.087 | 16.001 | 14.987 | 14.037 | 13.143 | 12.298 | 11.498 | 10.738 | 10.014 | 9.3227 | 8.6617 | 8.0283 | 7.4202
SINR for Channel N+4 | 46.721 | 45.272 | 43.95 | 42.733 | 41.607 | 40.558 | 39.577 | 37.787 | 34.736 | 32.197 | 30.022 | 28.119 | 26.429 | 24.907 | 23.525 | 22.257 | 21.087 | 20.001 | 18.987 | 18.037 | 17.143 | 16.298 | 15.498 | 14.738 | 14.014 | 13.323 | 12.662 | 12.028 | 11.42
MCS for Channel N+1 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6 | 5 | 4 | 4 | 3 | 3 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
MCS for Channel N+4 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6 | 5 | 5 | 4 | 4 | 3 | 3 | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 1 | 1 | 1
Chart: Fig. 5 Case B: SNIR and MCS of two-bonded channel for TxPower Diff = 4dB and No Interference on CH N+1 (MCS mapping is based on Fig. 2 on Slide 5) – PHY layer bonding
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
SNR/SINR on Two-bonded-channel | 45.166 | 43.718 | 42.395 | 41.178 | 40.052 | 39.003 | 38.022 | 36.232 | 33.182 | 30.642 | 28.467 | 26.565 | 24.874 | 23.353 | 21.97 | 20.702 | 19.533 | 18.446 | 17.433 | 16.482 | 15.588 | 14.743 | 13.943 | 13.183 | 12.459 | 11.768 | 11.107 | 10.473 | 9.8653
MCS for two-bonded channel | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6 | 6 | 5 | 4 | 4 | 3 | 3 | 3 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 7: Simulation Results - Throughput Comparison between MAC layer aggregation and PHY bonding with single interleaver and a common MCS
Fig.6 MAC layer throughput comparison between Independent MCS selection (MAC layer aggregation) and PHY layer bonding with single interleaver and a common MCS
Fig.7 Throughput Gain of Independent MCS selection (MAC layer aggregation) over PHY layer bonding with a common MCS
SNR difference between two channels = 4dB
Chart: Tput Performance vs. Distance for TxPower Diff = 4dB and No Interference on CH N+1
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
Tput for MAC layer aggregation | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 13.371 | 13.038 | 12.25 | 11.239 | 10.93 | 9.9495 | 9.1657 | 8.932 | 8.0054 | 7.2995 | 6.5595 | 6.4685 | 6.3533 | 5.6688 | 5.5618 | 4.8653 | 3.8693 | 3.8357 | 3.7948 | 3.7481
Tput for PHY layer bonding | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 13.578 | 13.211 | 12.494 | 12.144 | 10.835 | 10.425 | 8.7193 | 8.657 | 8.5276 | 8.3399 | 8.1041 | 6.6908 | 5.3244 | 5.2764 | 5.2456 | 5.1981 | 5.134 | 5.0628 | 4.9698 | 4.8499
Chart: Tput Gain vs. Distance for TxPower Diff = 4dB and No Interference on CH N+1
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
MAC layer Aggregation(Independent MCS Selection) over PHY Layer Bonding (Common MCS) | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.015245 | -0.013095 | -0.019529 | -0.074522 | 0.0087679 | -0.045612 | 0.051197 | 0.031766 | -0.061236 | -0.12475 | -0.19059 | -0.033225 | 0.19324 | 0.074369 | 0.060279 | -0.064023 | -0.24634 | -0.24238 | -0.23643 | -0.22718
Case A
Case B

## Slide 8: Simulation Results- Received SNIRs and MCS’s for 4dB Tx Power Difference and 5dB Interference Difference for 10dB SNIR difference
Chart: SNIR 8 Case A: SNIRs and MCS's on two channels for TxPowDiff=4dB and Interference to Noise Ratio on CH N+1=5dB (MCS mapping is based on Fig. 1 on Slide 4) - InterDigital
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
SINR on CH N+1 | 36.528 | 35.079 | 33.757 | 32.54 | 31.413 | 30.365 | 29.384 | 27.593 | 24.543 | 22.004 | 19.829 | 17.926 | 16.235 | 14.714 | 13.331 | 12.064 | 10.894 | 9.8079 | 8.7942 | 7.8439 | 6.9495 | 6.1048 | 5.3046 | 4.5444 | 3.8204 | 3.1294 | 2.4684 | 1.835 | 1.2269
SINR on CH N+4 | 46.721 | 45.272 | 43.95 | 42.733 | 41.607 | 40.558 | 39.577 | 37.787 | 34.736 | 32.197 | 30.022 | 28.119 | 26.429 | 24.907 | 23.525 | 22.257 | 21.087 | 20.001 | 18.987 | 18.037 | 17.143 | 16.298 | 15.498 | 14.738 | 14.014 | 13.323 | 12.662 | 12.028 | 11.42
MCS on CH N+1 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6 | 5 | 4 | 3 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
MCS on CH N+4 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 6 | 5 | 5 | 4 | 4 | 3 | 3 | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 1 | 1 | 1
Chart: SNIR 9 Case B: Combined SNIR/SNR and MCS for two-bonded-channel for TxPowDiff=4dB and Interference to Noise Ratio on CH N+1 = 5dB (MCS mapping is based on Fig.3 on Slide 5) – 802.11af
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
Combined SINR on Two-bonded Channel | 41.048 | 39.599 | 38.277 | 37.06 | 35.934 | 34.885 | 33.904 | 32.114 | 29.063 | 26.524 | 24.349 | 22.446 | 20.756 | 19.234 | 17.852 | 16.584 | 15.414 | 14.328 | 13.314 | 12.364 | 11.47 | 10.625 | 9.8249 | 9.0647 | 8.3407 | 7.6497 | 6.9887 | 6.3553 | 5.7472
Combined SNR on Two-bonded Channel | 45.166 | 43.718 | 42.395 | 41.178 | 40.052 | 39.003 | 38.022 | 36.232 | 33.182 | 30.642 | 28.467 | 26.565 | 24.874 | 23.353 | 21.97 | 20.702 | 19.533 | 18.446 | 17.433 | 16.482 | 15.588 | 14.743 | 13.943 | 13.183 | 12.459 | 11.768 | 11.107 | 10.473 | 9.8653
MCS for two-bonded-channel | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 5 | 4 | 2 | 2 | 2 | 2 | 3 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 9: Simulation Results - Throughput Comparison between MAC layer aggregation and PHY bonding with a single interleaver and a common MCS
SNR difference between two channels = 10dB
(TxPowDiff = 4dB, InterferenceDiff = 5dB)
Fig.7 MAC layer throughput comparison between Independent MCS selection (MAC layer aggregation) and PHY layer bonding with single interleaver and a common MCS
Fig.8 Throughput Gain of Independent MCS selection (MAC layer aggregation) over PHY layer bonding with a common MCS
Chart: Tput vs. Distance for TxPowDiff=4dB and Interference to Niose Ratio on CH N+1 = 5dB
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
Tput for MAC layer aggregation | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 14.011 | 13.543 | 13.301 | 12.955 | 12.068 | 11.158 | 10.39 | 9.9908 | 9.1492 | 8.3079 | 7.5618 | 7.3709 | 6.4945 | 5.4716 | 5.3758 | 5.2677 | 5.1306 | 4.4252 | 4.2947 | 3.5784 | 3.5088 | 3.4305 | 3.3441 | 3.2536
Tput for PHY layer bonding | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 14.346 | 13.172 | 12.567 | 10.75 | 7.2149 | 7.2149 | 7.0665 | 6.8533 | 7.7601 | 5.3244 | 5.2315 | 5.1529 | 5.0422 | 4.8986 | 2.8936 | 2.8406 | 2.7625 | 2.6747 | 2.5585 | 2.4181 | 2.2678 | 2.0863 | 1.8815
Chart: Tput Gain vs. Distance for TxPowDiff=4dB and Interference to Niose Ratio on CH N+1 = 5dB
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
MAC layer aggregation over PHY layer bonding | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.023351 | -0.055974 | 0.0097935 | 0.030875 | 0.1226 | 0.54652 | 0.44008 | 0.41383 | 0.33501 | 0.070592 | 0.42022 | 0.40895 | 0.26036 | 0.085161 | 0.097416 | 0.82047 | 0.80617 | 0.60188 | 0.60568 | 0.39863 | 0.45106 | 0.5127 | 0.60289 | 0.72926
Case A
Case B

## Slide 10: Weak Channel Throughput Contribution in MAC Layer Aggregation (Case A)
Chart: SNIR difference between two channels = 10dB
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
Weak Channel Contribution | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.48275 | 0.47332 | 0.45927 | 0.41951 | 0.37219 | 0.38864 | 0.38802 | 0.34533 | 0.30074 | 0.32537 | 0.32676 | 0.35953 | 0.2483 | 0.24731 | 0.24546 | 0.2429 | 0.26989 | 0.26374 | 0.29784 | 0.28802 | 0.27691 | 0.26467 | 0.25178
Chart: SNR difference between two channels = 4dB
| 50 | 55 | 60 | 65 | 70 | 75 | 80 | 90 | 110 | 130 | 150 | 170 | 190 | 210 | 230 | 250 | 270 | 290 | 310 | 330 | 350 | 370 | 390 | 410 | 430 | 450 | 470 | 490 | 510
Weak Channel Contribution | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.49999 | 0.47608 | 0.46269 | 0.4814 | 0.45603 | 0.45196 | 0.41611 | 0.44342 | 0.44441 | 0.48043 | 0.43654 | 0.38314 | 0.38555 | 0.38859 | 0.43006 | 0.43148 | 0.48357 | 0.35433 | 0.35329 | 0.35201 | 0.3505

## Slide 11: Discussions
In the high SNR range, MAC layer aggregation provides slightly lower throughput than PHY layer bonding
  The highest MCS is selected in both cases
  Higher overhead ratio of two packets generated for one transmission in MAC layer aggregation than one packet generated for two bonded channels in the PHY layer bonding case
For higher SNIR difference and larger distance, the throughput gain of MAC layer aggregation becomes evident
  Some gain drops at certain distances
    Quantization error on MCS selection
    PER curves of MCS2 and MCS3 are crossed over for the case that SNIR difference is 10dB (Fig.3)
Gain of MAC layer aggregation over PHY layer bonding
SNR Difference | Maximum Gain | Average Gain (110 to 510m)
4 dB | 19% | -5.7%
10dB | 82% | 42%

## Slide 12: Summary
Highly variable SNIR levels on aggregated TVWS channels:
  Different transmit power limits on adjacent/nonadjacent TVWS channels
  High interference levels on on DTV adjacent channels from DTV adjacent channel emissions.
Single MCS utilization for bonded channels leads to significant degradation and waste of spectrum
Independent MCS for multichannel permits efficient use of resources in real TVWS environments.
TGaf draft requires use of single MCS for multichannel and should be modified to add an option to permit effective multichannel operation using independent MCS selection.