## Slide 1: Higher Layer Setup Ad-hoc Summary
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
George Cherian | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | +1 858 651 6645 | gcherian@qti.qualcomm.com
Date: 2013-01-15
Authors:

## Slide 2: Abstract
This document is the summary of higher layer setup ad-hoc held on Tue. PM2.

## Slide 3: Problem Description
Draft 0.2, section 11.11.2.4 says:
  “The input ciphertext shall be the contents of the Association Response frame that follow the FILS Session element”
What does it mean?
  All vendor specific IEs will need to be encrypted
  All IEs added in the future will need to be encrypted

## Slide 4: Proposal
Define a new IE in Association Req/Resp that can be used to carry a set of TLVs (that include higher layer information, certificate etc.)
  Will need the ability to fragment this IE
  Will need the ability to encrypt this IE

## Slide 5: Container
Two types of containers: Encrypted & Plaintext container
  Encrypted container is used to carry higher layer information
  Plain text container is used to carry information like certificate
Container transports a sequence of TLVs
The container may be fragmented if the total number of octets of all TLVs is greater than the maximum that can be carried in a single IE

## Slide 6: Secure TLVs
Types (we have so far)
  HLP
    Carries ethernet frame that includes a higher layer packet such as DHCP packets (see 13/41r2)
  IP Address Assignment Req/Resp
    Carries the TGai defined elements to request/assign IP addresses (see 13/46r2)

## Slide 7: Plaintext TLV
Types (we have so far)
  Certificate

## Slide 8: Fragmentation
Several IEs with same element identifier will be sent in sequence carrying the fragments
The IE will include the fragmentation information

## Slide 9: Straw poll 1
Do you support to modify the encryption of Association Request/Response?
Result (Y/N/A):

## Slide 10: Straw poll 2
Do you support to create container IE for encryption and fragmentation?
Result (Y/N/A):