## Slide 1: 802.1Qbz–802.11ak Solutions: Unreliable Links
Date: 2013-01-16
Authors:

## Slide 2: Abstract
One of the problems described in Document 11/12-1441-01 (Finn) is the unreliability and variability of wireless links, and the complications this causes for networks incorporating them. The outline of a method for using heuristic algorithms to solve this problem is presented, including some requirements for those heuristics and a recognition of their limitations.

## Slide 3: Wireless links are dynamic
Wireless links can come up and go down frequently.
Wireless links can vary in speed over short time frames.
Stations can go to sleep for a while to conserve power.
Wireless stations can be mobile.
Bridges were invented to use wired connections that do none of the above.

## Slide 4: Link availability
You cannot have a bridge-to-bridge link flapping; frequent topology changes will keep the topology control protocols in turmoil, and disrupt connectivity throughout the network.
Bridge-to-end-station link flapping is a local matter, and causes no serious network problems.
Heuristics must be applied to prevent bridge-to-bridge link flapping—A flapping link is presented to the network as either:
  Always present, which causes frame loss if the outage lasts too long; or
  Always absent, which prevents the link from being used, and perhaps partitions what was intended to be one network.
  Pick your poison and drink heartily!

## Slide 5: Link speeds
Similarly, the network cannot be updated as link speeds change. A single speed should be chosen, and left alone, unless (perhaps) the heuristics indicate that it is stable in the long term.
All wireless links are represented to the network protocols as being very slow, so that the network will always prefer wired links, where connectivity permits.

## Slide 6: Notes on heuristics
If an unreliable wireless link must be used to achieve connectivity, then connectivity is unreliable. This is a fact, no matter what bridging or routing technology is used.
The parameters controlling whether an unreliable link is considered up or down certainly will be managed objects; further study is required to find good default values, and to determine whether automatic algorithms can adjust them.

## Slide 7: References
This presentation is also available at: http://www.ieee802.org/1/files/public/docs2012/bz-nfinn-soln-unreliable-links-0113-v01.pdf
It attempts to answer one of the questions raised by: https://mentor.ieee.org/802.11/dcn/12/11-12-1441-01-00ak-issues-list-for-p802-1qbz-p802-11ak-point-to-point-model.pptx