## Slide 1: 802.1Qbz–802.11ak Solutions: Tagging
Date: 2013-01-16
Authors:

## Slide 2: Abstract
One of the problems described in Document 11/12-1441-01 (Finn) is that current standards for adding protocol tags to LLC media place an 802.11 Bridge / Access Point in a very difficult position. A means for solving this offered, which would mean a change to the 802.1Q rules for tagging frames.

## Slide 3: Quick problem statement
According to 802.1, all tags on LLC media are added by inserting a SNAP-encoded tag ahead of the existing LLC MSDU.
A VLAN tag, for example, adds 10 bytes to the frame (8-byte SNAP encoding + 2 byte payload).
Adding N tags to an LLC frame adds 6*N bytes of SNAP, compared to the Length/Type format. These extra bytes are bad for wireless media.
Furthermore, when bridging between LLC and Type/Length media, the bridge has to understand every possible tag, so that it can change the first Type/Length to LLC or SNAP, and change all succeeding SNAPs (except the one encoding the data [which one is that???]) to Length/Type.
This means that no new tags can be developed without revising all LLC/Type translating bridges.

## Slide 4: Once a SNAP, always an EtherType
We could change all documents, particularly 802.1Q, to say the following when adding a tag:
  If this is an LLC medium, convert the MSDU to Length/Type encoding, then add the LLC-encoded tag to the beginning of the frame.
  If the medium is not LLC, simply add the tag.
And when removing a tag:
  Remove the tag. If this is not an LLC medium, you are finished.
  If this is an LLC medium, convert the Length/Type encoded MSDU to LLC encoding.
On an 802.3-style medium, when adding a SNAP-encoded tag (non-0 OUI) to a Length-encoded (LLC) MSDU, the length field of the tag encompasses the entire frame. (A possible scenario – vendor-specific tags can be constructed in this manner.)

## Slide 5: Encapsulating long LLC frames
These rules raise, in theory, one issue that we may wish to address, but could ignore: it is currently not possible to carry an LLC non-SNAP frame over 802.3 if the frame is larger than 1535 bytes.
Two ways of fixing this:
  Define a new EtherType that means, “The next three bytes start an LLC frame”.
  Redefine the Length/Type field, saying, “A length of 1535 means that the frame is 1535 bytes or longer.”

## Slide 6: What this solution means
After the first LLC, all media are Length/Type encoded.
This certainly changes IEEE 802.1Q, and may change other documents.
If any Wi-Fi devices currently in use follow the rule used by 802.5 Token Ring media and defined now in 802.1Q-2011, and encode a VLAN tag over Wi-Fi as {AA-AA-03, 00-00-00, Tag EtherType, tag value, LLC, SNAP or data}, then we have a compatibility problem. A device expecting one format (this one or the one proposed) will be completely confused if it receives a frame in the other format.

## Slide 7: References
This presentation is also available at: http://www.ieee802.org/1/files/public/docs2012/bz-nfinn-soln-tagging-0113-v01.pdf
It attempts to answer one of the questions raised by: https://mentor.ieee.org/802.11/dcn/12/11-12-1441-01-00ak-issues-list-for-p802-1qbz-p802-11ak-point-to-point-model.pptx