## Slide 1: FILS Handling of Large Objects
Date: 2013-02-05
Authors:
Name | Company | Address | Phone | email
René Struik | Struik Security Consultancy | Toronto ON, Canada | USA: +1 (415) 690-7363 Toronto: +1 (647) 867-5658 Skype: rstruik | rstruik.ext@gmail.com

## Slide 2
Review Comments on 802.11ai – D0.2
Ref: 13/0036r09 (tgai-draft-review-combined-comments)
CID #242 (David Goodall, 13/0016r0):
Comment (8.4.2.184): An X.509v3 certificate may be longer than 253 bytes and therefore requires fragmentation across multiple elements. A certificate chain may require additional fragmentation.
Proposed change: 11ai will need to provide a mechanism for fragmenting certificates and certificate chains. It may be possible to adopt a mechanism from 11af etc.
Generalized Problem Statement
What to handle large objects that fit within a single frame?
How to fragment FILS frames, if these become too long due to large objects?

## Slide 3
Outline
Constructs from 802.11-2012
  Frame fragmentation/defragmentation
  Management frame body components
Protocol recap
  Certificate-based protocol
  Protocol including “piggy-backed info”
Application to FILS protocol
  Handling of large objects
  Handling of “foreign” objects (e.g., higher-layer “piggy-backed data” along key confirmation flows)

## Slide 4
Frame Fragmentation (802.11-2012)
Conceptual Channel
802.11 Channel w/Fragmentation
Notes:
Headers contain Sequence Control Field that indicates fragment# (4-bits) and sequence # (12-bits)
Originator (A) partitions frame body and sends individual segments in separate frames, in order
Recipient (B) reconstructs original (conceptual) frame from received segments, in order
When secure channel used, each segment is individually secured (by originator) or unsecured (by recipient)
Duplicate segments and segments received after time-out are acknowledged
802.11-2012 allows fragmentation/defragmentation with individually addressed MSDUs and MMPDUs
HDR
Body2
FCS
A
B
HDR1
Body1
FCS1
A
B
HDR3
Body3
FCS3
HDR2
Body2
FCS2
Body3
Body1
A
A
B
B

## Slide 5
Management Frame Body Components (802.11-2012)
Information Elements (8.4.2):
Named objects with format (Type, Length, Value), where
Type: Element-ID (1-octet field);
Length: Octet-length of Value field (1-octet field);
Value: Variable field.
Non-Information Elements (8.4.1):
Specified objects with tailored length and value attributes
Notes:
Information elements cannot have size larger than 255 octets, whereas non-information elements can.
With 802.11-2012, Authentication frames (8.3.3.11) are specified with field elements that are non-IEs, as is the case with some field elements specified with association request frames (8.3.3.5) and Association Response frames (8.3.3.6).

## Slide 6
Protocol Recap
Notes:
Our exposition is relative to certificate-based public-key protocol (i.e., without online
third party), but does leave out details not necessary for current discussion
A
Random X, Nonce NA
{NA, NB,[CertCA(IdA,QA), signA]}KEK2
Key Establishment
Key Confirmation
B
Random Y, Nonce NB
{NB, NA,[CertCA(IdB,QB), signB]}KEK2
STA
AP

## Slide 7
Protocol Recap w/ “Piggy-Backed Info”
Notes:
Key confirmation messages can become quite large, due to accumulation of
  certificates;
  Signature;
  “piggy-backed info”.
Certificate (chain) verification has to happen after completion of the key computation (thus, forcing
a serialized implementation (optionally carrying out computations between A and B in parallel).
A
Random X, Nonce NA
{NA, NB,[CertCA(IdA,QA), signA, TextA]}KEK2
Key Establishment
Key Confirmation
B
Random Y, Nonce NB
STA
AP
{NB, NA,[CertCA(IdB,QB), signB, TextB]}KEK2

## Slide 8
Suggested Protocol Flows
Notes:
Easy fragmentation/defragmentation of Authentication frames (since no 802.11-2012 frame protection);
Fragmentation on Association frames possible (since no 802.11-2012 frame protection of those frames);
All objects that do not fit restrictions of IEs can easily be represented as field elements (in 802.11-2012’s 8.4.1 sense).
Intra-frame fragmentation of higher-layer TLV objects (13/133r3) can be handled uniformly and aligned
with 802.11-2012 fragmentation/re-assembly Sequence Control Field approach (details in next version)
Further “ugly” optimization:
Partition certificate that “just does not fit” over 1rst/3rd flow, resp. 2nd/4th flow (thus, not increasing #flows)
A
Random X, Nonce NA,
{NA, NB,[CertCA(IdA,QA), signA, TextA]}KEK2
Key Establishment
Key Confirmation
B
Random Y, Nonce NB
STA
AP
{NB, NA,[CertCA(IdB,QB), signB, TextB]}KEK2
CertCA(IdA,QA)
CertCA(IdB,QB)