## Slide 1: FILS Handling of Large Objects
Date: 2013-03-19
Authors:
Name | Company | Address | Phone | email
René Struik | Struik Security Consultancy | Toronto ON, Canada | USA: +1 (415) 690-7363 Toronto: +1 (647) 867-5658 Skype: rstruik | rstruik.ext@gmail.com

## Slide 2
Review Comments on 802.11ai – D0.2
Ref: 13/0036r09 (tgai-draft-review-combined-comments)
CID #242 (David Goodall, 13/0016r0):
Comment (8.4.2.184): An X.509v3 certificate may be longer than 253 bytes and therefore requires fragmentation across multiple elements. A certificate chain may require additional fragmentation.
Proposed change: 11ai will need to provide a mechanism for fragmenting certificates and certificate chains. It may be possible to adopt a mechanism from 11af etc.
Generalized Problem Statement
How to handle large objects that fit within a single frame?
How to fragment FILS frames, if these become too long due to large objects?
Additional problem statement:
How to apply tricks to still avoid fragmentation if this would otherwise be required?
How to facilitate potential implementation of “aggressive scheme” modes?

## Slide 3
Outline
Constructs from 802.11-2012
  Frame fragmentation/defragmentation
  Management frame body components
Protocol recap
  Certificate-based protocol
  Protocol including “piggy-backed info”
Application to FILS protocol
  Handling of large objects
  Handling of “foreign” objects (e.g., higher-layer “piggy-backed data” along key confirmation flows)
  Facilitating “aggressive schemes”

## Slide 4
Frame Fragmentation (802.11-2012)
Conceptual Channel
802.11 Channel w/Fragmentation
Notes:
Header contains Sequence Control Field that indicates fragment# (4-bits) and sequence # (12-bits)
Originator (A) partitions frame body and sends individual segments in separate frames, in order
Recipient (B) reconstructs original (conceptual) frame from received segments, in order
When secure channel used, each segment is individually secured (by originator) or unsecured (by recipient)
Duplicate segments and segments received after time-out are acknowledged
802.11-2012 allows fragmentation/defragmentation with individually addressed MSDUs and MMPDUs
HDR
Body
FCS
A
B
HDR1
Body1
FCS1
A
B
Body3
FCS3
Body2
FCS2
A
A
B
B
HDR2
HDR3

## Slide 5
Management Frame Body Components (802.11-2012)
Information Elements (8.4.2):
Named objects with format (Type, Length, Value), where
Type: Element-ID (1-octet field);
Length: Octet-length of Value field (1-octet field);
Value: Variable field.
Fields that are not Information Elements (8.4.1):
Specified objects with tailored length and value attributes
Notes:
Information elements cannot have size larger than 255 octets, whereas non-information elements can.
With 802.11-2012, Authentication frames (8.3.3.11) are specified with field elements that are non-IEs, as is the case with some field elements specified with association request frames (8.3.3.5) and Association Response frames (8.3.3.6).

## Slide 6
Protocol Recap
Notes:
Our exposition is relative to certificate-based public-key protocol (i.e., without online
third party), but does leave out details not necessary for current discussion
A
Random X, Nonce NA
{NA, NB,[CertCA(IdA,QA), signA]}KEK2
Key Establishment
Key Confirmation
B
Random Y, Nonce NB
{NB, NA,[CertCA(IdB,QB), signB]}KEK2
STA
AP

## Slide 7
Protocol Recap with “Piggy-Backed Info”
Notes:
Key confirmation messages can become quite large, due to accumulation of
  certificates;
  signature;
  “piggy-backed info”.
Certificate (chain) verification has to happen after completion of the key computation (thus, forcing
a serialized implementation, rather than option to carry out computations between A and B in parallel).
Processing of “piggy-backed info” can only be initiated after receipt of STA’s key confirmation message
(thus, precluding optional implementation of “aggressive scheme” modes (see, 13/041r4, Slides 36-37).
A
Random X, Nonce NA
{NA, NB,[CertCA(IdA,QA), signA, TextA]}KEK2
Key Establishment
Key Confirmation
B
Random Y, Nonce NB
STA
AP
{NB, NA,[CertCA(IdB,QB), signB, TextB]}KEK2

## Slide 8
Suggested Protocol Flows
Notes:
Easy fragmentation/defragmentation of Authentication frames (since no 802.11-2012 frame protection);
Fragmentation on Association frames possible (since no 802.11-2012 frame protection of those frames);
All objects that do not fit restrictions of IEs can easily be represented as field elements (in 802.11-2012’s 8.4.1 sense).
Intra-frame fragmentation of higher-layer TLV objects (13/133r3) can be handled uniformly and aligned
with 802.11-2012 fragmentation/re-assembly Sequence Control Field approach (details in next slides)
Further “ugly” optimization:
Partition certificate that “just does not fit” over 1rst/3rd flow, resp. 2nd/4th flow (thus, not increasing #flows)
A
Random X, Nonce NA,
{NA, NB,[CertCA(IdA,QA), signA, TextA]}KEK2
Key Establishment
Key Confirmation
B
Random Y, Nonce NB
STA
AP
{NB, NA,[CertCA(IdB,QB), signB, TextB]}KEK2
CertCA(IdA,QA)
CertCA(IdB,QB)

## Slide 9
Foreign Objects (e.g., 13/133r3)
Conceptual Object
802.11 Representation as Sequence of Information Elements
Notes:
Header contains Sequence Control field that indicates end-segment ‘’ (1-bit) and length field (8-bits)
‘’ symbol only required if multiple objects in single frame or if single object spread over multiple frames
beyond scope of frame fragmentation
Originator object partitions object body into individual segments, in order
Recipient object reconstructs original (conceptual) object from received segments, in order
Reconstruction of partitioned object unique, independent of how the object was partitioned
Handling of multiple objects: Repr(Object1 || Object2 || …) ::= Repr(Object1) || Repr(Object2) || …
Body
HDR1
Body1
Body3
Body2
HDR2
HDR3
Type
Type
Type
IE1
IE2
IE3

## Slide 10
Securing Foreign Objects (1)
Conceptual Object
Securing this conceptual object (in key confirmation context)
802.11 Representation as Sequence of Information Elements
Notes:
Security of object (=confidentiality) determined by Object Type
Object Type and Header fields (length info) visible, also to parties without access to keying material
Consequences:
One cannot decide on case-by-case basis whether or not to encrypt object of specific object type
Object types to be encrypted need to be clustered (since Object Types in increasing order)
Never possible to encrypt “vendor-specific” information element (Type:=0xFF), even if, e.g., privacy info
Party who monitors traffic can “jump” over secured object and parse remaining (unsecured) IEs.
Body
HDR1
Body1
Body3
Body2
HDR2
HDR3
Type
Type
Type
Body
IE1
IE2
IE3

## Slide 11
Securing Foreign Objects (2) – Towards More Flexibility
Conceptual Object
Securing this conceptual object (in key confirmation context)
802.11 Representation as Sequence of Information Elements
Notes:
Security of object (=confidentiality) determined by Marker (2-octet IE)
No object info (except length) visible to parties without access to keying material
Consequence:
Flexibility as to which objects to encrypt on case-by-case basis
Possible to encrypt multiple objects with non-contiguous Object Types (just re-order after un-securing)
Any party who implements “Marker Element” can find, resp. “jump” over, secured object(s) string
Body
HDR1
Body1
Body3
Body2
HDR2
HDR3
Type
Type
Type
Body
IE1
IE2
IE3
“Marker”
IE0
Length
Marker
Object Length indicates total length of object segments (2-octet field)
Object Length
L
L

## Slide 12
Recommended Approach
Use existing frame fragmentation mechanism (802.11-2012) to handle frames that
would otherwise not “fit”
Represent “foreign objects” as described on previous slide (#2):
  Introduce new Information Element (IE) for “foreign object” type
  Introduce new Information Element (IE) as “Marker Element” (4-octets), so
  as to indicate length of encryption segment following
  Implement end-fragment ‘’ with “empty” foreign object (which acts as simple separator), so that foreign object segment’s HDR field reduces to simple 1-octet length field (i.e., segments now coincide with information elements (802.11-2012, 8.4.2))
Facilitate “aggressive scheme”, as follows:
  Allow inclusion of certificate info both in Authentication Request and Association Request (for STA), resp. Authentication Response and Association Response (for AP)
  Similar remark for “piggy-backed” info
  Note: Whether or not this “aggressive scheme” is exploited, is up to implementer.

## Slide 13
Straw Poll #1
Use existing frame fragmentation mechanism (802.11-2012) to handle frames that
would otherwise not “fit”.
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 14
Straw Poll #2
Represent “foreign objects” as described on previous slide (#2):
Introduce new Information Element (IE) for “foreign object” type
Introduce new Information Element (IE) as “Marker Element” (4-octets), so
as to indicate length of encryption segment following
Implement end-fragment ‘’ with “empty” foreign object (which acts as simple separator), so that foreign object segment’s HDR field reduces to simple 1-octet length field
(i.e., segments now coincide with information elements (802.11-2012, 8.4.2))
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 15
Straw Poll #3
Facilitate “aggressive scheme”, as follows:
Allow inclusion of certificate info both in Authentication Request and Association Request (for STA), resp. Authentication Response and Association Response (for AP)
Similar remark for “piggy-backed” info
Note: Whether or not this “aggressive scheme” is exploited, is up to implementer.
Yes
No
“Don’t Care”
Need more information
Result: