## Slide 1: 802.11 QoS Queue Architecture and Possible 802.1bz Bridge Model
Date: 2013-03-04
Authors:

## Slide 2: Abstract
This presentation describes
the structure of the QoS Queuing in the 802.11 AP and non-AP STA devices,
and a possible architecture model for 802.1bz bridge.

## Slide 3: 802.11 - QoS Specifications
EDCA (Enhanced Distributed Channel Access)
  High-priority traffic has a higher chance of being sent than low-priority traffic
  Contention window (CW) and arbitration inter-frame space (AIFS) determines the probability to gain the access to the medium
    CW and AIFS values are a function of the priority level.
  Transmit Opportunity (TXOP) is the bounded time interval during which the transmitter can send as many frames as possible
Wi-Fi Alliance’s WMM (Wi-Fi Multimedia) is a subset of 802.11 (EDCA, TxOP)

## Slide 4: 802.11 Access Categories
EDCA/WMM Medium Access does not guarantee QoS
QoS can be improved by Admission Control that limits admission and bandwidth utilization per Access Category

## Slide 5: Access Categories (AC)
EDCA levels of priority are called access categories (ACs).
ACs map directly from 802.1D-2004 user priority levels:
 | 802.1D-2004 |  | 802.11 (UP) |  | Wi-Fi WMM | 802.11aa-2012 w/ Alternate-EDCA activated | 
Priority | Priority Level | Designation | AC | Designation | WMM Priority | AC | Designation
lowest | 1 | BK | AC_BK | Background | Background | BK | Background
 | 2 | - | AC_BK | Background |  |  | 
 | 0 | BE | AC_BE | Best Effort | Best Effort | BE | Best Effort
 | 3 | EE | AC_BE | Best Effort |  |  | 
 | 4 | CL | AC_VI | Video | Video | A_VI | Video (Alternative)
 | 5 | VI | AC_VI | Video |  | VI | Video (Primary)
 | 6 | VO | AC_VO | Voice | Voice | VO | Voice (Primary)
highest | 7 | NC | AC_VO | Voice |  | A_VO | Voice (Alternative)

## Slide 6: 802.11 QoS Queue Architecture

## Slide 7: 802.11aa QoS Queues
  802.11aa introduces 2 additional queues for “alternate voice” and “alternate video”.

## Slide 8: Current Bridge & AP Queue Architecture

## Slide 9: BSS Bridging “Common” Queue Architecture
Note: For the clarity of the figure, optional Tx intermediate buffers within the wireless MAC, handling the deferred access to the medium and the Tx retransmission on failure to receive an ACK are not represented.

## Slide 10: 802.11 – 802.1Q Priority Levels
ACs priority level mapping differ from 802.1Q-2012 priority level mapping
 | 802.1D |  | 802.11 | WMM | 802.11aa |  | 802.1Q-2012 |  |  |  |  | 
Priority | Priority Level | Desig. | Access Category | WMM Priority | Access Category |  | Priority Level | Traffic type | 6 traffic types | 4 traffic types | with SR Class A & B | with SR Class B only
lowest | 1 | BK | AC_BK | Background | BK |  | 1 | BK | BK | BE | BE | BE
 | 2 | - | AC_BK |  |  |  | 0 | BE | BE |  |  | 
 | 0 | BE | AC_BE | Best Effort | BE |  | 2 | EE | CA | CA |  | CA
 | 3 | EE | AC_BE |  |  |  | 3 | CA |  |  |  | 
 | 4 | CL | AC_VI | Video | A_VI |  | 4 | VI | VO | VO | SR-B | NC
 | 5 | VI | AC_VI |  | VI |  | 5 | VO |  |  | NC | 
 | 6 | VO | AC_VO | Voice | VO |  | 6 | IC | IC | NC | SR-A | SR-B
highest | 7 | NC | AC_VO |  | A_VO |  | 7 | NC | NC |  | NC | NC

## Slide 11: 802.11 Portal
802.11-2012, Section 4.3.6: “Logical point at which MSDUs from an integrated non-IEEE 802.11 LAN enter the IEEE 802.11 DS.”
802.1Q-2012, Section 6.7.2: “A Bridge to an IEEE 802.11 LAN shall connect to an IEEE 802.11 Portal, which in turn connects to an IEEE 802.11 Distribution System. For the purposes of bridging, the service interface presented at the Portal is identical to the service interface presented at the IEEE 802.11 MAC SAP.

## Slide 12: 802.3 – 802.11 MAC Relay
802.11 to 802.11 MAC relay
802.11 to 802.3 MAC relay
802.3 to 802.3 MAC relay
802.3 to 802.11 MAC relay
802.11 MSDU
Rx Queue
802.11 Tx Queue Selection
802.11 MSDU
Tx Queue
802.1x Ctrl
Port Filtering
802.11 MSDU
Rx Queue
802.11  802.3
MSDU Translation
(“M_MA Portal”)
802.3 Tx Queue Selection
802.1x Ctrl
Port Filtering
802.3 MSDU
Tx Queue
802.3 MSDU
Rx Queue
802.3 Tx Queue Selection
802.3 MSDU
Tx Queue
802.3 MSDU
Rx Queue
802.11 Tx Queue Selection
802.11 MSDU
Tx Queue
Forwarding
[Priority Handling]
802.3  802.11
MSDU Translation
(“M_MA Portal”)
Forwarding
[Priority Handling]
Forwarding
[Priority Handling]
Forwarding
[Priority Handling]

## Slide 13: 802.1bz Bridge Data Plane Model

## Slide 14: 802.11 – 802.3 MAC Relay in 802.1bz Bridge

## Slide 15: 802.1bz Bridge Forwarding Process
MAC DA
MAC SA
VID
Priority
802.1Q clauses to be modified
MA / M Portal :
- 802.11 - 802.1Q
classification mapping
- 802 11 - 802.3 MSDU translation
802.1x Ctrl Port Filtering
Multicast Handling
- Multicast “Port”
management
- “Multicast Reflection”
prevention
802.11 AC Queue selection
802.11 [block] Ack / Retry
No 802.11 PCF or flow control
EDCA “Shaping”

## Slide 16: References
  [1] IEEE 802.11-2012
  http://standards.ieee.org/getieee802/download/802.11-2012.pdf
  [2] IEEE 802.1D-2004
  http://standards.ieee.org/getieee802/download/802.1D-2004.pdf
  [3] IEEE 802.11aa-2012
  http://standards.ieee.org/getieee802/download/802.11aa-2012.pdf
  [4] Wi-Fi WMM Specification v1.2
  www.wi-fi.org/knowledge-center/published-specifications