## Slide 1: TXOP Sharing Operation for Relay
Date: 2013-03-25
Authors:

## Slide 5: Outline
The concept of TXOP sharing for relay to minimize power consumption and number of channel contentions has been presented in [1]
Two ACK procedures are accepted for TXOP sharing
  Explicit ACK [1]
  Implicit ACK [2]
This proposal elaborates on the rules for TXOP operation
Proposed to use a new bit for the purpose of operating within a relay shared TXOP

## Slide 6: Signaling for Relay TXOP
Relayed Frame field
  1-bit to indicate if a frame is relayed within a TXOP
For ACK and CTS frame, a similar bit is also needed in the Frame Control field and NDP SIG
If this bit is set in an initiating frame (e.g. DATA), then it is a capability indication for implicit ACK
If this bit is set in a responding frame (e.g. ACK, CTS), then it indicates relay shall share the TXOP and continue to transmit the frame over the next hop after SIFS
The choice of which ACK procedure is decided by the Relay
Protocol Version
Type
From DS
More Fragments
Power Mgmt
More Data
Protected Frame
EOSP
Relayed
Frame
2
4
1
1
1
1
1
1
3
TID
1
Bits:
Frame Control field in short MAC header

## Slide 7: Downlink with Explicit ACK
RelayedFrame=1
AckInd=11
Relay sends ACK, and set response frame bits to 11 for next outgoing frame
DATA
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RelayedFrame=X
AckInd=00
RelayedFrame=0
AckInd=00
RelayedFrame=0
AckInd=10
AP sends downlink DATA frame with response frame bits set to 00 to relay
After receipt of ACK, AP removes frame from buffer, and defers MAX_PPDU + ACK + 2*SIFS before next event
ACK
SIFS
In SIFS time, relay sends DATA with a different MCS and response frame bits set to 00. Relay buffers frame until successful delivery or reaching of retry limit

## Slide 8: Downlink with Implicit ACK
Relay sends DATA with a different MCS, and sets response frame bits to 00
DATA
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RelayedFrame=1
AckInd=11
RelayedFrame=0
AckInd=00
RelayedFrame=0 AckInd=10
AP sends downlink DATA frame with response frame bits set to 11, so that other STAs can expect another DATA frame will follow
Within SIFS time, AP receives a PHY SIG field with response frame bits set to 00, and checks next-hop PAID in PHY SIG field

## Slide 9: Uplink with Explicit ACK
RelayedFrame=1
AckInd=11
Relay sends ACK, and set response frame bits to 11 for next outgoing frame
DATA
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RelayedFrame=X
AckInd=00
RelayedFrame=0
AckInd=00
RelayedFrame=0
AckInd=10
STA sends uplink DATA frame with response frame bits set to 00 to relay
After receipt of ACK, STA removes frame from buffer, and defers MAX_PPDU + ACK + 2*SIFS before next event
ACK
SIFS
In SIFS time, relay sends DATA with a different MCS and response frame bits set to 00. Relay buffers frame until successful delivery or reaching of retry limit

## Slide 10: Uplink with Implicit ACK
Within SIFS time, STA receives a PHY SIG field with response frame bits set to 00, and checks next-hop PAID in PHY SIG field
Relay sends DATA with a different MCS, and sets response frame bits to 00
DATA
SIFS
DATA
ACK
AP
STA
RELAY
SIFS
RelayedFrame=1
AckInd=11
RelayedFrame=0
AckInd=00
RelayedFrame=0
AckInd=10
STA sends uplink DATA frame with response frame bits set to 11, so that other STAs can expect another DATA frame will follow

## Slide 11: TXOP Sharing Operation
When a Relay receives a valid frame, the Relay may response with
  An Implicit ACK in next-hop transmission after SIFS, if Relay has received Relayed Frame bit set to 1
  An ACK after SIFS with Relayed Frame bit set to 1, and continue with next-hop DATA transmission after SIFS
  An ACK after SIFS with Relayed Frame bit set to 0, and does not continue to use the remaining TXOP
A relay may set Relayed Frame bit to 1 only if it has received a More Data bit set to 0.

## Slide 12: Conclusion
Proposed to define a new Relayed Frame bit for operation within a relay shared TXOP.

## Slide 13: Straw Poll 1
Do you support a Relayed Frame bit in the Frame Control field for TXOP operation in slide 11?
  Yes
  No
  Abstain

## Slide 14: Straw Poll 2
Do you support a Relayed Frame bit in the NDP ACK SIG field for TXOP operation in slide 11?
  Yes
  No
  Abstain

## Slide 15: References
[1] E. Wong et al., “Two-Hop Relay Function,” IEEE 11-12/1330r0
[2] Y. Kwon et al., “Implicit ACK for Relay,” IEEE 11-13/0075r0