## Slide 1: Format of Open-Loop Link Margin Index Field
Date: 2013-03-10
Authors:

## Slide 4: Open-Loop Link Margin Index Element
Open-Loop Link Margin Index information element has been accepted in 11ah.
The Open-Loop Link Margin Index is computed as
  Open-Loop Link Margin Index=Transmit Power + RX Sensitivity
  The transmit power is the transmit power used to transmit the frame containing the Open-Loop Link Margin Index element.
  The RX sensitivity is the minimum required receive power for reception of MCS10 for 1MHz channel.
The detailed format of Open-Loop Link Margin Index Field is TBD.

## Slide 5: Range of Open-Loop Link Margin Index
RX Sensitivity in 11ah specification has been proposed in [1]
  For 1MHz MCS10:
    Sensitivity_1MHz_MCS10 = truncate (-82 – 10*log(20) – 3 – 0.16) = -98dBm
True RX Sensitivity may be different from 11ah spec. due to implementations, environment and number of receive antennas.
  Assume up to 20dB margin on the best RX Sensitivity in 11ah specification
  Bring the minimum RX sensitivity to: -118dBm
Assume that transmit power variation is within 36dBm
  Transmit power range: 0dBm to 36dBm
  With consideration of MCS difference, BW difference and FCC regulatory.
Range of Open-Loop Link Margin Index
  -118+0= -118dBm to -98+36=-62dBm

## Slide 6: Proposed Format of Open-Loop Link Margin Index
    1 Byte Open-Loop Link Margin Index field can indicate 256 levels.
    Propose the granularity is 0.5dB.
      For open-loop, high precision is not necessary
The proposed format of Open-Loop Link Margin Index field is (-128+D*0.5) dBm.
  where D is the value shown in Open-loop link margin index field
  Examples:
    D=0, then Open-loop link margin index is -128dBm;
    D=255, then Open-loop link margin index is -0.5dBm;
  This proposal leaves enough rooms for variations and future changes on both directions.

## Slide 7: Straw Poll
Do you agree that the format of open-loop link margin index field is (-128+D*0.5) dBm, where D is an integer number within [0, 255]?
Yes/No/Abstain

## Slide 8: Reference
[1] “Receiver Sensitivity Levels”, IEEE 802.11-13/0061r0, Marvell.