## Slide 1: Spectral Flatness for 11ah
Date: 2013-03-18
Authors:

## Slide 4: Introduction
In this submission, we propose:
  802.11ah spectral flatness definitions and requirements for normal 1/2/4/8/16MHz modes and for 1 and 2MHz DUP modes
  Resolution BW for PSD measurements
Normal mode spectral flatness definitions taken from 11n/ac and extended for 1MHz
1 and 2MHz Duplicate transmission modes need modified spectral flatness definitions from normal modes
  Due to extra guard tones, DC tones and data tones introduced when duplicating 1 or 2MHz frequency segments across wider bandwidths.
  Take same approach as in 11ac for DUP modes based on 20MHz.

## Slide 5: 802.11ah 1/2/4/8/16MHz Spectral Flatness
Transmission BW(MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum Deviation (dB)
1 | -8 to -1 and +1 to +8 | -8 to -1 and +1 to +8 | ±4
 |  | -13 to -9 and +9 to +13 | +4/-6
2 | -16 to -1 and +1 to +16 | -16 to -1 and +1 to +16 | ±4
 |  | -28 to -17 and +17 to +28 | +4/-6
4 | -42 to -2 and +2 to +42 | -42 to -2 and +2 to +42 | ±4
 |  | -58 to -43 and +43 to +58 | +4/-6
8 | -84 to -2 and +2 to +84 | -84 to -2 and +2 to +84 | ±4
 |  | -122 to -85 and +85 to +122 | +4/-6
16 | -172 to -130, -126 to -44, +44 to +126, and +130 to +172 | -172 to -130, -126 to -44, +44 to +126, and +130 to +172 | ±4
 |  | -250 to -173, -43 to -6, +6 to +43, and +173 to +250 | +4/-6

## Slide 6: 802.11ah Spectral Flatness for 2 MHz DUP Mode
Transmission BW(MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum Deviation (dB)
4 | -42 to -33, -31 to -6, +6 to +31, and +33 to +42 | -42 to -33, -31 to -6, +6 to +31, and +33 to +42 | ±4
 |  | -58 to -43 and +43 to +58 | +4/-6
8 | -84 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to +58, +70 to +84 | -84 to -70,-58 to -33, -31 to -6, +6 to +31, +33 to +58, +70 to +84 | ±4
 |  | -122 to -97, -95 to -85 and +85 to +95, +97 to +122 | +4/-6
16 | -172 to -161, -159 to -134, -122 to -97, -95 to -70, -58 to -44, +44 to +58, +70 to +95, +97 to +122, +134 to +159, +161 to +172 | -172 to -161, -159 to -134, -122 to -97, -95 to -70, -58 to -44, +44 to +58, +70 to +95, +97 to +122, +134 to +159, +161 to +172 | ±4
 |  | -250 to -225, -223 to -198, -186 to -173, -43 to -33, -31 to -6, +6 to +31, +33 to +43, +173 to +186, +198 to +223, +225 to +250 | +4/-6

## Slide 7: 802.11ah Spectral Flatness for 1 MHz DUP Mode
Transmission BW(MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum Deviation (dB)
2 | -15 to -3 and +3 to +15 | -15 to -3 and +3 to +15 | ±4
 |  | -29 to -17 and +17 to +29 | +4/-6
4 | -42 to -35, -29 to -17, -15 to -3, +3 to +15, +17 to +29, and +35 to +42 | -42 to -35, -29 to -17, -15 to -3, +3 to +15, +17 to +29, and +35 to +42 | ±4
 |  | -61 to -49, -47 to -43, +43 to +47, and +49 to +61 | +4/-6
8 | -84 to -81, -79 to -67, -61 to -49, -47 to -35, -29 to -17, -15 to -3, +3 to +15, +17 to +29, +35 to +47, +49 to +61, +67 to +79, and +81 to +84 | -84 to -81, -79 to -67, -61 to -49, -47 to -35, -29 to -17, -15 to -3, +3 to +15, +17 to +29, +35 to +47, +49 to +61, +67 to +79, and +81 to +84 | ±4
 |  | -125 to -113, -111 to -99, -93 to -85, +85 to +93, +99 to +111, and +113 to +125 | +4/-6
16 | -172 to -163, -157 to -145, -143 to -131, -125 to -113, -111 to -99, -93 to -81, -79 to -67, -61 to -49, -47 to -44, +44 to +47, +49 to +61, +67 to +79, +81 to +93, +99 to +111, +113 to +125, +131 to +143, +145 to +157, and +163 to +172 | -172 to -163, -157 to -145, -143 to -131, -125 to -113, -111 to -99, -93 to -81, -79 to -67, -61 to -49, -47 to -44, +44 to +47, +49 to +61, +67 to +79, +81 to +93, +99 to +111, +113 to +125, +131 to +143, +145 to +157, and +163 to +172 | ±4
 |  | -253 to -241, -239 to -227, -221 to -209, -207 to -195, -189 to -177, -175 to -173, -43 to -35, -29 to -17, -15 to -3, +3 to +15, +17 to +29, +35 to +43,+173 to +175, +177 to +189, +195 to +207, +209 to +221, +227 to +239, and +241 to +253 | +4/-6

## Slide 8: Resolution Bandwidth for 802.11ah
11a/11n/11ac specs define a 100 kHz resolution bandwidth for PSD measurements.
  Subcarrier spacing for 11a/11n/11ac is 312.5kHz
11ah subcarrier spacing is 1/10 of 11a/11n/11ac
  New subcarrier spacing of 31.25kHz
The resolution bandwidth for 11ah should be selected as 10kHz
  Keeps the same subcarrier spacing to resolution bandwidth ratio as 11ac
  Same measurement accuracy for each subcarrier being tested as 11ac

## Slide 9: Straw Poll 1
Do you agree with the proposed spectral flatness definitions and requirements for normal modes and 1 and 2MHz DUP-modes on slides 5, 6, and 7?
  Y
  N
  A

## Slide 10: Straw Poll 2
Do you agree with a resolution BW of 10kHz for 802.11ah?
  Y
  N
  A