## Slide 1: Short MAC Header Design
Date: 2013-03-15
Authors:

## Slide 4: Introduction
The MAC header is a significant overhead for short MPDUs [1, 2]
  30-36 octets in 11n, without security
  This is inefficient for short-packet applications
    E.g., the FR-EM document includes traffic specifications for sensors (256Bytes), and industrial process automation (64Bytes) [3]. Other applications with very short packets can be envisioned
Shortening the MAC header has advantages for 11ah
    Prolonged battery lifetime
    Reduced medium occupancy
Motions that define the structure of the Short MAC header have passed [5]
  See next slide for details on the structure
This presentation follows up on other design details for the Short MAC header

## Slide 5: Short MAC Header Format – current status
Frame Control (2 Bytes)
  There are 3 available bits
Short ID (2 Bytes)
  Contains the Association ID (13 bits) of the RX/TX STA depending on From DS value
  There are 3 available bits
A3 is optionally present based on A3 Present indication bit
Octets: 2 | 2/6 | 6/2 | 2 | 6 | variable | 4
Frame Control | A1 | A2 | Sequence Control | A3 | Frame Body | FCS
bits 2 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3
Protocol Version | Type | From DS | More Fragments | Power Management | More Data | Protected Frame | EOSP | A3 Present | TBD
13 | 3
Association ID (AID) | Reserved
Short ID (SID)
Frame Control

## Slide 6: A3 Present
Propose to move A3 present bit from Frame Control to Short ID field
  One additional free bit is available in FC for other features
  A3 is not necessary for the Short MAC header with 2 full MAC addresses
    That would have similar overhead to normal MAC header, with only 2 Bytes less due to Duration field removal
bits 2 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3
Protocol Version | Type | From DS | More Fragments | Power Management | More Data | Protected Frame | EOSP | A3 Present | TBD
13 | 3
Association ID (AID) | Reserved
Short ID (SID)
Frame Control

## Slide 7: A4 Present and A-MSDU
The 11ah spec framework requires the following
  A Relay shall use 4-address frames or A-MSDU to forward packets [6]
We propose to indicate presence of A4 and A-MSDU in short MAC header
  Use reserved bits in SID field to indicate presence of A4 and A-MSDU
Allows to use short MAC header for relay operation
From an overhead perspective
  22 Bytes for a short MAC header with A4 (when A3 is stored at the Relay)
  40 Bytes for a normal MAC header with 4 addresses
13 | 1 | 1 | 1
Association ID (AID) | A3 Present | A4 Present | A-MSDU
Short ID (SID)

## Slide 8: Traffic Identifier (TID)
TID identifies the TC/TS to which the MSDU or A-MSDU belongs
  It also identifies the TC or TS of traffic for which a TXOP is being requested
    Through the setting of TXOP duration requested or queue size
Including the TID in the short MAC header has already been accepted [7]
  Sufficient for correct operation with EDCA (0—7)
  We propose to send the 3 LSBs of the TID in the Frame Control
    First MSB of TID can be stored at the receiver if HCCA or HEMM is used
    Fits perfectly in the available bits in the Frame Control
      One additional bit is still available
bits 2 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3
Protocol Version | Type | From DS | More Fragments | Power Management | More Data | Protected Frame | EOSP | Reserved | TID
Access policy | Usage | Allowed values in TID subfield (4 bits)
EDCA | UP for either TC or TS, regardless of whether admission control is required | 0–7
HCCA | TSID | 8–15
HEMM | TSID, regardless of the access mechanism used | 8–15

## Slide 9: Conclusions
Following up on the design of short MAC header [5], we propose
  Move A3 Present bit from Frame Control to SID field
  Include A4 Present and A-MSDU indication bits in the SID field
  Include 3 LSBs of the TID in FC to enable correct operation of EDCA

## Slide 10: References
[1] 11-12-0365-01-00ah-mac-header-compression
[2] 11-12-0110-06-00ah-frame-header-compression
[3] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology
[4] 11-12-0324-00-00ah-short-ack
[5] 11-12-0857-00-00ah-short-mac-header-design
[6] 11-13-0068-00-00ah-group-addressed-mpdu-transfer-in-relay
[7] 11-13-0027-00-00ah-duplicate-detection-of-short-mac-frame

## Slide 11: Straw Poll 1
Do you support to update in the spec framework, in section 4.5, the Frame Control field of the short MAC Header with the following:
  Move the A3 Present subfield to the SID field
  Include the 3 LSB bits of the TID
bits 2 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3
Protocol Version | Type | From DS | More Fragments | Power Management | More Data | Protected Frame | EOSP | Reserved | TID

## Slide 12: Straw Poll 2
Do you support to specify in the spec framework, in section 4.5, that the 2 Byte address field is called Short ID field and that it includes the following subfields:
Association ID (AID), A3 Present, A4 Present, A-MSDU
13 | 1 | 1 | 1
Association ID (AID) | A3 Present | A4 Present | A-MSDU