## Slide 1: Very Low Energy Paging Followup
Date: 2013-3-17
Authors:

## Slide 4: Introduction
The concept of NDP Paging (very low energy paging) signal was accepted in TGah:
Allows paging indication with an NDP frames
  much shorter than short beacon
Enables use of optimized receivers for this paging frame
When requested by a STA, the AP schedules a DL (downlink) synch frame at the slot boundary or the target wake time of the STA as the next frame for transmission [Nov 2012 meeting minutes, 11-12/1324r0]
  Synch frame is an NDP frame including at least
    (Partial) identifier of the target STA(s)/group of STAs (# bits TBD)
    BU present (1 bit)
    Partial TSF (# bits TBD)
Check beacon (# bits TBD

## Slide 5: Definition of TBDs and Enhancements:
This Proposal:
  Defines the use of the protocol with TWT
  Defines the behavior of the STA
  Enhances the protocol avoiding unnecessary transmissions

## Slide 6: Proposal Summary
When setting up a TWT, a STA may request the following protocol to be used
  Request though additional field in the TWT Information Element
AP shall send the NDP Paging frame as the fist frame to the STA during the agreed NDP TWT period if:
  There are buffer units for the STA
  There are critical change to the beacon
  A max time until the previous NDP Paging frame has expired
    For time synch purpose and also latency requirement guarantee
    Open on this part; Initial text required this interval to be equal to the TWT period
Otherwise AP shall not send any frame to the STA during the NDP TWT duration
At TWT, STA will listen to medium for an NDP Paging frame from AP
  After Receiving the NDP Paging frame, STA may go to sleep and wakeup later to perform an action
    Actions include:
      Sending PS-Poll/ trigger frame
      Wakeup after T (time unit)
      Receiving the Beacon

## Slide 7: Straw poll
Do you support the proposed revised protocol for NDP Paging (very low energy paging) in page 4.

## Slide 8: References
Very Low Energy Paging:
TGah:
  11-12-1324-00-00ah-Very-Low-Energy-Paging.pptx

## Slide 9: Appendix

## Slide 10: NDP Paging Setup
TWT1: AP sends NDP
TWT2
TWT3: AP sends NDP
TWT4
TWT5: AP sends NDP
TWT6
TWT7: AP sends NDP
TWT8
TWT9: AP sends NDP