## Slide 1: Experimental test report of FILS
Date: 2013-03-18
Authors:

## Slide 2: Abstract
The presentation report the result of field experimental trial of a FILS prototype.
The implemented prototype is not equal to the current TGai spec (D0.4).
The purpose of this trial is to confirm the prospected performance of reduced AKM.

## Slide 3: Over View of field experimental trial
Field and Date
  Kyoto University, 22nd Feb 2013
AP Setup
  IEEE802.11g ch13 commercial AP
STA Setup
  Android 2.3 tablet device

## Slide 4: Implemented Protocol
AS is collocated on AP
WPA2:DHCP server is connected by Ethernet.
FILS: IP address pool is collocated on AP.
AP
STA
DHCP
Beacon
Probe
Authentication
Association
EAPOL Key
DHCP
AS
EAP
(PEAP/MSCHAPv2)
AP
STA
DHCP
Beacon
Probe
AS
FILS
WPA2
FILS

## Slide 5: Implementation of FILS Prototype
ANonce
ANonce, SNonce, NAI, MIC
ANonce, IPv4 (addr, mask, gateway, DNS), GTK, MIC
144 octets
147 octets
STA
AP
No any change of scanning mechanism
WPA2 and FIlS Prototype are implemented on the same AP
No any change of hardware

## Slide 6: Environment AP1
One AP was installed on window side of 2nd floor.
0m
-30m
+30m
-60m
+60m
-90m
AP

## Slide 7: Test Scenario 1
A pair of FILS and WPA2 are entering the service area.
Measured the distance of STA and AP where STA establish link successfully and received http contents.
Measured the time from Association/FILS request to IP address assignment by propriety application.
FILS
Service Area
歩きながら移動
WPA2
非接続
非接続
Established Link Point

## Slide 8: Result of test scenario 1 (Distance)
*WPA2 No3 did not establish the link.
Working Direction

## Slide 9: Result of test scenario 1 (Time)
*WPA2 No3 did not establish the link.

## Slide 10: Result summary of test scenario 1
All FILS STA established link before arriving at in the front of AP.
All WPA2 established link since they passed in the front of AP.
Average link established time between FILS request to IP address assignment is 1.224 Sec.
Average link established time between Association request to IP address assignment is 9.827Sec

## Slide 11: Test Scenario 2
20 FILS and 20 WPA2 are entering the service area continuously.
Measured the distance of STA and AP where STA establish link successfully and received http contents.
Measured the time from Association/FILS request to IP address assignment propriety application.
FILS
Service Area
歩きながら移動
WPA2
非接続
非接続
Established Link Point

## Slide 12: Result of test scenario 2 (Distance)
Working Direction

## Slide 13: Result of test scenario 2 (Time)

## Slide 14: Result summary of test scenario 2
90% (18/20) FILS STA established link before arriving at in the front of AP.
85% (17/20) WPA2 established link since they passed in the front of AP.
Average link established time between FILS request to IP address assignment is 0.742Sec.
Average link established time between Association request to IP address assignment is 21.599Sec

## Slide 15: Test Scenario 3
41 FILS are entering the service area continuously.
Measured the distance of STA and AP where STA establish link successfully and received http contents.
Measured the time from FILS request to IP address assignment.
FILS
Service Area
歩きながら移動
非接続
Established Link Point

## Slide 16: Result of test scenario 3 (Distance)
Working Direction

## Slide 17: Result of test scenario 3 (Time)

## Slide 18: Result summary of test scenario 3
80% (33/41) FILS STA established link before arriving at in the front of AP.
Average link established time between FILS request to IP address assignment is 0.78Sec.

## Slide 19: Scenario 2
Blue bibs : FILS vs White bits:WPA2
The 0 sign marker was located around 30m from AP
1.5m/Sec = 5.5km/h working speed

## Slide 20: Test Scenario 4
20 FILS and 20 WPA2 are entering the service areas continuously.
STA download contents related to the linked AP automatically.
Measured the number of downloaded content.
  STA will download two different contents (109KB Gif image ) if STA connected to two AP in turn definitely.
FILS
歩きながら移動
WPA2
非接続
非接続
Down load content1
Down load content2
AP1
A2

## Slide 21: AP2
Another AP(AP2) was located on the opposite of building.
The coverage of AP1 and AP2 are not over wrapped each other.
0m
-30m
+30m
-60m
+60m
-90m
AP1
AP2

## Slide 22: Result summary of test scenario 4
95% (19/20) of FILS STAs downloaded two different contents correctly.
  1 error caused by application error.
50% (10/20) of WPA STAs could not download any content.

## Slide 23: Test scenario 5
50 FILS and 50 WPA2 are setting on table.
One AP was implemented in the same room.
Activate AP.
Measured the time from Association/FILS request to IP address assignment.

## Slide 24: Result of test scenario 5
Average of established Link time at FILS 0.685 Sec
Average of established Link time at WPA2 15.880 Sec

## Slide 25: Conclusion
FILS STAs completed the association process in significantly less time than WPA STAs.
 More time within the coverage area of an AP to use for (user) data exchange
The large number of frame exchanges for WPA2 STAs (as compared to FILS STAs) made them vulnerable for fading when entering the AP‘s coverage
  If retransmission of a lost frame did not succeed after three attempts, the association process had to restart from the beginning
Further performance increase expected once advanced FILS Discovery schemes are employed