## Slide 1: TGai Principles and Mechanisms (Joint TGai and TGaq Meeting)
Date: 2013-03-08
Authors:

## Slide 2: Abstract
Overview on TGai principles and mechanisms to enable for Fast Initial Link Set-Up as of March 2013.
Disclaimer: This document has not been approved by TGai as an official TGai overview document. It has been assembled by the authors based on submissions approved for going into the TGai Draft (D0.4) as well as on documents currently under discussion.
The 802.11ai scanning enables QoS oriented fast discovery that is backward compatible.

## Slide 3: Objective
TGai aims at providing mechanisms enabling a fast initial link set-up in less than 100ms.
Note that TGai mechanisms will enable this performance but will not guarantee the 100ms link set-up time under all circumstances.
The initial link setup includes all operations required for IP data exchange:
  Discovery of the network and the BSS
  Authentication and association signaling
  IP address configuration
See also: TGai PAR: 11-10/1152r1

## Slide 4: Main drivers
Environments
  Busy areas: The famous ”Tokyo Metro Station” and KDDI measurements
  Increased amount of spectrum & number of networks & number of devices
Signaling overhead
  Unnecessary information exchange
  QoS violations
Offloading, WLAN use is increasing
  It is equally important to shorten the link setup time as it is to shorten the data transmission time
  Shorter scanning reduces power consumption of the device
See also: TGai Use Cases: 11-11/238r19

## Slide 5: Where we are
Draft D0.4
  Available on mentor
  Currently under “volunteer review” to increase clarity and maturity of language
  Expect a (major?) editorial change to reflect / align to changes introduced by 11ac into 802.11
Contributions related to DISCOVERY / SCANNING
  D0.4 stable with respect to technical contents on network discovery / scanning
  No new technical contributions for the last two meetings
Contributions related to HIGHER LAYER SET-UP
  Two approaches currently under discussion (down selection expected in March 2013)
  General container to carry any protocol (including DHCP) vs. IP-set-up-specific information

## Slide 6: Not Quoting the Time Plan
Down selection of higher layer set-up proposal (hopefully) to conclude in March 2013 meeting
Issue of Request for Comments by end of March / End of May meeting, depending on
  Progress on resolving comments from volunteer reviewers and agreement
  Approving / down selecting higher layer set-up approach

## Slide 7: What’s next in the presentation
Overview on DISCOVERY / SCANNING approaches
  Active scanning related
  Passive scanning related
Overview on HIGHER LAYER SET-UP & SECURITY

## Slide 8: 802.11ai Active Scanning enhancements

## Slide 9: General scanning enhancements
More control to scanning procedures:
  Terminating the ongoing scan
  More reporting options of the scanning result
    Immediate reporting
    Reporting after a channel is scanned
    Legacy, reporting after scanning is completed
Announcing one or more neighbor BSS or channel information in Beacon, Probe Response and Fast Discovery (FD) frame
  Avoids scanning of channels with no AP
  BSSID enables more precise active scanning
  Additional parameters may be included to provide more information of the neighbor BSSs

## Slide 10: Active scanning, expedited scanning procedure
If device has received a probe request, it should avoid transmitting the same probe request as transmitted
STA 1
Probe Request
STA 2
Delay probe request transmission
AP1
AP2
AP3
STA 1
Probe Response
STA 2
Abort probe request transmission
AP1
AP2
AP3

## Slide 11: Active scanning, Probe Response collision avoidance
The APs avoids sending unnecessary copies of probe responses
Single copy of probe response or beacon frame is enough
STA 1
Probe Request
STA 2
STA2 misses the probe request transmission
AP1
AP2
AP3
STA 1
Probe Response
STA 2
Receive probe responses
AP1
AP2
AP3
STA 1
Probe Request
STA 2
AP1
AP2
AP3

## Slide 12: Active scanning, comprehensive response
One probe response may contain information of multiple APs
The total amount of responses is reduced
STA 1
Probe Request
Chn 1
Chn 6
Request for information of other BSSs
AP1
AP2
AP3
STA 1
Probe Response + Neighbor List
Contains information of itself (AP 2), as well as AP 1 and AP 3 or channel 6
Chn 1
Chn 6
AP1
AP2
AP3

## Slide 13: Active scanning, new response criteria
Probe Request contains criteria to transmit Probe Response. Response is transmitted only if the criteria is met
Criteria include:
  Transmission power
  AP transmission Delay
  Vendor specific information
  Data delivery rate to Internet
  AP capabilities
STA 1
Probe Request
Criteria for AP delay performance & RSSI
AP1
AP2
AP3
STA 1
Probe Response
Probe response is transmitted if all the criteria are met
AP1
AP2
AP3

## Slide 14: Active scanning, Probe Response Reception Time element
The transmitters of the Probe Request may indicate how long the transmitter will be available to receive Probe Responses
Probe Response Reception Time is set to MAX_Probe_Response_Time

## Slide 15: Reducing sizes of the responses
AP Configuration Change Count (CCC) keeps count of changes of the parameters in Probe Response and Beacon
  One octet in length
  Changes of BSS Load, Average Access Delay and other rapidly changing parameters are not considered in CCC

## Slide 16: 802.11ai Passive Scanning enhancements

## Slide 17: Passive Scanning, key enhancements
FILS Discovery (FD) frame: a new public action frame
  small-size: 30-byte MAC framing + 10 to about 25 bytes FD frame body, i.e., 40 to 55 bytes for typical uses;
  One Mandatory information item: SSID;
  Optional information items: AP’s Next TBTT, AP-CCC, Access Network Options, Capability, Security, Neighbor AP information.
  transmitted between beacon frame transmissions, for a fast AP/Network discovery;
  Transmitted as non-HT duplicate PPDU, when using a larger channel than 20MHz;
Payload/FD Frame
Primary channel of the transmitter
Preamble
Payload/FD Frame
Payload/FD Frame
Payload/FD Frame
Preamble
Preamble
Preamble
T2
time
Example #1
T1
time
T3
time
Example #2
Example #3
Beacon
FD frame

## Slide 18: Network Discovery, key enhancements
GAS query enhancement by using an AP white-list
  A new IE with one or multiple 6-byte BSSIDs in GAS request to indicate the AP(s) that the requesting STA wants to query.
  GAS traffic reduction by using GAS Configuration Sequence Number
  A new IE with an 1-byte unsigned integer:
    indicating the version number of AP’s GAS configuration information set;
    monotonically incrementing whenever there is any change in the AP’s GAS configuration information set;
    Used in Beacon and/or Probe Response.

## Slide 19: 802.11ai Security & Higher Layer Set-Up

## Slide 20: FILS Security Status
Current Status:
Three FILS authentication protocol options specified:
  FILS Authentication with Trusted Third Party
  FILS Authentication with Trusted Third Party and “PFS”
  FILS Authentication without Trusted Third Party
Main differences:
  Different trust assumptions
  Different assumption on “pre-existing” system set-up
  Different assumptions on online availability of the “backbone network”
Common elements:
  All have only four protocol flows
  All implemented via Authentication/Association Request/Response frames
  All allow piggy-backing of other info along Association frames
  (e.g., IP address assignment)
Current Work in Progress:
How to deal with large objects (e.g., certificates, higher-layer data objects)
How to specify main piggy-backing details (e.g., on IP address assignment)

## Slide 21: FILS Key Establishment
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
online/offline assistance
with authentication
FILS key establishment protocol options provided:
FILS Authentication with TTP, based on ERP
(two flavors: with or without “PFS” (ERP+ECDH, resp. ERP)  see next slides)
Authentication without online TTP, based on ECDH and ECDSA certificates

## Slide 22: FILS Key Establishment with TTP
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
Secret keys
TTP
{(STA: KSTA),
(AP: KAP), …}
FILS authentication with online TTP:
TTP actively assists STA and AP in deriving shared keying material (hence, “online”)
Two flavors: with or without “Perfect Forward Secrecy” (PFS)
NOTE: With “PFS”, TTP usually does not learn shared key STA-AP, nor can re-compute past sessions should node get compromised (in short: better security)
Requires STA and AP to share secret key with same TTP (e.g., via ISPs that have pre-existing business relationships)
KAP
KSTA

## Slide 23: FILS Key Establishment w/o. TTP
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
Public
keys
CA
{CertSTA,
CertAP, …}
FILS authentication without online TTP:
STA and AP can derive shared keying material and authentication directly, via use of
certificates (so, no need for any active involvement third party for authentication)
Third party may still be involved for authorization or for configuration (as with all
FILS key establishment protocols)
Requires STA and AP to certify their own public
key with some CA (e.g.,
during manufacturing)
CA root key
CA root key

## Slide 24: Adding “piggy-backed info” to protocol flows …
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
Services
+ piggy-backed info response
+ piggy-backed info request
Authentication help
Configuration help
IP address assignment
Authorization
Subscription
credentials
Piggy-backing info along FILS authentication protocol:
Higher-layer set-up, including IP address assignment
Authorization functionality, subscription credentials, etc.
See details elsewhere in presentation

## Slide 25: Higher Layer Setup
TGai draft specification will include higher layer setup function.
Information for higher layer setup, such as IP address, will be piggy-backed in Association Request and Association Response.
Piggy-backed higher layer setup information will be protected (encrypted and authenticated).
We have 2 proposals and we have not agreed yet which one to be the specification.
It will be decided in this week.

## Slide 26: Concept
How to assign higher layer information will not be specified by TGai.
STA
AP
Association Request
(Higher Layer Information Request)
Association Response
(Higher Layer Information Response)
Successful Key Confirmation
Beacon/Probe Resp.
Authentication
Authentication/Key Derivation
Authentication
Key Derivation
Higher Layer Information such as IP address is assigned.

## Slide 27: Proposals
Proposal A
  Just provides container to carry higher layer information such as DHCP messages.
  Expect to use DHCP for IP layer setup, but it can carry any higher layer messages.
Proposal B
  Define IEEE802.11ai specific IP address assignment protocol.
  Specific to IPv4 and IPv6, and IEEE802.11ai.

## Slide 28: References
TGai PAR https://mentor.ieee.org/802.11/dcn/10/11-10-1152-01-0fia-fast-initial-link-set-up-par.doc
TGai Use Case Document https://mentor.ieee.org/802.11/dcn/11/11-11-0238-19-00ai-use-case-reference-list-for-tgai.docx
TGai D0.4