## Slide 1: IP Address assignment: Offline discussion summary
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com
George Cherian | Qualcomm |  | +1-858-651-6645 | gcherian@qti.qualcomm.com
Date: 2013-03-18
Authors:

## Slide 2: Summary: Include both options
REASON: Proposals address different use-cases
Use of DHCP using HLP
Benefits:
IP address continuity
More general
Cost:
Additional rounds of signaling before data transmission can begin [2 additional roundtrips: (i) for Duplicate Address detection for IPv6; (ii) for DNS MAC address discovery for local DNS]
Additional latency for IPv6: Duplicate Address detection requires that the all the existing/associated devices need to be given time to respond to the query sent out by the new incoming device. Deployment of “Optimistic DAD (RFC4429)” can reduce this latency
Association response may be delayed if DHCP server does not respond in time
FILS IP Address assignment
Benefits:
No additional signaling: helps in crowded situations, transit stations to reduce signaling storms
IP address locally assigned (by AP): Does not introduce additional latency to send Association Response message
Cost
Minimized feature set (only limited options of DHCP are supported)
IP address continuity outside of an ESS not supported

## Slide 3: Which one to use?
Which mechanism to use?
Based on application requirement
How to select the IP address assignment method?
Beacon/Probe Response advertises which options are supported by the AP
STA selects the appropriate option based on the AP support and the application requirement