## Slide 1: STA Optimized Link Setup
Date: 2013-04-11
Authors:

## Slide 2: Abstract
802.11ai enhances the link setup. The enhanced link setup is fast and reduces the number of setup frames.
802.11ai has not considered whether the terminal needs to operate in Awake state during the link setup.
The presentation describes means to enable the terminal to operate in power save during the link setup.
The possibility to operate in power save simplifies terminal implementation and improves battery lifetime.

## Slide 3: Motivation, challenges of the terminal implementation
Mobile terminals have typically many radios
  Each radio operates according to its standard
    Multiple radios may use the same antenna. This prevents the simultaneous operation of the radios
  WLAN radio may concurrently operate in multiple topologies, i.e. in IBSS and in BSS
    Different BSSs may operate in different channels and single radio is not capable to simultaneous operate in multiple channels
The implementation must satisfy the requirements of each radio and topology
  The standards should avoid unncessary requirements for the STAs

## Slide 4: Recap, link setup signaling
Currently, the AP and the terminal transmit over 20 frames at the link setup
  The link setup delay depends on the round-trip delay and the implementations of the AP and the authentication server
802.11ai targets to transmit four (4) frames or burst of frames at the link setup
  The delay between transmitted frames may increase, because each frame may carry more information
  The total link setup time is shortened

## Slide 5: STA optimized link setup
The terminal operation in Awake State should be minimized
  The terminal may operate in Doze state and operate in Awake State only to receive the responses from the AP
Authentication request
Processing delay of the AP.
Authentication response
Association response
Association request
STA
AP
Processing delay of the STA.
No frames are expected from the AP.
Processing delay of the AP.
Terminal need not operate in Awake State during these delays.

## Slide 6: Operations to enable the power save during the link setup
The terminal needs to know when the AP is able to transmit the responses
  The terminal should not try to obtain information before the AP is ready
The power saving STA indicates when it is available to receive the responses
  The terminal controls when the AP may transmit the responses

## Slide 7: GAS Query to provide information when AP ready transmit the response
The GAS request requests the Comeback delays of the AP
GAS response provides Comeback delay 1 and Comeback delay 2
The GAS Query may also provide the delays of legacy link setup
The link setup time may be used as criteria to select AP for association
Authentication request
GAS.request
GAS.response
Authentication response
Association response
Association request
STA
AP
Comeback delay 1
Comeback delay 2

## Slide 8: Recap, U-APSD principles
Unscheduled APSD is typically used for power save
  The AP may transmit frames to the power saving STA after it has received an indication / a trigger frame from the STA
  The trigger frame ensures that the power saving STA is available to receive frames
  When AP desires to stop frames transmission it transmits a frame with EOSP field set to 1
    When terminal receives this frame it knows that AP will not transmit more frames before new service period triggering
AP transmits frames immediatedly to active mode STA
  The STA is available to receive at all times

## Slide 9: Indicating the operation in power save mode at the link setup
The STA sets the Power Management field to 1 in Authentication request frame to indicate that it operates in power save mode during the link setup
  This is the same operation as in unscheduled APSD
When the STA is in active mode, the AP transmits the response frames as soon as possible
When the STA is in power save mode, the Link setup comeback requests are used as shown in the next slide

## Slide 10: Operation in power save
The power saving STA triggers the response frame transmission with Link setup comeback request
The last response frame indicates that the terminal may return to Doze state
Authentication request
Authentication response
Association response
Association request
STA
AP
Comeback delay 1
Comeback delay 2
Link setup comeback request
Link setup comeback request

## Slide 11: Summary
The presentation describes means to enable the terminal to operate in power save during the link setup
GAS Query requests the Comeback delays
  Gas Query may provide delays also for legacy link setup
The link setup responses are transmitted to power saving after the STA has transmitted Link setup comeback request frame
  STA indicates does it operate in power save mode during the link setup