## Slide 1: 802.11mc CIDs 1136,1118,1458
Date: 2013-04
Authors:

## Slide 2: Abstract
This document contains a discussion and proposals relating to CIDs 1136, 1118, and 1458

## Slide 3: CID 1136
Clause 8.2.4.5.8 (AP PS Buffer State subfield
If a QoS Data frame is fragmented, may the QoS AP Buffered Load value remain constant in all fragments even if the total buffer size changes as successive fragments are transmitted?
Proposal
Add following text after last paragraph of 8.2.4.5.8.
“If a QoS Data frame is fragmented, the QoS AP Buffered Load value may remain constant in all fragments even if the total buffer size changes as successive fragments are transmitted.”

## Slide 4: CID 1136
Figure 8.5 QoS AP PS Buffer State subfield
  8-bit field that indicates the PS buffer state at the AP for a STA
  It is used for a QoS Data frame sent by HC.
The AP Buffered Load subfield is 4 bits in length and is used to indicate
the total buffer size, rounded up to the nearest multiple of 4096 octets and
expressed in units of 4096 octets, of all MSDUs and A-MSDUs buffered at
the QoS AP (excluding the MSDU or A-MSDU of the present QoS Data frame.

## Slide 5: CID 1136
As the size is in increments of 4096 I doubt if fragmented frames would ever be larger than this, so I doubt if the number in the field could change anyway.
Is it possible that a packet of greater than 4096B would be fragmented? Surely an A-MPDU aggregation does not need fragmentation, and does an A-MSDU also need fragmenting? Seems to me to defeat the object of aggregation.
Having said that, I do not see a problem with accepting the text but would recommend “Reject”

## Slide 6: Motion
CID 1136 “Reject”.
The size of the field is in increments of 4096. Fragmented frames would never be larger than this.

## Slide 7: CID 1118
Comment
The Average Access Delay values do not appear to correspond to practice.
Access delay is defined in 10.11.16 as "begins CSMA/CA access". This can be read such that the access delay includes the SIFS, AIFS,0-CWmin time but definitely includes the time for retries (SIFS + AIFS + 0 to 2^n x CWmin). For example average access delay for VO would be 47.5us and DCF 101.5us. 2 retries is 65.5 and 304us average respectively.
Why, therefore do we have 8, 16 and 32us steps in the element (8.4.2.41)? The granularity seems way out of step and way too fine. Then what about the time for packets from other STAs which hold up the queued packet? - at 130Mbps a 1500B packet is 184us (inc ACK).
The accuracy is set (correctly) at 100us (10.11.16) so again the 8, 16 and 32us steps in the element are wrong.
Proposal
Revise the values of the Average Access Delay to be in 100us steps, i.e. (n x 100)us < Access Delay < (n+1) x 100 us

## Slide 8: Original intent of this IE (Courtesy Roger Durand)
This field was an attempt by others (an AP vendor proposal) to call out an “averaged”, “additional access delay” beyond what you are calling out below for a “first try” at the medium for a network load element... the focus here is the word “additional”… This is not “access delay”… This might best be thought of a listen before talk delay when testing the medium for energy or channel occupancy… The basic increment after some debate was called out as 16 microSeconds per increment…
So lightly loaded BSS network might report a 10 and it would equal 160 microseconds beyond what you are communicating below for each COS category… 100 might be a more heavily loaded network with occasional collisions which might average to 1.6 milliseconds… a number greater than 100 should only happen when more than one collision is occurring.

## Slide 9: What happened? Courtesy Roger Durand
I think the word additional was removed as some English perfectionist thought it was redundant with delay in the same phrase.
And in 10.11.16 someone misidentified its purpose and said it included CSMA delay at start when it was not meant to do this, if anything this paragraph should say CSMA delay at end of count.
This was not supposed to include MAC delays but only RF or medium delays when the packet is “ready to be transmitted” it does say this in 10.11.16 but someone else added “begins CSMA/CA access” and this is flat wrong. It should say “ends CSMA/CA access” and then it makes sense…
(Note GS : …except for the 100us accuracy!)

## Slide 10: Access Delay 8.4.2.41 Values
0: Access Delay < 8 μs
1: 8 μs ≤ Access Delay < 16 μs
2 ≤ n ≤ 14: n × 8 μs ≤ Access Delay < (n + 1) × 8 μs
15: 120 μs ≤ Access Delay < 128 μs
16: 128 μs ≤ Access Delay < 144 μs
17 ≤ n ≤ 106: (n × 16) – 128 μs ≤ Access Delay < ((n + 1) × 16) – 128 μs
107: 1584 μs ≤ Access Delay < 1600 μs
108: 1600 μs ≤ Access Delay < 1632 μs
109 ≤ n ≤ 246: (n × 32) – 1856 μs ≤ Access Delay < ((n + 1) × 32) – 1856 μs
Hence steps range from 8us to 32us.

## Slide 11: What do we do?
The Commenter was right, as written the values in the table are wrong and do not agree with the definition and the accuracy.
If the intention was that this is “additional delay” and 16us then the text must be changed in 10.11.16 to make this clear.
I do not know who the original proponents of this “Access Delay” were. It does appear to be applicable to an enterprise AP and maybe a member in that field should look at it.

## Slide 12: Edit Definition of Access Delay, 10.11.16
Access delay is measured by the AP’s MAC layer being the average medium access delay for transmitted frames measured from the time the MPDU is ready for transmission (i.e., begins CSMA/CA access) until the actual frame transmission start time.
….The accuracy for the average medium access delay shall be ± 100 μs or better when averaged over at least 200 frames. ….
One option, along the lines that Roger suggests:
“Access delay is measured by the AP’s MAC layer being the average additional medium access delay for transmitted frames measured from the time the MPDU is ready for transmission (i.e., after CSMA/CA access) until the actual frame transmission start time.
….The accuracy for the medium access delay shall be ± 100 32 μs or better when averaged over at least 200 frames. ….”

## Slide 13: CID 1118
Propose “Revise” Change 10.11.16 as per previous slide.
Option is to get an original proponent to look at this, or at least an Enterprise AP member to approve or change it.

## Slide 14: CID 1458
Comment 8.4.2.32
It's not clear how to indicate A-MSDU/A-MPDU aggregation in TSPECs; this can have a significant effect on the medium time required for a particular traffic stream
Proposal
Create a new IE to signal this information (sadly, the TSPEC IE is not extensible). Consider whether A-MSDU aggregation would be better handled by redefining the Nominal MSDU Size field to be the nominal A-MSDU size if A-MSDUs are used, and if so (a) whether giving information on A-MSDU aggregation could be useful and (b) how the Data Rates in the TSPEC should account for the A-MSDU overheads

## Slide 15: Nominal MSDU
The Nominal MSDU is already defined to include A-MSDU.
“The Nominal MSDU Size field is 2 octets long, contains an unsigned integer that specifies the nominal size, in octets, of MSDUs or A-MSDUs belonging to the TS under this TSPEC.”
The text proposed in 13/0013 does recommend how to calculate the Medium Time for the case of A-MSDUs.

## Slide 16: Aggregation
13/0012 and 13/0013 propose adding new section to Annex N on :Use of TSPEC with aggregated MSDUs and MPDUs.
It proposes using the Max SI field to indicate aggregation and latency.

## Slide 17: Proposal for CID 1458
Revise
Consider this with CIDs 1112, 1113, 1114, 1115, 1116, 1117, 1458
Propose acceptance of 13/0013r1.