## Slide 1: Discussions on FILS Authentication
Date: 2013-05-03
Authors:

## Slide 2: Abstract
This document provides further discussions regarding FILS Authentication, for a comment submitted as a response to 802.11 WG Comment Collection 8 (CC8), on the question "Please provide comments on Draft P802.11ai D0.5".

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3, 4

## Slide 4
Re-Cap: FILS Authentication
Three FILS Authentication Methods in 11ai/D0.5
  EAP-RP with no PFS
  EAP-RP with PFS
  Non-TTP with PFS
  FILS Authentication Operations
  Using Authentication frames and Association frames with newly introduced FILS authentication information content items;
  Piggybacking IP address assignment in FILS association frames;
  Designed to effectively reduce the authentication time and IP address setup time for STAs during initial link setup.

## Slide 5
FILS Authentication with TTP
Authentication with TTP (Trusted Third Party)
  AP and STA perform mutual authentication using a mutually-trusted third party, e.g., AAA server;
  The TTP is known to both AP and STA;
  Current applications/adoption/common use cases:
    3GPP - WLAN interworking: TS23.234, TS23.402.
    Secure Authentication for the Passpoint program from the Wi-Fi Alliance to enable seamless and secure Wi-Fi access in hotspots (2012)
    Next Generation Hotspot (NGH) Program of the Wireless Broadband Alliance: http://www.wballiance.com/wba-initiatives/next-generation-hotspot
Two Schemes of FILS Authentication with TTP
  EAP-RP without PFS (Perfect Forward Secrecy)
  EAP-RP with PFS
   Both are based on EAP-RP

## Slide 6
Discussions about EAP-RP
  EAP Extensions for the EAP Re-authentication Protocol (ERP)
  IETF RFC 5295/6696
  Applying to the cases where STA and the trusted third party already share a valid rRK (re-authentication Root Key)
    Based on an EMSK (512 bits) derived out of a previous full EAP authentication process.
    Do all of the EAP methods generate an EMSK necessary for the subsequent process EAP-RP as a result of successful full EAP authentication process?
    What happens to the EAP-RP session when the lifetime of the full-EAP Master key (MK) expires?
    What happens to EAP-RP Re-Authentication when there are several AAA servers in the network (typical deployment)?
  Allowing single-roundtrip re-authentication with an authentication server following an initial full EAP authentication

## Slide 7
Applying EAP-RP
Requirements for becoming EAP-RP capable
  At device/UE side:
    Requires STA to support EAP extensions, including: EAP-Initiate, EAP-Finish
  At network / infrastructure side:
    Requires AP and AS to support EAP extensions, including: EAP-Initiate, EAP-Finish
Current EAP-RP Capable Devices / network equipment
  Could not find any through public search.
  Current EAP-RP Applications and Standards
  adopted by 3GPP2 in the following UMB specification published in December of 2007:
    http://www.3gpp2.org/Public_html/specs/X.S0054-100-0_v1.0_071219.pdf
    http://en.wikipedia.org/wiki/Ultra_Mobile_Broadband
  Any networks, any trials, any deployment announcements:
    Could not find any through public search.

## Slide 8
Concerns with FILS Authentication with TTP
FILS Authentication with TTP: only based on EAP-RP
  EAP-RP is still pending to be adopted in devices/networks;
  EAP-RP applies to the STAs with valid security associations with a TTP.
For STAs with pre-established security association with a TTP
  Direct dependency on EAP-RP in both adoption time and scope
  Adoption time: only when or after EAP-RP is adopted
    How about the cases where people want to update AP/STAs to enable some quick improvement on the initial link setup time; but may not be ready to upgrade the network infrastructures to enable EAP-RP?
  Adoption scope: only where EAP-RP is adopted
    How about the applications / use cases where EAP-RP is not adopted?
    What if EAP-RP won’t be widely adopted?
For STAs without pre-established security association with TTP
  No help from the current FILS authentication schemes;
  Such STAs exist;
  Should 11ai consider improving initial link setup time for such STAs?

## Slide 9
Discussions on FILS Authentication with TTP
  Should 11ai consider any alternative / additional schemes?
  To fill in the potential gaps in the adoption time between FILS and EAP-RP;
  To cover the use cases where EAP-RP is not in use, e.g., in networks that are not EAP-RP capable;
  To cover the STAs to which EAP-RP is not applicable, e.g., the STAs without valid pre-established security associations with TTP;
  To allow solutions which have less impact on the requirements for device and infrastructure.

## Slide 10
Discussions on FILS Authentication with TTP –con’t
  If the answer is yes, then:
  For the STAs with valid pre-established security associations with TTP
    What’s the performance expectation?
    Can we still keep the same number of message exchanges as the current EAP-RP based FILS authentication schemes?
  For STAs without valid pre-established security associations with TTP
    Use Full EAP, any room for optimization?
    Any alternatives to using Full EAP?

## Slide 11: Straw Polls
Straw-Poll-1: Do you support to have further discussions in TGai to address the concerns listed in Slide 8 of this document about FILS authentication with TTP?
Result Yes No Abstain_______________

## Slide 12
References:
IEEE Std 802.11™-2012
Draft-P802.11ai_D0.5