## Slide 1: Compressed X.509 certificate for FILS authentication protocol
Name | Affiliations | Address | Phone | email
Robert Sun | Huawei Technologies Co., Ltd. | Suite 400, 303 Terry Fox Drive, Kanata, Ontario K2K 3J1 | +1 613 2871948 | Rob.sun@huawei.com
Date: 2013-4-1
Authors:

## Slide 2: Abstract
This document provides further discussions regarding FILS Authentication, for a comment submitted as a response to 802.11 WG Comment Collection 8 (CC8), on the question "Please provide comments on Draft P802.11ai D0.5".

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: Problem Statement
In some occasions, an oversized X.509 certificates or chained X.509 certificate will impose the fragmentation on EAP message during the FILS authentication/association, per RFC 2716 and RFC 5216.
Fragmentation of the Certificate is not ideally supported in FILS authentication in order to satisfy the performance purpose.
FILS authentication/association protocol are supposed to be over low-speed management frame and handshakes of the FILS authentication/association protocol is sensitive to the latency potentially caused by the size of the frame
It’s highly desirable to avoid verbose encodings that increase the size of the frame.
X.509 certificates could be much larger than the cryptographic data that they carry because the abundant optional fields.
Note: RFC 5216 , section 2.1.5 specifies that when fragmentation is needed, EAP-TLS must respond with a EAP-Response with EAP-Type=EAP-TLS with no data when the M bit is set. The EAP server must wait until it receives the EAP-Response before sending another fragment.

## Slide 5: Example of X.509 certificate
Samples:
  Version: 2 (X.509v3-1996)
  SubjectName: CN=Rob Sun [1365183108], DC=Rogers.com, DC=org
  IssuerName: CN=Rogers CA 2, DC=Rogers.com, DC=org
  SerialNumber: 09:AC:CE:3F:F9:26:77:15
  Validity - NotBefore: Fri Apr 05 13:31:55 2013 (130405173155Z)
  NotAfter: Sat Apr 05 13:31:55 2014 (140405173155Z)
  Public Key Fingerprint: 7966 3CF8 5A9D 7987 119F 6459 F13A C36D
  SubjectKey: Algorithm rsa (OID 2.5.8.1.1), Keysize = 2048
  Public modulus (no. of bits = 2048):
  0 FDE51BCC 03228165 C99EA8BF 40C0F9B6
  10 B5F09FCE 86C56290 6295F20C ED8BAB79
  20 0BD6CD42 A1B2396F E8CCCEEA E1AE3DB4
  30 3C2662D4 C9A285FE 5D70865D A5CF7F0A
  40 7EA6E561 3C2D6705 6D129DAB 06E8DD60
  50 E9AA0D25 307B1A9B 65BA69DD FE3B6798
  60 0A7FD425 D2521032 BD5D52B4 02950FFF
  70 0AD44079 14890720 25C29F68 3303181D
  80 F6763272 40BDB843 589E3D5C 123C8233
  90 654BB2EB 2E193FB7 232D38F1 AAB07712
  A0 20EA6ABB D905A71E 815A71CF 2E076520
  B0 3CB7A3A3 10147AB2 CF5F35E5 2613B460
  C0 35CA1C84 D4A95B76 9E3F8781 1ED10B40
  D0 91928E93 78CB48E7 FFF52D7F 31E3C2CE
  E0 25924F8F 75039BED F985FCF8 15F9CC46
  F0 55159D9A B3809F41 ACC9CD6F D031A59B
  Public exponent (no. of bits = 17):
  0 010001
  Certificate extensions:
  Private extensions:
  OID 2.206.5.4.3.2:
  PrintableString:
  |[Sun][Rob][RSA-2048][1365183108]|
  |[TEST] |
  SHA1 digest of DER code of ToBeSigned:
  0 16D3108A 7BE18C9C 6F9F9177 3EA14978
  10 9EFAFA57
  Signature: Algorithm sha1WithRSASignature (OID 1.3.14.3.2.29), NULL
  0 7A513F75 E3C5DDAC 96DD2F04 29C7B289
  10 E4261817 346898D7 740297A1 9A8AF59B
  20 68509D7F 0003ECA3 74031820 F134B0E8
  30 F4106532 831007AA 098C0558 35CD23BE
  40 667B963A 48A507CE 100426E9 E977AA95
  50 79E999B5 19922C27 E3DCA465 4033608B
  60 7603AE86 66C067DF E0CB3431 28E98306
  70 8FE83160 F1BA72B9 67C4439D 923DD471
  80 DC59A072 814557A0 C2CAFF99 E773C815
  90 35F89CCD 22ECD234 5A083B96 57177300
  A0 F7E4ED6E 0D3C512C B1A28C71 E231D590
  B0 7D4A3D2D 68DBC182 83AC8170 85144C90
  C0 59C33528 33DC6D48 86459C17 E1C3C619
  D0 646AA951 94163336 78806C3E 2BE28598
  E0 18E06BC2 763843CA CBC01332 6EFBC543
  F0 23D782EA E20A767C 7F52286C AFF0CB12
  Certificate Fingerprint (MD5): 90:31:20:FF:C2:94:DF:61:AD:30:22:03:18:23:A2:67
  Certificate Fingerprint (SHA-1): F630 34AF 1A6A 5826 B390 5B45 3F4F EBFF BAB5 521E

## Slide 6: Solution: Compress the X.509 certificate
Proposed solution: Compress the X.509 certificate based on Draft-pritikin-comp-x509-0
Detail of the scheme:
  X.509 certificates are often several kilobytes long, even though the cryptographic data that they carry is often no more than 512 bytes and can be as low as 64 bytes.
  The compression scheme is working on the indication of the public key type which indicates type 4 is the compressed X.509v3 format.
  Both STA and AP will agree on the certificate encoding scheme to be CXF (compressed X.509 Format)
  If FILS AP and STA are both capable of compressing the X.509 certificate, the STA will continue with the compression scheme as per the CXF format ( defined in the Draft-pritikin-comp-x509-0).
    Note: The CXF format will also applies to other types of certificates, i.e
    individual X.509 Signature Certificates
    PKCS #7 wrapped x.509 certificate
    a sequence of X.509 certificates that are concatenated together with no delimiters or other encoding (RFC 5246)
-

## Slide 7: Compression Efficiency
A X.509 certificate consists of multiple parts, except the Cryptographic data which are incompressible, the rest of parts are very suitable for compression
The compression ratio is claimed to be >0.32
( compression ratio = compressed size/uncompressed size)

## Slide 8: Compressed X.509 cert encoding scheme
Modify section
8.4.2.183 FILS public key element
The FILS public key element is used to communicate the device’s (certified) public-key for use with the FILS authentication exchange. The format of the FILS certificate element is shown in Figure <ANA-11> FILS certificate element.
Where the Key Type subfield is as follows:
0: Reserved
1: An X.509v3 certificate encoded according to RFC 5280.
2: A raw public key encoded according to RFC 5480
3: A raw public key encoded according to RFC 3279
4: A X.509v3 certificate with compressed encoding according to pritikin-comp-x509-0
 | Element ID |  | Length | Key Type | FILS public key
Octets: | 1 |  | 1 | 1 | variable
 |  | Figure <ANA-11>-- FILS public key element format(#1248) |  |  | 

## Slide 9: How it works in FILS authentication
Certificate based
FILS?
Start
FILS Frame construction
With CXF encoded Certificate
Note: Today’s 802.11 MAC Data Frame data
portion MTU =2043 Bytes before encryption
Y
Other types of
FILS authentication
N
Public Key Type= 4
FILS Frame construction
Over MAC MTU *
N
Next
Error “Frame is
over MTU !!!”
Y
Y
N

## Slide 10: Further Thinking
Can compression be also applied to HLD?
802.11 MAC Data Frame MTU is 2304bytes, if a FILS authentication frame is over this size, should it be a data Frame instead of management frame (Management frame is usually transmitted in low speed)?
Even though the fragmented X.509 cert could be handled per RFC 5216 section 2.1.5, the EAP ACK/NACK fashion of handshake for the fragmented X.509 imposes performance impairment. Would fragmentation really pay off in FILS ?

## Slide 11: Summary of the design
Memory storage and Frame size efficiency
Reduce the possibility of fragmentation of the FILS association frame is needed so that avoid modifying the whole FILS authentication protocol and potentially the security complexity.

## Slide 12: Motion
To instruct the editor to modify section 8.4.2.183 as shown in slide 8
Move:
Second:
Results: Yes/No/Abstain