## Slide 1: MAC Efficiency Analysis for HEW SG
Date: 2013-05-13
Authors:

## Slide 2: Introduction
Dense deployments of 802.11 STAs were discussed in WNG SC as usage models for HEW SG (see reference list)
  Wireless Office
  Cellular offload (home, corporate, hotspot)
  Residential / apartment building
  Shopping mall
  Airport waiting halls/lounges
  Stadium
  Lecture Hall
  Airliner / railroad car
802.11 MAC is based on contention based medium access.
This presentation analyzes 802.11 MAC efficiency for such dense deployment scenarios.

## Slide 3: MAC Overhead and Efficiency
RTS
CTS
A-MPDU
BA
pr
pr
pr
pr
SIFS
SIFS
SIFS
DIFS
CW (variable)
overhead
overhead
Actual data
A-MPDU
BA
pr
pr
SIFS
SIFS
overhead
TXOP
MAC efficiency increases as
    TXOP  fixed overhead (e.g. DIFS and SIFS)
    Number of BAs  aggregation overhead
    CW (or # of stations) + collisions  contention overhead
up to 64 subframes
Max A-MPDU size ~ 1MB
MAC throughput =
Total MAC payload (bits)
Time consumed for transmitting total MAC payload (sec)
MAC efficiency =
MAC throughput
PHY rate

## Slide 4: MAC Throughput with Contention
RTS
DIFS
CW=4
RTS
CTS
A-MPDU
BA
SIFS
DIFS
freeze
CW=2
SIFS
SIFS
RTS
CW=2
DIFS
DIFS
RTS
CW=2
SIFS
SIFS
DIFS
DIFS
RTS
CW=8
SIFS
CTS
A-MPDU
BA
SIFS
SIFS
SIFS
RTS
CW=10
freeze
TXOP
RTS
CTS
A-MPDU
BA
SIFS
DIFS
CW=2
SIFS
SIFS
DIFS
RTS
CTS
SIFS
DIFS
RTS
CW=8
SIFS
CTS
A-MPDU
BA
SIFS
SIFS
SIFS
STA-A
STA-B
Aggregate throughput: STA-A + STA-B
Overhead due to collision is shared by all the stations in the network
Collision overhead
When there is no collision between the stations, the station with the smallest CW will access the channel and thus CW overhead gets smaller as the number of stations increases
CWmax doubled
CWmax doubled
Actual data
overhead
overhead
Actual data
overhead
Collision overhead
*) CTS Timeout = SIFS + aPHY-RX-START-Delay + aSlotTime
CTS
CTS
Timeout*
CTS
Idle CW time slots

## Slide 5: Contention Analysis 1
Number of contending STAs: 1~100, 200
The collision probability increases as the number of STAs increases
Chart: 
| 1 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 200
Prob. Collision | 0 | 0.26459 | 0.36871 | 0.45929 | 0.50943 | 0.54572 | 0.57127 | 0.59496 | 0.61423 | 0.62906 | 0.64427 | 0.65745 | 0.74132
Chart: 
| 1 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 200
Num. of collisions per successful transmission | 0 | 0.35978 | 0.58406 | 0.84942 | 1.0385 | 1.2013 | 1.3325 | 1.4689 | 1.5922 | 1.6958 | 1.8111 | 1.9193 | 2.8658

## Slide 6: Contention Analysis 2
Idle slots during contention window
  The overhead due to idle time slots during contention windows decreases as the number of STAs increases
Chart: 
| 1 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 200
Idle CW slots | 7.512 | 5.8983 | 4.5666 | 3.8165 | 3.4742 | 3.2796 | 3.1298 | 3.0257 | 2.9453 | 2.8866 | 2.8178 | 2.7785 | 2.4796

## Slide 7: Simulation Setup for Single BSS case
AP
STA
1 AP, 1 ~ 50 STAs
Payload 1500 Bytes
A-MPDU: max 64 frames
  No limitation in size
TXOP = 1, 2, 3 mS
STA configuration
  2x2 MIMO, 40 MHz
Transmit power = 17dBm
PHY rate
  Maximum PHY rate = 270 Mbps
  Link adaptation enabled
  MCS feedback during RTS/CTS exchange
Channel model
  5GHz, TGn channel B
Simulation time: 10 seconds
Bi-directional traffic
25 meters

## Slide 8: MAC Efficiency
TXOP Limit = 3mS
As the number of STAs increases, MAC efficiency drops due to increased contention overhead
Chart: Number of STAs
| 1 | 10 | 20 | 30 | 40 | 50
Aggregated Goodput | 225.0504 | 209.2584 | 204.12 | 200.13 | 196.2144 | 194.202
Effective PHY Rate | 264.2158 | 262.9541 | 262.6391 | 262.4395 | 261.7326 | 261.4546
MAC efficiency | 0.85177 | 0.7958 | 0.77719 | 0.76258 | 0.74967 | 0.74278

## Slide 9: Medium Access Delay
Medium access delay increases as the number of STAs increases and the TXOP increases
STA1’s TXOP
STA2’s TXOP
STA1’s TXOP
Medium access delay
RTS, CTS, BA
A-MPDU
Chart: Number of STAs
| 1 | 10 | 20 | 30 | 40 | 50
TXOP 1mS | 0.0012739 | 0.01902 | 0.056308 | 0.07326 | 0.11296 | 0.13421
TXOP 3mS | 0.0033099 | 0.038366 | 0.10391 | 0.14571 | 0.22762 | 0.29243
Medium access delay is measured as shown in the following figure

## Slide 10: MAC Efficiency – Different TXOPs
MAC efficiency measured for different TXOP Limits:
  TXOP = 1, 2, and 3 mS
MAC efficiency drops as TXOP gets shorter due to increased fixed MAC overhead per TXOP
Chart: Number of STAs
| 1 | 10 | 20 | 30 | 40 | 50
TXOP 1mS | 0.62793 | 0.61082 | 0.60414 | 0.59751 | 0.58938 | 0.58573
TXOP 2mS | 0.79293 | 0.76598 | 0.75663 | 0.75141 | 0.74462 | 0.73902
TXOP 3mS | 0.85177 | 0.7958 | 0.77719 | 0.76258 | 0.74967 | 0.74278

## Slide 11: Overlapping BSSs Case
Setup
30 m
45 m
BSS1
Aggregated Goodput | Average PHY rate | MAC efficiency
30 Mbps | 81 Mbps | 37 %
Each BSS has 30 STAs
Number of APs = 7
Number of STAs per BSS = 30 STAs
  Total number of STAs = 210 STAs
TXOP = 3 mS
Simulation time = 7 seconds
2.4 GHz
Other parameters are same as the single BSS case (shown in slide 7)
MAC efficiency measured at BSS1
Average medium access delay = 648 mS
Increased interference and contention from overlapping networks lowers MAC efficiency

## Slide 12: Summary and Next Steps
Dense deployment scenarios have been discussed for HEW SG
802.11 MAC efficiency is analyzed for dense deployment scenarios
  MAC efficiency drops as STA density increases
SG needs to define metrics to measure QoE
  Minimum required average (or CDF) throughput per STA
  Maximum medium access delay
  Average area throughput
  …
Investigate existing features in other task groups (11aa/ac/ad/ah/…) to see how those features affect PHY/MAC efficiency in dense deployment scenarios
  HCCA (scheduling), 11aa OBSS management, 11ac MU-MIMO, etc.

## Slide 13: References
https://mentor.ieee.org/802.11/dcn/13/11-13-0331-05-0wng-high-efficiency-wlan.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-0287-03-0wng-beyond-802-11ac-a-very-high-capacity-wlan.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0343-00-0wng-operator-oriented-wi-fi.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0309-00-0wng-next-gen-wlan.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0313-00-0wng-usage-models-for-next-generation-wi-fi.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0314-00-0wng-on-future-enhancements-to-802-11-technology.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0113-00-0wng-applications-and-requirements-for-next-generation-wlan.pptx
https://mentor.ieee.org/802.11/dcn/13/11-13-0514-00-0hew-usage-scenarios-and-applications.pptx