## Slide 1: Phase Rotations for 1MHz DUP Mode
Date: 2013-05-13
Authors:

## Slide 4: Background and Problem
In 802.11ah, a 1MHz Duplicate frame format is being adopted
  Refers to a 2/4/8/16 MHz frame, which contains 2/4/8/16 replicas of a 1MHz frame in each 1MHz frequency segment of the transmission BW.
  Such frames have many uses
    E.g., being able to clear the medium for a higher than 1MHz transmission
Duplication in frequency can cause a sharp increase in PAPR of the overall waveform
  Higher PAPR forces the device to operate at a higher PA back-off
    To avoid signal distortion as well to avoid violating the spectral mask
  Higher PA back-off leads to a lower power added efficiency of the PA

## Slide 5: Solution
To reduce PAPR of 1MHz DUP mode frames, we propose multiplying each 1MHz sub-band by a factor drawn out of the set {1, -1, j, –j}
  Proposal uses similar methodology as 11ac
    11ac had 20MHz DUP frames which needed similar phase rotation sequences
  Optimal sequences chosen to balance the PAPRs of LTF, random MCS0 data and random MCS10 data
Sequences shown on next slide

## Slide 6: Sequences Proposed
Data PAPR corresponds to 5e-3 point of the PAPR CCDF
Always kept LTF PAPR much lower than data PAPR
A little higher LTF PAPR was allowed for avoiding very high PAPRs in data
A little increase in data PAPR was allowed for achieving a big reduction in LTF PAPR
Bandwidth in MHz of the 1MHz DUP Frame | Phase rotation sequence based on balancing the PAPR of LTF, MCS0 data and MCS0 rep 2 data | 
 | Best Sequence | PAPR with best sequence (dB) (LTF, MCS0 data, MCS0 rep2 data)
2 | [1 -1] | (6.59, 11.65, 12.09)
4 | [1 j -j -1] | (6.59, 11.58, 11.81)
8 | [1 -1 1 1 1 1 -1 -1] | (5.60, 11.68, 12.94)
16 | [1 1 1 -1 1 1 1 -1 -1 -1 1 -1 1 1 -1 1] | (6.021,11.89,13.05)

## Slide 7: Conclusion
We proposed phase rotation sequences for 1MHz DUP Frames in 11ah
  The sequences were chosen to balance the PAPRs of LTF, and random MCS0 (with and without repetition) data

## Slide 8: Pre-motion 1
  Do you agree to adopt phase rotation sequences for 1MHz DUP mode proposed on slide 6 for 2, 4, 8 and 16 MHz BWs?

## Slide 9: Motion 1
  Move to adopt phase rotation sequences for 1MHz DUP mode proposed on slide 6 for 2, 4, 8 and 16 MHz BWs?