## Slide 1: FILS Piggy-Backing Aspects
Date: 2013-05-15
Authors:
Name | Company | Address | Phone | email
René Struik | Struik Security Consultancy | Toronto ON, Canada | USA: +1 (415) 690-7363 Toronto: +1 (647) 867-5658 Skype: rstruik | rstruik.ext@gmail.com
Note: Material extracted from 13/201r8

## Slide 2: FILS Key Establishment
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
online/offline assistance
with authentication
FILS key establishment protocol options provided:
FILS Authentication with TTP, based on ERP
(two flavors: with or without “PFS” (ERP+ECDH, resp. ERP)  see next slides)
Authentication without online TTP, based on ECDH and ECDSA certificate
Slide source: 13/324r0

## Slide 3: Adding “piggy-backed info” to protocol flows …
STA
AP
Association Request
Beacon/Probe Resp.
Authentication Request
Authentication Response
Association Request
Key
Establishment
Key
Confirmation
TTP
Services
+ piggy-backed info response
+ piggy-backed info request
Authentication help
Configuration help
IP address assignment
Authorization
Subscription
credentials
Piggy-backing info along FILS authentication protocol:
Higher-layer set-up, including IP address assignment
Authorization functionality, subscription credentials, etc.
See details elsewhere in presentation
Slide source: 13/324r0

## Slide 4: FILS Security Status
Current Status:
Three FILS authentication protocol options specified:
  FILS Authentication with Trusted Third Party
  FILS Authentication with Trusted Third Party and “PFS”
  FILS Authentication without Trusted Third Party
Main differences:
  Different trust assumptions
  Different assumption on “pre-existing” system set-up
  Different assumptions on online availability of the “backbone network”
Common elements:
  All have only four protocol flows
  All implemented via Authentication/Association Request/Response frames
  All allow piggy-backing of other info along Association frames
  (e.g., IP address assignment)
Current Work in Progress:
How to deal with large objects (e.g., certificates, higher-layer data objects)
How to specify main piggy-backing details (e.g., on IP address assignment)
Slide source: 13/324r0

## Slide 5
Questions
1. How to deal with large objects (e.g., certificates, higher-layer data objects)?
Intra-frame fragmentation. DISCUSSED ELSEWHERE
How to handle large objects that fit within a single frame
Inter-frame fragmentation. DISCUSSED ELSEWHERE
How to fragment FILS frames, if these become too long due to large objects
2. How to specify main piggy-backing details (e.g., on IP address assignment)?
Flexibility re AEAD authenticated encryption mode. DISCUSSED HERE
Authentication and potential encryption of piggy-backed information

## Slide 6
Authenticated Encryption (1)
General mechanism
After AEAD protection
Now with Information elements:
or...
or...
Main problem: How to pinpoint the portions that are encrypted? (only problem for recipient)
Header
Payload
Header
Secured Payload
Authentication of entire frame
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
Encrypted segments starts here

## Slide 7
Authenticated Encryption (2)
How to pinpoint the portions that are encrypted? (only problem for recipient)
Recipient can easily find this “L”-symbol: simply retrieve from leftmost 2 octets
Does this also work for other “encryption ON/OFF” combinations?
YES! Exploit structure in IEs: encryption/decryption is essentially on “unordered” set of IEs.
(This Option #3 is not discussed any further – see 13/201r6)
0
7
1
3
4
6
5
8
9
A
0
7
1
3
4
6
5
8
9
A
L
5
1
6
7
8
0
9
3
4
A
“L”
2
L
“L”

Encryption length indicator
(2 octets)

## Slide 8
Authenticated Encryption (3)
Options:
1. No flexibility. Always encrypt FILS Association Request/Response “body”
2. Some flexibility. Allow only encryption of “first chunk”…
No re-ordering of IEs at all.
3. Full flexibility. Allow encryption of any chunks, as set by senders policy…
Potential re-ordering of IEs “under the hood”. Put “right” as part of AEAD routine.
Details in 13/582r2.
Option #2 in 13/582r3.
Header
Secured Payload
Header
Secured Payload
Visible Chunk
“L”
Header
Secured Payload
Visible Chunk
“L”

## Slide 9
Authenticated Encryption – Straw Poll
  Implement flexible encryption scheme as specified in 13/582r3:
  Facilitate Option #2 of previous Slide (#22).
  For clarity: This only applies to FILS Association frames
Yes
No
“Don’t Care”
Need more information
Result:

## Slide 10
Authenticated Encryption – Motion
Instruct the editor to incorporate changes to D0.5, as indicated in 13/582r3
Yes
No
Abstain
Result: Y/N/A