## Slide 1: Usage models and requirements for IEEE 802.11 High Efficiency WLAN study group (HEW SG) – Liaison with WFA
June 2013
Laurent Cariou (Orange)
Slide <number>
Date: 2013-06-05
Authors:
Notes: doc.: IEEE 802.11-12/xxxxr0
June 2013
        Osama Aboul-Magd (Huawei Technologies)
Page <number>

## Slide 2: Abstract
June 2013
Slide <number>
Laurent Cariou (Orange)
As part of the effort to develop a PAR and 5C for High Efficiency WLAN (HEW), the IEEE 802.11 Working Group is interested in input from the WFA on prioritization of usage scenarios and requirements.
As input to the WFA, this document gathers the main use cases and requirements that have been discussed in HEW SG.

## Slide 3: Context: Creation of HEW SG in IEEE 802.11
Slide <number>
Laurent Cariou, Orange
June 2013
Genesis of HEW SG
On March 22, 2013 the IEEE 802 EC approved an 802.11 request to create a new Study Group called High Efficiency WLAN (HEW).
  Request approval by IEEE 802 LMSC to form an 802.11 Study Group to consider High-efficiency WLAN [as described in documents 11-13-0331r5 and 11-13-339r10] with the intent of creating a PAR and five criteria.
  Do you support starting a new study group called “high efficiency WLAN” to enhance 802.11 PHY and MAC in 2.4 and 5GHz with a focus on:
    Improving spectrum efficiency and area throughput
    Improving real world performance in indoor and outdoor deployments
      in the presence of interfering sources, dense heterogeneous networks
      in moderate to heavy user loaded APs
Notes: doc.: IEEE 802.11-11/1507r1
November 2011
        Stephen McCann, RIM
Page <number>

## Slide 4: Context: HEW SG main drivers
Increased usage of mobile devices
 most environments will become characterized by a high density of STAs and/or BSSs
  User demand for WIFI anytime and everywhere pushes its deployment/usage in new environments characterized by a high density of STAs and BSSs
    hotspots in airport/train stations, malls, stadium, parks, streets, campus
  Increased usage of WIFI leads to an increased density in “traditional” WIFI environments as well
    home (dense apartments buildings), entreprise (generalization of P2P links)
  2.4GHz already congested, and likely 5GHz to be congested soon
 growing use of WIFI outdoors
  parks, campus, street deployments
  coverage of special outdoor events
New WIFI applications
  per user real-world throughput need regularly growing (higher resolution video more demanding in throughput)
  cloud services generating more Uplink traffic
  more and more peer-to-peer applications
HEW aims to achieve a very substantial increase in the real-world throughput achieved by each user in such scenarios
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 5: HEW SG scope
Improve MAC and PHY for operations in networks with high density of STAs and/or BSSs that potentially interfere with each other
  There is much evidence of issues due to OBSS/dense deployments
    Insufficient per-user throughput for common applications
  MAC/PHY operations of current 802.11 is not designed/optimized for efficient OBSS and dense network operation
  Solutions to these issues will have a broad sets of applicability
Improve MAC and PHY for operations in new indoor and outdoor environements
By improve, we mean achieve a very substantial increase in the real-world throughput achieved by each user in such scenarios
  Creating an instantly recognizable improvement in Quality of Experience of the major use cases and generating spatial capacity increase (area throughput)
Provide such improvements both in 2.4 and 5GHz.
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 6: HEW SG scenarios
In the following slides, we present a list of usage models that have been identified so far in HEW SG
  WFA is asked to provide market priorities for these usage models
For clarification, we sorted them by the types of requirements that they would induce
  note that this classification is not a priorization
the main usage models defined for 802.11ac should also be taken into account, assuming adaptation with the evolution in throughput and regarding densification of STAs and BSSs
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 7: Usage model terminology
June 2013
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 8: Terminology
June 2013
Usage Model – A usage model is the combination of all the things below; not to be confused with a use case which is the specific set of steps to accomplish a particular task.
Pre-Conditions – Initial conditions before the use case begins.
Application – A source and/or sink of wireless data that relates to a particular type of user activity. Examples are streaming video and VoIP.
Environment – The type of place in which the network of the use case is deployed, such as home, outdoor, hot spot, enterprise, metropolitan area, etc.
Traffic Conditions – General background traffic or interference that is expected while the use case steps are occurring. Overlapping BSSs, existing video streams, and interference from cordless phones are all examples of traffic conditions.
Use case – A use case is task oriented. It describes the specific step-by-step actions performed by a user or device. One use case example is a user starting and stopping a video stream.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 9: Usage Model Environments
June 2013
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 10: Environments
June 2013
Enterprise
  On desk and in cubicle (short range, line of sight)
  Conference room (medium range, mostly line of sight)
  Dense deployment
Small Office
  Single BSS with unmanageable interferences and limited number of users
Hotspot in public places
  Transportation Hub (Airport, Train Station, Bus Station)
  Exibition halls, Shopping malls
Outdoor hotspots
  park, streets, stadium, special crowded events
  co-location with cellular base stations (small cell deployments) in dense zones
Home
  dense apartment buildings
Campus (Educational space, Hospital)
  Auditorium/lecture halls/classrooms in the educational space
  Video conferencing/tele-presence
  Hospitals where Remote Medical Assistance for Operations is via Wireless Networks
Airplane/Bus/Train/Ship
  Intra-large-vehicle communication, where a large vehicle can be an airplane, bus, train or ship
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 11: Environments
June 2013
Most environments are characterized by the overlap, in the same area, of multiple WiFi networks that need to cohabit efficiently and fairly.
Different types of networks that overlap:
  one or multiple cluster of APs (ESS), each of these ESS are managed by a controller
  one or multiple stand-alone APs (home, shops private APs…), each of them with their own private management entity
  one or multiple single-link networks for P2P communications (tethering, miracast…)
We can talk about “heterogeneous networks” which refers to an environment with diverse management entities
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 12: Applications
June 2013
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 13: New/enhanced applications for consideration
June 2013
Wireless docking
Unified Communications - Including Video conferencing
Display Sharing - 1-to-1 (Miracast), 1-to-many (classroom, medical), Many-to-1 (security)
Cloud Computing - including VDI (Virtual Desktop Infrastructure)
Video distribution at home – new video resolution (VHD, UHD)
Progressive Streaming
User Generated Content (UGC) Upload & Sharing
Interactive Multimedia & Gaming
Real-time Video Analytics & Augmented Reality
Support of wearable devices
Scenarios are characterized by a mix of traffic that are more and more heterogeneous (from very low to very high throughput, latency/no latency constraints…)
A general trend is the increase of applications requiring Uplink traffic
A high proportion of this traffic is due to cellular offloading
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 14: List of usage models
June 2013
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 15: Usage models classified by requirement characteristics
June 2013
Slide <number>
1 | high density of APs and high number of STAs per AP | a | stadium
 |  | b | airport/train stations
 |  | c | exhibition hall
 |  | d | shopping malls
 |  | e | E-Education
 |  | f | Large-scale deployment with high density in City Square/Hot Spot
2 | high density of STAs | a | dense wireless office
 |  | b | public transportation
 |  | c | lecture hall
3 | high density of APs (low/medium number of STAs per AP) | a | dense apartment building
 |  | b | Community WiFi
4 | new outdoor deployments | a | Very dense urban Street – Public Access
 |  | b | Pico-cell street deployment – Public Access
 |  | c | Cellular offload - co-site offloading
5 | single-link throughput increase | a | surgery/health care (2e from 11ac)
 |  | b | production in stadium (similar to 1d-1e from 11ac)
 |  | c | smart car
Laurent Cariou (Orange)

## Slide 16: 1
high density of APs and high number of STAs per AP
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 17: 1a Usage in Stadium - Public
June 2013
Pre-Conditions
High density users have operational WLAN network for Internet access. The traffic is bursty in time and is uneven according to different users' participation in physical space.
Environment
Open area with few obstacles and single/multiple operators’ deployed multiple APs. Most of the transmissions are LOS and the layout of APs are frequently changed.
High density of users (0.5users/m²), inter-AP distance between 12 and 20 meters.
Applications
200 users at 20 Mbps best effort accessing the internet for recreational content
Users are following ESPN event or similar blog as supplemental event content.
Users are receiving VHD video feed highly compressed (100Mbps)
Peer-to-peer link for tethering
User Generated Content (UGC) Upload & Sharing
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference with unmanaged networks (P2P)
Interference with Bluetooth
Use Case
Users are attending an event in an outdoor stadium.
Users access the internet for recreational content, supplemental event content (e.g., game stats), and live video and/or audio event content (e.g., various live camera feeds).
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 18: 1b Public Access – Airports and Train Stations
June 2013
The Next Generation Wi-Fi is expected to provide very high capacity for the people using bandwidth consuming applications in a dense deployed environments.
streaming video
Talking over
video phone
VPN access to the office
Airports and train stations are typical places where many service providers install their APs and many passengers use WLAN services.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 19: 1b Public Access in Airport/train stations
June 2013
Pre-Conditions
High density users access internet through multiple operators’ WLAN network. The venue owner possibly manages or controls multiple operators’ WLAN networks uniformly for the purpose of users’ QoS.
Environment
The environment is very complex and June suffer severe interference.
Each AP serves 120 users in a 200m2 area. The inter-AP distance is in the range of 15~20m. Single/multiple operators.
Applications
Video based applications: TV, VOD, Video conference; VHD highly compressed (100 Mbps): 50% of users
VPN applications (20 Mbps): 10% of users
Game online; 100 Mbps, < 100 ms jitter; < 100 ms latency: 10% of users
Internet access: email, twitter, web surf, IM. (20 Mbps): 30% of users
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with unmanaged networks (P2P)
Use Case
Travelers are using the network to surf websites, watch movies, play online games and access cloud services.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 20: 1c Public Access – Exhibition Hall
June 2013
People access the digital contents such as demonstration and promotion video files that the exhibitors prepared from the exhibitors’ APs or from the APs provided by the event coordinator. People also access the internet to see exhibitors’ web sites, to send reports to the companies, etc.
VPN access to the office
Exhibition halls are another example of high density deployment use cases. There June be many WLAN networks installed be the exhibitors and event coordinator.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 21: 1c Public Access in an Exhibition Hall
June 2013
Pre-Conditions
High density users access internet and local contents prepared by the exhibitors. Exhibitors June have their own APs installed or use the shared AP that the event coordinator.
Environment
There will be many APs and STAs and June suffer severe interference. Each AP serves 100 users in a 100m2 area. The inter-AP distance is in the range of 5~10m.
Applications
Video based applications: VOD, Contents Downloading; VHD highly compressed (100 Mbps) : 60% of users
VPN applications; Contents (Picture) Uploading; Internet access: email, twitter, web surf, IM. (20 Mbps): 40% of users
User Generated Content (UGC) Upload & Sharing
Traffic for wearable devices
Traffic Conditions
Interference between APs belonging to the same managed ESS due to high density deployment.
Interference with stand-alone APs in the exhibition booth.
Interference with unmanaged networks (P2P)
Use Case
Users June download the digital contents such as demonstration and/or promotion video files to their laptops or tablets. Users also access the internet for event content, surf website, and send emails.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 22: 1d Shopping Mall
Internet access
Push, data download (coupons)
Indoor location
Cellular offload
Multicast
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 23: 1d Shopping malls
June 2013
Pre-Conditions
High density users access internet through multiple operators’ WLAN network (one from the venue owner and possibly others).
Private WLAN networks in each shops/restaurants.
Environment
Indoor multi-floor location, composed of large open-spaces surrounded by shops and restaurants.
High density of users and high density of APs.
Applications
Classical public access traffic mix: web browsing, online gaming, cloud-based synchronization and highly compressed web video
More specific applications: Push, data download (coupons), Indoor location, Multicast
Traffic Conditions
Strong interference between overlapping networks (managed WLAN network deployed by the owner (ESS) and private WLAN networks deployed in shops and restaurants (stand-alone APs).
Use Case
Shoppers are using the network to localize themselves in the mall and receive coupons ((potentially with augmented reality). As for classical public access, users also use the network to surf websites, watch movies, play online games and access cloud services.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 24
June 2013
1e e-Education
Scenario Characteristics:
  Dense STAs (40~60 STAs) in one classroom with one AP
  20~30 classrooms in one typical school building (3~6 floors)
  Thus, nearby 1,000 STAs with 20~30 APs within a building space.
Typical education applications:
  Video streaming among teacher and students;
  Teachers/Students demonstrate theirs desktop to others;
  File transfer and sharing;
  4+ subgroup in one classroom with multicasting traffic for screen sharing or video;
  Throughput Requirement: longtime/stable throughput in one classroom >= 20 Mbps
Challenges and Issues:
  Fast Connection: Very long STAs registering time (1~5 minutes) delay the start of a class;
  Interference Control and Delay Optimization:
    Annoying lag in screen sharing, video streaming and command response (sometimes it is longer than 20 seconds)
    Very low bandwidth for e-homework submission in the same period.
Slide <number>
Laurent Cariou (Orange)

## Slide 25: 1e e-Education
June 2013
Pre-Conditions
WLAN is deployed in a each classroom of a campus in order to provide communication tools for e-Education.
Environment
Dense STAs (40~60 STAs) in one classroom with one AP. 20~30 classrooms in one typical school building (3~6 floors).
Nearby 1,000 STAs with 20~30 APs within a building space.
Applications
Video streaming among teacher and students;
Teachers/Students demonstrate theirs desktop to others;
File transfer and sharing;
4+ subgroup in one classroom with multicasting traffic for screen sharing or video;
Throughput Requirement: longtime/stable throughput in one classroom >= 20 Mbps
Traffic Conditions
Interference between APs in different classrooms belonging to the same managed ESS due to high density deployment.
interference with peer-to-peer networks within each classroom.
Use Case
e-Education starts in multiple classrooms simultaneously.
Teacher/students demonstrated their desktop to others, video or screens are shared.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 26: 1f Super-dense STAs in City Square/Hot Spot
June 2013
Slide <number>
At an outdoor/indoor open area, huge number of pedestrians are attending a big event with smart phones at their hand for downloading streaming video on-line and uploading their own-taken/created video/picture at the very spot to YouTube (without any delay) to share with others.
Street Supporting in Word Cup 2002
PSY’s Performance Outdoor
Man. United’s Street Parade
Laurent Cariou (Orange)

## Slide 27: 1f Large-scale deployment with high density in City Square/Hot Spot
June 2013
Slide <number>
Pre-Conditions
Super density users access internet through multiple operators’ WLAN network.
Street or hot spot in the city possibly manages or controls multiple operators’ WLAN networks, but there are also many private AP’s there.
Environment
The environment is very complex and June suffer severe interference.
There are 100,000 users in a 1km2 area. 400 AP’s are deployed in an non-uniform way which belong to multiple operator’s WLAN networks. The inter-AP distance is in the range of 25~75m. Single/multiple operators and some private AP’s.
Applications
For each AP, video based applications: TV, VOD, HD compressed (20 Mbps): 50 users
Internet access: email, twitter, web surf, IM. (10Mbps): 200 users
Real-time Video Analytics & Augmented Reality
User Generated Content (UGC) Upload & Sharing
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with stand-alone private APs from surrounding buildings.
Interference with unmanaged networks (P2P)
Use Case
Huge number of pedestrians are using the network to surf websites, watch movies, play games and access cloud services and upload their own created contents to YouTube to share with others without any delay.
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 28: 2
high density of STAs
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 29: 2a Wireless Office
June 2013
Pre-Conditions
User has operational WLAN network for Internet and cloud access. User and devices are within a densely deployed WLAN access network for a single or multiple administrative domains. The wireless network used for cloud desktop June or June not be part of the other operational WLAN network.
Environment
Devices are operating in close proximity in a multi-cubicle office. Transmissions are mostly LOS. Multiple APs per floor. Typical distances between STAs and AP in the room are < 50m. 20-30 STAs per AP.
Applications
Cloud based applications supporting VDI (Virtual Desktop Infrastructure) access and VHD video streaming.
Cloud-based VDI requirements are: 100 Mbps, best effort.
Video requirements are: ~600Mbps, jitter is <20 ms, delay is < 20ms, 1.0E-7 PER.
Peer-to-peer communications (WiFi direct and display)
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple entreprise in the same building.
Interference with peer-to-peer networks.
Use Case
An user starts his online interactive video training on a fixed or mobile device with VHD display.
User connects to the training server in the cloud.
The server streams the video in VHD format with interactive content.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 30: 2b Public Transportation
June 2013
Slide <number>
Pre-Conditions:
High density users have operational WLAN network for Internet access during very crowded time such as commuting time. User can access the onboard entertainment system (internal) and Internet (external).
Environment:
Indoor open area with many obstacles most of which are human body blockings. Each cabin has separate WLAN connectivity for subway cabin. For bus, there is a single cabin. People can be slowly moving in the cabin.
Application:
Onboard entertainment: Broadcast and local VoD services, Internet Access, Gaming, public safety: Local VoD services, monitoring: 50 x 20 Mbps = 1.0 G
25 users listening to HD audio
25 users doing interactive gaming ; 25 x 20 Mbps = 0.5 Gbps, <100 ms jitter and <100 ms latency
Traffic Conditions
Potential interference from traffic in the surrounding outdoor environment for public transports in cities.
Use Case
100 passengers in one cabin (10 m x 3m).
Passengers access via WLAN the onboard the entertainment system for video display, audio, and interactive gaming activities.
Passengers also access the Internet via the WLAN.
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 31: 2c Campus Network - Lecture Halls
June 2013
Pre-Conditions
An operational WLAN network is used for mass “tele-presence” or interactive demo events. Lecture hall is connected remotely through a high speed link to the actual person/people doing the presentation. The WLAN also provides internet service to the users.
Environment
Mostly open indoor space of ~100meters by 100meters. Mostly LOS with a few obstacles such as partitions and people. Max distance between end-points ~200 meters.
Applications
Lecture is delivered remotely using tele-presence multimedia applications. The lecture is delivered to the projector in the lecture hall over the campus WLAN network. Reciprocal video of the lecture hall is delivered to the remote lecturer over the campus WLAN network. Supplemental information is made available using internet access.
Tele-presence requires 2x3.6 Gbps for 3D UHD lightly compressed
Internet traffic (20 Mbps): 150 users.
Traffic Conditions
Potential interference from overlapping networks (e.g. neighbors, other WLANs). Data transfers and video display should be operational simultaneously.
Use Case
A professor remotely delivers a lecture to 300 students gathered in a lecture hall. The lecture includes both real-time video of the professor and supplemental video content as she conducts the lecture.
The professor receives reciprocal video of the students gathered in the lecture hall and has the ability to pan and zoom to view the audience.
Students are simultaneously using wireless devices to access supplemental material via the internet.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 32: 3
high density of APs (low/medium number of STAs per AP)
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 33
June 2013
3a Dense apartment building
Pre-Conditions
Each apartment has Wi-Fi network deployed to access internet and cloud services. In each apartment up to 3 users stream concurrently video content from the network and up to 50% of the networks are active.
At the same time each of the active Wi-Fi networks is used by 2 users for web browsing
Environment
Building with 100 apartments. One AP in each apartment of 10mx10m randomly positioned. 5 STA per AP randomly positioned in the apartment.
Applications
Cloud based applications supporting video streaming with 8k resolution.
Video requirements are: ~112Mbps per STA (16x1080P), delay is < 200ms, 1.0E-3 PER.
The application is able to buffer up to 2s of the content to avoid interruptions of the service, allowing relaxed delay requirements
Web browsing requirements for Social Networking are: ~20Mbps, PER 1e-3, delay<50ms
150 active video users and 100 active web browsing users in the building with an aggregate data rate requirement of 18.8Gbps in the building.
The service requirements should be met for 98% of the users in the building.
Traffic Conditions
Strong interference from unmanaged overlapping networks (neighboring apartments, and outdoor Wi-Fi network).
Multiple video display are operational simultaneously.
Interference with Zigbee, Bluetooth
Use Case
User starts cloud video service on a fixed or mobile device with 8k display.
The cloud service streams the video in 8k format.
Slide <number>
Laurent Cariou (Orange)

## Slide 34: 3a Home (should be merged with slide 33)
June 2013
Pre-Conditions
Many WLAN networks installed by the home users operate in high density environment (overlapping each other). Home users have a variety of terminals such as TV, PVR, PCs, tablets and game terminals and access the personal cloud services and/or SNS over the WLAN.
Environment
Most of the home users have one or more WLAN APs. Distance between two APs ranges from 5 to 20 m and the WLAN areas overlap each other.
Applications
Video Stream (from cloud or YouTube etc.)
Video chat or VoIP (smart phone)
Online game
Cloud-based application as big storage
web browsing?
Traffic Conditions
Potential interference from overlapping networks (e.g. neighbors, other WLANs). Data transfers and video display should be operational simultaneously. Consideration for QoS for the streaming applications such as VoIP and high quality video will be needed.
Use Case
Users watch the high quality video contents coming from the Internet or video contents stored in their PVR with VHD Display. There June be another video streams to be recorded in the Blu-ray deck.
People enjoy playing online games or local game machine with two or more people.
There June be other users just accessing the Internet for email access, web browsing, etc.
Tele-work using VPN
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 35: 3b Community WiFi
Slide <number>
Home private APs used as hotspots
  Private SSID for home users and public SSID to offer public access in the vicinity
Private
Public
Home APs used as Hotspots
Coffee shop
July 2012
Laurent Cariou, Orange

## Slide 36: 3b Community WiFi
June 2013
Pre-Conditions
Many WLAN APs installed by the home users operate in high density environment (overlapping each other). Those WLAN APs have a private SSID for home/apartment users and a public SSID for public hotspot usage.
Environment
A street surrounded by neighboring buildings where a high number of APs are operating.
A building with a coffee shop/restaurant in the ground level and many APs operating in the apartments’ upper floors.
Density: 20 APs per channel accessible at BSS edge by hotspot clients in the street or coffee shop.
Applications
Typical hotspot traffic:
mix of web browsing, online gaming, cloud-based synchronization and highly compressed web video
Traffic Conditions
Some proportion of traffic on private SSID by home users.
Interference between private and public traffic.
Use Case
Users in street and coffee shop connect to community WIFI hotspots, watch web video, play online gaming, perform UL/DL synchronization, or do web browsing.
Some users are in mobility, walking or driving down the street.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 37: 4
new outdoor deployments
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 38: 4a Very dense urban Street – Public Access
June 2013
Pre-Conditions
High density users access internet through multiple operator’ WLAN network. The traffic is bursty in time and is uneven according to different users' participation in physical space.
Environment
Outdoor with many obstacles and single/multiple operators’ deployed multiple APs. The inter-AP distance is in the range of 10 ~ 20m. User distribution density is about 0.5~ 1 user/ m2.
Applications
Assume that there are 100 users per a AP: total 3.6 Gbps is required with low mobility supporting.
- 20% users: Video based applications (TV, VOD): UHD (4k*2k) highly compressed. 100 Mbps *20= 2Gbps.
- 20% users: Game online: 20 Mbps * 20 = 0.4 Gbps.
60% users: Internet access (email, twitter, web surf): 20 Mbps * 60= 1.2Gbps.
User Generated Content (UGC) Upload & Sharing
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with stand-alone private APs from surrounding buildings.
Interference with unmanaged networks (P2P)
Use Case
Users are walking on GangNam street in Seoul, Korea.
Users see some high-quality video clips and access the internet to surf websites, watch Youtube, listen music streaming, play online games and/or chat with friends. QoE needs to be guaranteed as user is moving. Services are seamlessly continued through cellular and WLAN.
* A operator’s WLAN networks in GangNam (each 500x700m)
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
John Doe, Some Company
Page <number>

## Slide 39: 4b Pico-cell street deployment
June 2013
Pre-Conditions
Street deployment for cellular offload purpose (co-location with cellular network small cells) or for city neighborhood blanket coverage.
Environment
Most outdoor street deployments will be made with placement below rooftop (3 - 10m: typical location of cellular network pico cells): lamp poles, hanged on cables, stuck to walls. It will be mostly side coverage (omni or directional).
Inter-AP distance between 150 and 200 meters for blanket coverage. Shorter distance in higher density zones.
Applications
User traffic mix is similar to cellular traffic mix.
Mix of VOIP, Best effort FTP, Internet access, Web video, teleconferencing.
Throughput Requirement: longtime/stable throughput per user >= 20 Mbps
Real-time Video Analytics & Augmented Reality
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with stand-alone private APs from surrounding buildings. (at 2.4GHz, between 15 to 20 APs in all 3 channels (beacons already occupy 20% of channel)
Interference with unmanaged networks (P2P)
      Interference with 2G-3G-LTE in case of co-site deployments
Use Case
Users connect to hotspot, perform a mixture of applications, including VOIP calls, FTP, Internet access, video conference…
Some users are in mobility (walking down the street).
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 40: 4c Cellular Network – Co-site Offloading
June 2013
Interactive real-time gaming: 20% of users. (100 Mbps, <100 ms jitter and <100 ms latency)
Traffic Conditions
Interference between APs belonging to the same managed ESS due to very high density deployment.
Interference between APs belonging to different managed ESS due to the presence of multiple operators.
Interference with stand-alone private APs from surrounding buildings. (at 2.4GHz, between 15 to 20 APs in all 3 channels (beacons already occupy 20% of channel)
Interference with unmanaged networks (P2P)
      Interference with 2G-3G-LTE in case of co-site deployments
Use Case
Users perform a mixture of applications, including VOIP calls, FTP, Internet access, video conference, inter-active real-time gaming.
Cellular BS offloads part/all of the traffic to the co-site WLAN AP for the specific users.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 41: 5
single-link throughput increase
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 42: 5a Health Care - Remote Surgery
June 2013
Pre-Conditions
Remote diagnosis and treatment involving video, audio and data interaction. Video sourced from the surgery room and sent to the remote offices is uncompressed. Video sourced from the remote offices and sent to the surgery room is lightly compressed.
Environment
Indoor hospital surgery room of 20 by 20 meter at one end, an office room of 10x10 meter to 40x40 meter coverage at the remote end. There are some unmanageable interference around both ends.
Applications
Surgery is shared remotely using tele-presence multimedia applications. The remote doctors consultation is shared to the surgical theatre using tele-presence multimedia applications. Supplemental information is made available using cloud and internet access. The remote doctors exercise remote access and control of surgical theatre equipment via the Internet.
Tele-presence requires 3.6 Gbps for 3D UHD lightly compressed; and 10x600 Mbps VHD.
10x100 Mbps internet connection, < 20 ms jitter, and <20 ms latency.
Traffic Conditions
Potential interference from overlapping networks (e.g. neighbors, other WLANs). Data transfers and video display should be operational simultaneously.
Use Case
A surgical team is performing surgery with consultative assistance and observation from doctors at other locations.
The team interacts with the other doctors using multimedia tele-presence
The remote doctors also have access to real time patient diagnostic information and supplemental information.
The remote doctors have the ability to interact and operate in real time surgical theatre equipment.
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 43: 5b Usage in Stadium - Event Video Production
June 2013
Pre-Conditions
Highly Controlled WLAN network for local Video distribution operations.
Environment
Outdoor stadium equipped with 30 fixed and mobile cameras. Multiple operators’ WLAN networks.
Applications
3 3D UHD camera per AP lightly compressed (3.6Gbps)
Traffic Conditions
Potential interference from overlapping networks (e.g. neighbors, other WLANs). Data transfers and video display should be operating concurrently.
Use Case
Camera crew shoots the 3D UHD lightly compressed video and transmits over WLAN to Video Editing Studio
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 44: 5c Smart Car – Car Entertainment
June 2013
Pre-Conditions
User has operational WLAN network for internet access and service sharing between devices in a moving car.
Environment
In a car, embedded devices such as head unit, real seat displays and user devices such as smart phones, smart pads, and notebooks exist. Devices in a car are operating in close proximity. Transmissions are mostly LOS. Typical distances between STAs and AP are < 5m. But there might be interferences from the neighbor cars. Smart Car has an ability to internet access using cellular network.
Applications
Total 1.8 Gbps is required.
Video based applications (TV, VOD, Video conference): lightly compressed UHD (4k*2k). (600 Mbps): 3 users
Internet access (email, twitter, web surf): (20 Mbps): 1 user
Game online: (20 Mbps): 1 user
Traffic Conditions
Potential interference from overlapping networks (e.g. neighbors, other WLANs). Data transfers and video display should be operational simultaneously.
Use Case
Users operate many devices in a car.
Parents show different videos to different back seat screens or children’s tablets through AP and/or P2P.
* RSE: Real Seat Entertainment
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
John Doe, Some Company
Page <number>

## Slide 45: References
13/0331r5 “High-Efficiency WLAN”, Laurent Cariou (Orange)
13/514r0 “HEW Usage Scenarios and Applications”, Eldad Perahia (Intel)
13/538r0 “Dense apartment building use case for HEW”, Klaus Doppler (Nokia)
13/554r0 “Use Cases”, Minho Cheong (ETRI)
13/567r0 “Proposed HEW Usage Models”, Yasuhiko Inoue (NTT)
13/527r2 “Usage Models for Next Generation”, David Xun Yang (Huawei) and James Wang (MediaTek)
13/534r1 “Direction and Use Cases for HEW”, HanGyu Cho (LG Electronics)
13/542r0 “discussion on scenarios and goals for HEW”, Simone Merlin (Qualcomm)
12/0910r0 “Carrier oriented WIFI for cellular offload”, Laurent Cariou (Orange)
12/1123r0, “Carrier oriented WIFI for cellular offload”, Laurent Cariou (Orange)
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 46: Annexes
June 2013
Slide <number>
Laurent Cariou (Orange)

## Slide 47: Key Requirements on Major Traffic Types
June 2013
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 48: Key Requirements on Major Traffic Types
June 2013
Traffic | Subtype | Description | Rate, Mbps | Packet Error Rate | Jitter, ms | Delay, ms
Videos | Video Uncompressed† | HD, 1920x1080 pixels, 12bits/pixels, 60fps[3] | 1500 | 1e-8 | 10 | 10
 |  | VHD, 4k*2k pixels, 12bits/pixels, 60fps | 6000 | 1e-8 |  | 
 |  | UHD, 8k*4k pixels, 12bits/pixels, 60fps | 23000 | 1e-8 |  | 
 |  | 3D VHD, 4k*2k pixels, 12bits/pixels, 60fps | 9000 | 1e-8 |  | 
 |  | 3D UHD, 8k*4k pixels, 12bits/pixels, 60fps | 35000 | 1e-8 |  | 
 | Video Lightly Compressed† | HD, 1920x1080 pixels, Motion JPEG2000[3] | 150 | 1e-7 | 20 | 20
 |  | VHD, 4k*2k, Motion JPEG2000 | 600 | 1e-7 | 20 | 20
 |  | UHD, 8k*4k, Motion JPEG2000 | 2400 | 1e-7 | 20 | 20
 |  | 3D VHD, 4kp, Motion JPEG2000 | 900 | 1e-7 | 20 | 20
 |  | 3D UHD, 8kp, Motion JPEG2000 | 3600 | 1e-7 | 20 | 20
 | Video Compressed† | Blu-ray™ [3] | 50 | 1e-7 | 20 | 20
 |  | HD MPEG2[3] | 15 | 3e-7 | 20 | 20
 |  | VHD, 4k*2k pixels, 60fps | 100 | 3e-7 | 20 | 20
 |  | UHD, 8k*4k pixels, 60fps | 250 | 3e-7 | 20 | 20
† 1/10 compression rate for lightly compressed video and 1/100 for compressed video
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>

## Slide 49: Assumptions for Video Requirements
June 2013
Single frame is 1500 bytes
Packet Error Rate, Jitter, and Delay are measured at the upper MAC, not at the PHY.
Loss of single packet is noticeable by the renderer
Packet Error requirements are derived based on expectations of “error free viewing”
Below is a table deriving error-free interval from video rate and frame loss probability:
Video Rate (Mbps) | Packet Error Rate | Expected Error free interval, min
3000 | 1e-8 | 6.7
1500 | 1e-8 | 13
1300 | 1e-8 | 15
150 | 1e-7 | 13
50 | 1e-7 | 40
20 | 3e-7 | 30
Slide <number>
Laurent Cariou (Orange)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page <number>