## Slide 1: 802.11ak Security Discussion
Date: 2013-06-27
Authors:

## Slide 2: Abstract
This presentation discusses
802.11 and 802.1AE security
802.11 Security Keys
Group Key per VLAN
Privacy vs. Flooding

## Slide 3: 802.1AE security and 802.11 Security
802.1AE security and 802.11 security protect the link between two MAC entities, and do not provide end-to-end security
802.1AE-2006 was not intended for use with 802.11
  The 802.1AE message authentication check is not able to offer protection to 802.11 MAC headers without change
  Running 802.1AE security over an 802.11 link may not be possible unless 802.1 frames are encapsulated in 802.11 frames
Therefore it seems reasonable to say that an 802.11 link between two 802.11ak devices will need to be protected by 802.11 security

## Slide 4: 802.11 Security Keys
When a STA associates to an AP configured for robust network security (RSNA), a number of keys may be derived that are specific to that MAC-to-MAC link:
  PTK (Pairwise Transient Key) for unicast data frame transmissions
  Other keys may also be derived depending on security configuration, e.g. for protection of management frames, etc…
The AP provides the STA with a GTK (Group Temporal Key) for decrypting group addressed (multicast, broadcast) data frames
  A temporal key for group addressed management frames is also provided if Management Frame Protection is being used

## Slide 5: Group Key per VLAN
An 11ak BSS may support multiple VLANs
One GTK per VLAN will prevent exposure of MSDUs from one VLAN to 11ak MAC entities in another VLAN
Proposed solution:
In the case of an 802.11ak BSS, the generation of GTKs should be extended to generate a GTK per VLAN (VGTK)
  The VGTKs could be derived from the same GMK (Group Master Key)

## Slide 6: Privacy vs Flooding
802.11 privacy assumes that unicast MSDUs between two MAC entities never get exposed unnecessarily to other MAC entities of the same BSS [#1]
In the case of a self learning bridge, MSDUs with unknown unicast DA will first be flooded to all the 11ak MAC entities of the 11ak BSS belonging to the same VLAN, exposing the MSDUs to these MAC entities.
  Is this a violation of [#1] ?
  Is encrypting flooded unicast MSDUs with a VGTK, so that only members of the same VLAN can decrypt them, an acceptable solution ?

## Slide 7: Privacy vs Flooding (cont)
“By product” question:
  Flooding can make use of the 4-address frame format by retaining the original unknown DA and making the RA a group address, and using a VGTK to encrypt the result
  To make flooding reliable, could 11aa robust multicast be used in conjunction with 11ak, or could 11ak simply specify that all 4-address frames are ACKed, regardless of RA?