## Slide 1: Simulation scenarios and metrics for HEW
Date: 2013-07-15
Authors:

## Slide 2: Abstract
We presented in 13/0520r1 [1] some proposed general approaches for defining the evaluation scenarios, methodologies and metrics for HEW
In this document, we propose a small number of specific evaluation scenarios and corresponding metrics, based on categorization of the usage models outlined in 13/0657r3 [2]

## Slide 3: Context
A total of 15 different usage models are outlined in 13/0657r3, each with some variations
  too many to all be included in the evaluation methodology
We expect that WFA will provide input on prioritization and/or additional considerations, nevertheless it is useful to start defining key scenarios for evaluation as soon as possible
We prefer a small number of scenarios that are complete models of real-world environments
  i.e. approximately model what would be seen if one were to “Wireshark” a WLAN channel
  in particular, to model the interferences in a realistic way
Evaluation metrics should follow naturally from the scenarios by clarifying the elements of each scenario that we are actually interested in

## Slide 4: What forms a scenario?
A scenario can be formed by fully specifying the environment corresponding to a usage model
We define three components in a layered approach [1] as follows:
(i) “networks of interest”: networks used to realise the usage model
  described in usage models “pre-conditions”, “environment” and “applications”
(ii) “other interfering networks”: networks not required to realise the usage model but that coexist in the same real-world scenario
  described only in usage models “traffic conditions” (as other interferences)
(iii) “idle devices”: STAs and APs that are not transmitting data but still causing interference with management frames
  e.g. beacons from Soft APs (WFD, tethering, …), probe and association requests from STAs, radio resource management reports, …
* The term “interference” refers to all other co-channel transmissions, no matter if they are sharing airtime (i.e. normal CSMA/CA operation) or causing link-level interference (e.g. hidden node)

## Slide 5: Scenario downselection
A. HOTSPOT / MANAGED ESS
  1a Usage in stadium
  1b Airports and Train Stations
  1c Exhibition hall
  1d Shopping mall
  4a Super-dense urban street
  4b Pico-cell street deployment
B. RESIDENTIAL
  3a Dense apartment building
  3b Community Wi-Fi
C. OFFICE / SCHOOL
  1e e-Education
  2a Wireless Office

## Slide 6: A. Hotspot / Managed ESS
Networks of interest
  managed hotspot/WLAN ESS (all)
  + unmanaged APs in retail, booths, etc (1c exhibition hall, 1d shopping mall)
Other interfering networks
  tethering Soft-APs (1a stadium, 1b airport/station)
  other operators’ hotspots (1b airport/station, 4a/b outdoor hotspots)
Idle devices
  idle STAs (e.g. probe requests, esp. with WFD discovery)
  idle personal routers (e.g. beacons – esp. in 1a stadium, 2b airport/station)
* due to siting constraints
AP density
Variations: 2 sub-categories
Hotspot channel model
moderate (4b*)
very high (1a, 4a)
outdoor (4a, 4b)
indoor (1a, 1b, 1c, 1d)
A1
A2
(1b, 1c, 1d)

## Slide 7: B. Residential
Networks of interest
  unmanaged AP in each apartment (all)
Other interfering networks
  none
Idle devices
  idle STAs (e.g. probe/association requests from outdoor STAs in 3b community Wi-Fi)
Variations:
  STA location: larger drop range in 3b community Wi-Fi (including outdoor STAs)

## Slide 8: C. Office / school
Networks of interest
  managed WLAN ESS (all)
  + wireless display/docking P2P – many links (all)
Other interfering networks
  other tenants’ ESS (2a wireless office)
Idle devices
  none
Variations
  denser deployment of wireless display/docking P2P in 2a wireless office

## Slide 9: Association
In some cases a STA will not associate to the AP with lowest path loss, e.g.
  No credentials (e.g. neighboring apartment’s residential AP, different operator’s hotspot, etc)
  Different network service provided (e.g. internet vs intranet vs P2P link)
  Load balancing, etc (in special cases)
We propose dropping STAs associated with each network in a scenario separately
  Allows for simple but accurate association rules and STA placement
  Both “networks of interest” and “other interfering networks” should be simulated
  Some STAs may be associated with two networks (e.g. WLAN + wireless display/dock in scenario C)
  STA density and spatial distributions to be derived from usage models (with some refinement/precision)

## Slide 10: Traffic models
Based on mixture of the traffic types defined in the usage models
For networks of interest, primarily web, streaming/IPTV video, file transfer
  relatively high per-user throughput requirements in 2a wireless office and 3a dense apartment building
  mostly TCP, except IPTV / Miracast / VoIP which are typically UDP
  include small packets (video – reverse direction ACKs, VoIP, etc)
  other interfering networks can be modeled in the same way
For idle device traffic, consider modeling as chaotic interference or specific model
  e.g. probe request transmitted by each STA every X secs, followed by flurry of probe responses from other STAs

## Slide 11: Evaluation metrics
We propose evaluation metrics are calculated over the Networks of interest only
  If multiple types of Networks of interest (e.g. scenario C - WLAN ESS + many wireless display/dock links), it may be useful to express metrics for each type individually
  For simpler analysis of certain techniques (e.g. PHY), a single (or partial) Network of interest can be selected from the full scenario as described in [1]
For hotspot / classical WLAN, the most important metric is per-user MAC layer throughput
  Average per-user throughput gives good indication of typical QoE
  Probability of throughput < 2 Mbps describes % of users with less than acceptable QoE
  5% throughput (cdf over multiple random drops) describes the “worst case” experience
    A good proxy for drop-out rate (below throughput for minimal connectivity)
  Jitter, PER etc may be optional considerations for certain usages (e.g.. Gaming, telephony/UCC)
Higher-layer QoE metrics (e.g. association time) should be mapped to corresponding PHY/MAC metrics by separate simulation if necessary (e.g. depending on protocol, architecture)
Using the same metrics, a baseline reference can be calculated (e.g. based on 11ac) to quantify relative gains achieved with HEW
  “Area throughput” may be optional to show the aggregate spectral efficiency limits of HEW technology

## Slide 12: References
[1] IEEE 802.11-13/0520r1 - T. Derham - “HEW scenarios and evaluation metrics”
[2] IEEE 802.11-13/0657r3 – L. Cariou - “Usage models for IEEE 802.11 High Efficiency WLAN study group (HEW SG) – Liaison with WFA”

## Slide 13: Key performance issues per usage case category
Category 1
  difficulties to perform frequency/spatial reuse between neighboring BSSs
  reduced efficiency when multiple APs are sharing the same channel
  reducing the size of each BSS (to reduce number of STAs per APs, enable channel reuse in neighboring BSSs and increase capacity per STA) is limited by co-channel interference and protection
  per user throughput collapses with high number of STAs per AP: bad efficiency per BSS
Category 2
  per user throughput collapses with high number of STAs per AP: bad efficiency per BSS
Category 3
  difficulties to perform frequency/spatial reuse between neighboring BSSs with different management entities (co-channel interference)
  weak performance at BSS-edge with low SINR in such an interfering environment
Category 4
  weak performance at BSS-edge with low SINR in such an interfering environment
  difficulties to perform frequency/spatial reuse between neighboring BSSs
  per user throughput collapses with high number of STAs per AP: bad efficiency per BSS
  performance is affected by outdoor propagation conditions